## Slide 1: Z. Gu
Fall 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 12
Fixed-point Numbers
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Fixed-point Format: Q Notation
Integer Part
Fractional Part
m bits
n bits
UQm.n for unsigned fixed-point
Integer Part
Fractional Part
m bits
n bits
sign bit
Qm.n for signed fixed-point
m + n + 1 bits
Radix Point
Radix Point

## Slide 3: Q Notation: UQm.n

## Slide 4: Converting Fixed-point UQ5.3 to Float
24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
=
Integer Part
Fractional Part
Radix
Point

## Slide 5: Converting Fixed-point Q4.3 to Float
-24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
Integer Part
Fractional Part
Radix
Point
Signed
Bit
=
Another way of computing the int part:
MSB = 1 → number is negative
Find magnitude:
  Invert: 10101 → 01010
  Add 1: 01010 + 1 = 01011 → decimal 11
So the value is −11

## Slide 6: UQ5.3 vs. Q4.3
Signed Fixed-point Representation Qm.n
Unsigned Fixed-point Representation UQm.n

## Slide 7: Two Ways of Calculating Two’s Complement (integer)
Convert into decimal with Two’s Complement notation
Method 1, invert bits and add 1:
  01010 + 1 = 01011 = 11 in decimal, hence 10101 = -11 in decimal
Method 2, calculate directly:
  in decimal
The two definitions are mathematically identical (proof omitted)

## Slide 8: Convert Float to Fixed-point UQ4.12
Calculate
Round the result to nearest integer,
Convert the integer to binary: 12868 = 0011_0010_0100_01002
Organize into UQ4.12: 0011.0010_0100_01002
Final result in hex: 0x3244
Approximation Error = reconstructed_value − true_value = (due to limited number of fractional bits (12))
Example: Convert to UQ4.12 (4 bits integer, 12 bits fraction)
UQm.n for unsigned fixed-point

## Slide 9: Convert Float to Fixed-point Q3.12
Calculate
Round the result to an integer,
Find the 16-bit two’s complement: 1100_1101_1011_11002
  Invert bits and add 1 →
Organize into Q3.12: 1100.1101_1011_11002
Final result in hex: 0xCDBC
Approximation Error = reconstructed_value − true_value =
Example: Convert to Q3.12 (1 sign bit, 3 bits integer, 12 bits fraction)
Qm.n for signed fixed-point

## Slide 10: Why use fixed-point?
Floating Point
Shorter Development Time
Wide Dynamic Range
Fixed Point
Higher Performance
Lower Product Cost
More bits for precision

## Slide 11: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 13
Floating-point Numbers
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 12: Normalization
We can convert 10.74626 to normalized format as follows:

## Slide 13: IEEE Standard 754 (Signed Floating Point)
IEEE 754 value:
where Bias = 27 - 1 = 127 for single precision FP32
Bias = 210 - 1 = 1023 for double precision FP64
Hidden bit refer to the implicit leading 1 in (1 + fraction)
Fraction is also called significand or mantissa
Notes: https://mp.weixin.qq.com/s/LQgPT8opkjjZzbn0nUevUw

## Slide 14: Why Bias?
FP32’s exponent field has 8 bits. So it can represent integers from 0 to 255. But real exponents in normalized floating-point numbers range roughly from –126 to +127. To store both negative and positive exponents in that 0–255 range, IEEE-754 adds a bias, shifting all values upward so they become non-negative.
For an exponent field of n bits, the bias is 2(n−1)- 1.
For FP32, the bias is chosen as 2(8−1)- 1 = 127, so half the range is allocated for negative exponents, and half for positive.
  Actual Exponent = Stored Exponent -127
  Stored exponent 0 → reserved for zero and subnormal numbers
    For subnormal numbers: effective exponent = -126, and there is no hidden leading 1
  Stored exponent 127 → actual exponent = 0
  Stored exponent 255 → reserved for special values (like infinity and NaN)
Notes: 8位有符号整数的范围是 -128 到 127。

## Slide 15: Decoding 0xC1FF0000 into a floating-point number
Binary 11000001111111110000000000000000
Sign = 1
Exponent =
Fraction =
If Exponent = , then
  Exponent – bias =
If Exponent = , then
  Exponent – bias =
Notes: 10000101

## Slide 16: Decoding 0x40900000 into a floating-point number
Binary 01000000100100000000000000000000
Sign = 0
Exponent =
Fraction =
How Floating Point Numbers Work (in 7 minutes!)
  https://www.youtube.com/watch?v=W_Knvo9NuJY

## Slide 17: Decoding 0x3F800000 into a floating-point number
Binary 00111111100000000000000000000000
Sign = 0
Exponent =
Fraction =
How Floating Point Numbers Work (in 7 minutes!)
  https://www.youtube.com/watch?v=W_Knvo9NuJY

## Slide 18: Decoding 0x41680000 into a floating-point number
Binary 01000001011010000000000000000000
Sign = 0
Exponent =
Fraction =

## Slide 19: Encoding 14.5 into IEEE Std 754 Single-Precision
Normalization:
Hence
Conversion:
(multiply by 2 repeatedly)
Assume
  => b1 = 1
  => b2 = 1
  => b3 = 0
  => b4 = 1
14.5 = 01000001011010000000000000000000 in binary or 0x41680000 in hex
Notes: 1.3

## Slide 20: Encoding 1.3 into IEEE Std 754 Single-Precision
Normalization:
Hence
Conversion:
(multiply by 2 repeatedly)
Assume
  => b1 = 0
  => b2 = 1
  => b3 = 0
  => b4 = 0
  => b5 = 1
  => b6 = 1
1.3 = 00111111101001100110011001100110 in binary or 0x3FA66666 in hex
Repeats infinitely
Notes: 32-9=23

## Slide 21: Decoding 0x3FA66666 into a floating-point number
Binary 00111111101001100110011001100110
Sign = 0
Exponent =
Fraction = (calculation process skipped)
Error:
Why Is This Happening?! Floating Point Approximation4
https://www.youtube.com/watch?v=2gIxbTn7GSc

## Slide 22: Special Values
Exponents 00000000 and 11111111 are reserved.
Example of Not-A-Number (NaN)
  log(-10.0), sqrt(-1.0), 0.0/0.0, ,

## Slide 23: Subnormalized Float Number
To represent numbers between 0 and the minimum positive number that the normalized format can represent.
Normalized Format
Sub-normalized Format

## Slide 24: Overflow and Underflow
Smallest Positive Normal Number:
0 00000001 00000000000000000000000
Smallest Positive Subnormal Number:
0 00000000 00000000000000000000001

## Slide 25: Overflow and Underflow
To find the largest representable number:
Exponent = largest possible finite value = 254 (since 255 is reserved for infinity and NaN)
Mantissa = all 1s →
Numbers farthest from zero:
Notes: Numbers farthest from zero

## Slide 26: Resolution
Given a hypothetical five-bit floating-point system (similar to IEEE 754).
  the sign bit, an exponent (2 bits), and a fraction (2 bits)

## Slide 27: Tradeoff between Range and Precision
Floating-Point
  Resolution: difference between two neighbor numbers
  Precision decreases as the magnitude increases
Fixed-Point
  Numbers are evenly distributed among the representable range
  Precision is fixed
A simplified 5-bit floating-point (IEEE 754 style)

## Slide 28: FP formats used in AI and machine learning
bf16 (bfloat16) and bf8 (bfloat8) are floating point formats used in AI and machine learning for efficient computation with lower precision while retaining useful range.
bf8 is cutting edge and experimental for very efficient AI deployment where accuracy can be slightly sacrificed for speed and lower memory footprints. bf16 is established as a good practical balance for many ML tasks
Notes: https://www.edge-ai-vision.com/2025/08/introduction-to-data-types-for-ai-trade-offs-and-trends-a-presentation-from-synopsys/

## Slide 29: References
Recommended: How Floating-Point Numbers Are Represented
  https://www.youtube.com/watch?v=bbkcEiUjehk
Recommended: Floating Point Numbers Work (in 7 minutes!)
  https://www.youtube.com/watch?v=W_Knvo9NuJY
HOW TO: Convert IEEE-754 Single-Precision Binary to Decimal, Steven Petryk
  https://www.youtube.com/watch?v=4DfXdJdaNYs
Why Is This Happening?! Floating Point Approximation
  https://www.youtube.com/watch?v=2gIxbTn7GSc
IEEE 754 Binary to Float Conversion
  https://www.youtube.com/watch?v=9k5rdPUzij8&list=PL-ftFcielQtGxBUfzkbz9tWlRZb-rlJ2p&index=2
IEEE 754 Float to Binary Conversion
  https://www.youtube.com/watch?v=9k5rdPUzij8&list=PL-ftFcielQtGxBUfzkbz9tWlRZb-rlJ2p&index=2