## Slide 1: Z. Gu
Fall 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises

## Slide 2: Stack
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=?, r1=?

## Slide 3: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3} (same as POP {r0, r1, r2, r3})
Draw stack after each instruction. What is in registers after execution?
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
After POP {r0-r3}
r0=?, r1=?, r2=?, r3=?

## Slide 4: What’s wrong? Passing arguments and Returning Value
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOV r0, #5 ; e32
MOV r0, #1 ; a8
MOV r1, #2 ; b8
MOV r2, #3 ; c16
MOV r3, #4 ; d16
BL sum
...
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
ADD r0, r0, r1 ; add e32
BX LR
ENDP

## Slide 5: Program Understanding
0x10000200 | 60 | 1B | 11 | 12 | EE | FF | 11 | 22 | 33 | 44 | 55 | 66 | 77 | 88 | 99 | 92
0x100001F0 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B | 1C | 1D | 1E | 1F
0x100001E0 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 0A | 0B | 0C | 0D | 0E | 0F
R0 | 0x00000000
R1 | 0x10000200
R2 | 0x0000FFFF
R3 | 0x18675309
R4 | 0x00000000
R5 | 0x00000000
… | 
R13 | 0x10000200
PUSH {R1, R3}
POP {R5}
Compute register and memory values at each step of this program, given initial register values and memory contents, assuming little-endian memory ordering.
Initial Register Values
Initial Memory Contents

## Slide 6: Passing arguments and Returning Value
a64
b8
c16
d16
Subroutine
Register:
Register;
Register:
Return Value
Register R1:R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack
Fill in register names.
Register:

## Slide 7: Argument Passing
Which registers are used to pass the arguments and return the result?
long fun (short a1, char a2, double a3, int a4, char a5)
R0 | R1 | R2 | R3
Registers
Stack in Memory

## Slide 8: What is Wrong?
Caller Program
extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s; ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 9: toLower
Caller Program
#include <stdio.h> extern int toLower(int); /* assembler routine */ int main(void) { static const char str[] = "Hello, World!"; const int len = sizeof(str)/sizeof(str[0]); char newstr[len]; int i; for (i = 0; i < len; i++) newstr[i] = toLower (str[i]); printf("%s\n", newstr); return 0; }
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Consider the following C program that converts all ASCII letters to lower case. Write the toLower function in ARMv7 assembly code.
Callee Program Assembly
.text .global toLower toLower:
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 10: If Then Else
Translate the following program into ARMv7 assembly.
C Program | Assembly Program
int foo(int x, int y) { if (x+y < 0) return 0; else return 1; } | @ int foo(int x, int y) - returns 0 if (x+y) < 0, else 1 @ x in r0, y in r1, return in r0 foo: … BX lr

## Slide 11: Factorial
Fill in the blanks (TODO) for the assembly programs for calculating the factorial of a number, corresponding to the following C programs. One recursive version, one iterative version.
//Recursive algorithms for Factorial
#include <stdint.h>
uint32_t fact_rec(uint32_t n) {
if (n <= 1) {
return 1;
}
return n * fact_rec(n - 1);
}
//Iterative algorithms for Factorial
#include <stdint.h>
uint32_t fact_iter(uint32_t n) {
uint32_t acc = 1;
if (n <= 1) {
return 1;
}
while (n > 1) {
acc *= n;
n -= 1;
}
return acc;
}
Notes: (In the exams, I may provide most of the code and let you fill in the blanks.)

## Slide 12: Factorial
@ uint32_t fact_iter(uint32_t n);
@ r0 = n, returns r0 = n!
.global fact_iter
fact_iter:
PUSH {r4, lr} @ save callee-saved we’ll use and return addr
MOV r1, r0 @ r1 = n (loop counter)
MOV r0, #1 @ r0 = acc = 1
CMP r1, #1
BLS .Ldone_iter @ if n <= 1, return 1
.Lloop_iter:
@ TODO
.Ldone_iter:
POP {r4, lr}
BX lr
@ uint32_t factorial(uint32_t n);
@ r0: n
@ returns r0: n!
factorial:
CMP r0, #1 @ if (n <= 1) ...
BLS base_case @ ... return 1
PUSH {lr} @ save return address for this frame
PUSH {r0} @ save current n on stack (we'll need it after the recursive call)
SUB r0, r0, #1 @ r0 = n - 1 (argument for recursive call)
BL factorial @ r0 = factorial(n - 1)
POP {r1} @ r1 = saved n (restore caller's n)
MUL r0, r0, r1 @ r0 = factorial(n - 1) * n
POP {lr} @ restore return address
BX lr @ return with result in r0
base_case:
@ TODO

## Slide 13: What is wrong?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0, r2, LSL #1]
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3 ; return result in r0
BX lr
ENDP

## Slide 14: Program Understanding
Write out the sequence of values of r0 and r7 after running this program.
start:
mov r0, #1
main:
add r0, r0, #1
cmp r0, #5
bne skip
bl call
skip:
b main
call:
add r7, r7, #255
mov r0, #1
bx lr
Notes: Here’s what the program does in practice:
It starts with x0 = 1.
It loops, incrementing x0 each time.
When x0 reaches 5, it calls call.
call adds 255 to x7 and resets x0 to 1.
Control returns to main, and the cycle repeats.
So the pattern goes like this:
x0: 1 → 2 → 3 → 4 → 5 → (call resets to 1)
x7: +255 each time x0 reaches 5