## Slide 1: Z. Gu
Fall 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 4
ARM Arithmetic and Logic Instructions
Exercises ANS
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Barrel Shifter: Explanations
LSL (logical shift left): shifts left, fills zeros on the right; C gets the last bit shifted out of bit 31. This is multiply by for non-overflowing values.
LSR (logical shift right): shifts right, fills zeros on the left; C gets the last bit shifted out of bit 0. This is unsigned division by .
ASR (arithmetic shift right): shifts right, fills the sign bit on the left to preserving the sign; C gets the last bit shifted out of bit 0. This is signed division by with sign extension
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C receives the bit that wrapped. This is a pure rotation without data loss.
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0.
Review
Notes: Useful for multiword shifts and certain crypto/bit-manip patterns
LSR (used here): Always fills with zeros, converting the negative value to a large positive number
ASR: Would preserve the sign bit, maintaining the negative value (-4096)

## Slide 3: Carry and Overflow Flags w/ Arithmetic Instructions
3
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs; Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
Tip: Convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 Borrow flag=0 (Result incorrect) | true result < 0  Carry flag=0 Borrow flag=1 (Result incorrect) | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1 Overflow flag=1 (Result incorrect)
Review
Notes: Convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0.”
convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; for all other cases, V = 0
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. ) or smaller than the minimum signed integer (i.e. ) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. 2^(𝑛−1)−1) or smaller than the minimum signed integer (i.e. 〖−2〗^(𝑛−1)) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 4: Bit Manipulations
Compute 32-bit register values after each instruction
MOV R0, #0x0ABC
MOV R1, #0x0DEF
AND R2, R0, R1
ORR R3, R0, R1
EOR R4, R0, R1
ORN R5, R0, R1
BIC r6, R0, R1

## Slide 5: Bit Manipulations ANS
MOV R0, #0x0ABC
MOV R1, #0x0DEF
AND R2, R0, R1
ORR R3, R0, R1
EOR R4, R0, R1
ORN R5, R0, R1
BIC r6, R0, R1
R0 = 0x0ABC
R1 = 0x0DEF
R2 = R0 AND R1 = 0x08AC
R3 = R0 ORR R1 = 0x0FFF
R4 = R0 EOR R1 = 0x0753
R5 = R0 ORN R1 = R0 | (~R1) = 0x00000ABC | 0xFFFFF210 = 0xFFFFFABC
  ~R1 (32-bit) = 0xFFFFF210
r6 = r0 BIC R1 = R0 & (~R1) = 0x00000ABC & 0xFFFFF210 = 0x00000210
AND Rn Operand2 performs bitwise conjunction on Rn and Operand2.
ORR performs bitwise OR on Rn and Operand2.
EOR performs bitwise XOR on Rn and Operand2.
ORN computes Rn OR NOT Operand2, i.e., Rn | (~Rm).
BIC computes Rn AND NOT Operand2, i.e., Rn & (~Rm).
(Hint: convert hex to binary, perform operation, and convert back to hex.)

## Slide 6: Bit Manipulations
Find the Register Value to Complement, CLEAR & SET 5th, 7th, 12th bit of the given value and also find the result: 0xDECB.

## Slide 7: Bit Manipulations ANS
Find the Register Value to set, clear, or toggle the 5th, 7th, 12th bit of the given value and also find the result: 0xDECB.
ANS:
Set/Clear/Complement
  Set a bit: x |= mask, which forces those bit positions to 1 without changing others. (| is OR)
  Clear a bit: x &= ~mask, which forces those bit positions to 0. (& is AND)
  Toggle (Complement) a bit: x ^= mask, which flips those bit positions. (^ is XOR)
Masks for 5th, 7th, 12th
  Bit 5 → 1<<5 = 0x20.
  Bit 7 → 1<<7 = 0x80.
  Bit 12 → 1<<12 = 0x1000.
Combined mask = 0x1000 | 0x80 | 0x20 = 0x10A0 = 0b0001 0000 1010 0000
Apply to 0xDECB
  Set: 0xDECB | 0x10A0 = 0xDEEB
  Clear: 0xDECB & ~0x10A0 = 0xCE4B
  Toggle: 0xDECB ^ 0x10A0 = 0xCE6B

## Slide 8: Clearing a Register
What are the different ways by which all bits in register r12 can be cleared? No other register is to be used.

## Slide 9: Clearing a Register ANS
What are the different ways by which all bits in register r12 can be cleared? No other register is to be used.
Method 1: XOR with itself
  EOR r12, r12, r12
Method 2: AND with zero
  AND r12, r12, #0
Method 3: Move zero
  MOV r12, #0
Method 4: Subtract from itself
  SUB r12, r12, r12
Method 5: Clear 32 bits in r12 starting from bit 0
  BFC r12, #0, #32
Method 6: r12 = r12 AND NOT r12 (bitwise clear)
  BIC r12, r12, r12
  BIC Rd, Rn, Rm ; Rd = Rn & (~Rm)

## Slide 10: Set bits
Write an instruction that sets bits 0, 4, and 12 in register r6 and leave the remaining bits unchanged
Write an instruction that clears bits 0, 4, and 12 in register r6 and leave the remaining bits unchanged

## Slide 11: Set bits ANS
Write an instruction that sets bits 0, 4, and 12 in register r6 and leave the remaining bits unchanged
ANS:
  ORR r6, r6, #(1<<0) | (1<<4) | (1<<12)
Write an instruction that clears bits 0, 4, and 12 in register r6 and leave the remaining bits unchanged
ANS:
  BIC r6, r6, #(1<<0) | (1<<4) | (1<<12)
  Or: AND r6, r6, #~( (1<<0) | (1<<4) | (1<<12) )
Notes:   ORR r6, r6, #0x1011 @ Set bits 0, 4, and 12 (0x1011 = binary 1000000010001)

## Slide 12: Add two 128-bit numbers
Add two 128-bit numbers, assuming one number is stored in r4, r5, r6, r7 registers and the other stored in r8, r9, r10, r11. Store the result in r0, r1, r2, r3.

## Slide 13: Add two 128-bit numbers ANS
Add two 128-bit numbers, assuming one number is stored in r4, r5, r6, r7 registers and the other stored in r8, r9, r10, r11. Store the result in r0, r1, r2, r3.
ANS:
  @ Add 128-bit numbers (r4,r5,r6,r7) + (r8,r9,r10,r11) = (r0,r1,r2,r3)
  ADDS r0, r4, r8 @ Add lowest 32 bits with carry flag update
  ADCS r1, r5, r9 @ Add with carry
  ADCS r2, r6, r10 @ Add with carry
  ADC r3, r7, r11 @ Add with carry (final)
    Or ADCS r3, r7, r11, but the flags are not used

## Slide 14: Absolute value
Write a program to calculate the absolute value of a number by using only two instructions (HINT: Check CMP and RSB)

## Slide 15: Absolute value ANS
Write a program to calculate the absolute value of a number by using only two instructions (HINT: Check CMP and RSB)
ANS
  CMP r0, #0 @ Compare with zero
  RSBLT r0, r0, #0 @ If less than zero, r0 = 0 - r0

## Slide 16: Arithmetic with Shifts
Assuming 32-bit registers:
Q1:
  LDR r0, =0x00000007
  MOV r0, r0, LSL #7
Q2:
  LDR r0, =0x00000400
  MOV r0, r0, LSR #2
Q3:
  LDR r0, =0xFFFFC000
  MOV r0, r0, LSR #2
Q4:
  LDR r0, =0xFFFFC000
  MOV r0, r0, ASR #2
Q5:
  LDR r0, =0x00000007
  MOV r0, r0, ROR #2

## Slide 17: Q1 ANS
Q1:
  LDR r0, =0x00000007
  MOV r0, r0, LSL #7
ANS:
  Original r0 = 0000 0000 0000 0000 0000 0000 0000 0111
  After LSL 7, r0 = 0000 0000 0000 0000 0000 0011 1000 0000 = 0x00000380 (896 in decimal)
  In decimal: 7 × 2^7 = 7 × 128 = 896 (Not required for exam)

## Slide 18: Q2 ANS
Q2.1:
  LDR r0, =0x00000400
  MOV r0, r0, LSR #2
ANS:
  Original r0 = 0000 0000 0000 0000 0000 0100 0000 0000
  After LSR 2, r0 = 0000 0000 0000 0000 0000 0001 0000 0000 = 0x00000100 (256 in decimal)
  In decimal: 1024 ÷ 2² = 256 (Not required for exam)
Q2.2:
  LDR r0, =0x00000400
  MOV r0, r0, ASR #2
ANS:
  r0 = 0x00000100 (LSR and ASR have no difference for positive numbers)
  In decimal: 1024 ÷ 2² = 256 (Not required for exam)

## Slide 19: Q3 ANS
Q3.1:
  LDR r0, =0xFFFFC000
  MOV r0, r0, LSR #2
ANS:
  Original r0 = 1111 1111 1111 1111 1100 0000 0000 0000
  After LSR 2, r0 = 0011 1111 1111 1111 1111 0000 0000 0000 = 0x3FFFF000
  In decimal: 4,294,950,912 ÷ 4 = 1,073,737,728 (Not required for exam)
Q3.2:
  LDR r0, =0xFFFFC000
  MOV r0, r0, ASR #2
ANS:
  r0 = 1111 1111 1111 1111 1111 0000 0000 0000 = 0xFFFFF000
  In decimal: −16384 ÷ 4 = −4096 (Not required for exam)

## Slide 20: Q5 ANS
Q5:
  LDR r0, =0x00000007
  MOV r0, r0, ROR #2
ANS:
  Original r0 = 0000 0000 0000 0000 0000 0000 0000 0111
  After ROR r0 = 1100 0000 0000 0000 0000 0000 0000 0001 = 0xC0000001

## Slide 21: Assembly Programming
Write ARMv7 assembly for pseudocode
  r1 = (r0 >> 4) & 15

## Slide 22: Assembly Programming ANS
Write ARMv7 assembly for pseudocode
  r1 = (r0 >> 4) & 15
ANS:
  MOV r1, r0, LSR #4
  AND r1, r1, #15
Notes: Alternative solution:
  AND r1, r0, #0xF0
  MOV r1, r1, LSR #4

## Slide 23: Shift LSL ANS
Compute register values:
  LDR R1, =0x11223344
  MOV R2, R1, LSL #4
  MOV R3, R1, LSL #8
  MOV R4, R1, LSL #16
  MOV R5, R1, LSL #6
ANS:
  Pseudo-instruction LDR R1, =0x11223344 loads 32-bit constant 0x11223344 into R1.
  LSL performs a logical left shift of Rm by the immediate count and writes the result to Rd, zero-filling low bits and discarding overflow in 32-bit registers
  MOV R2, R1, LSL #4 performs a logical left shift of R1 by 4 bits, inserting zeros; 0x11223344 << 4 = 0x12233440.
  MOV R3, R1, LSL #8 shifts by 8 bits; 0x11223344 << 8 = 0x22334400.
  MOV R4, R1, LSL #16 shifts by 16 bits; 0x11223344 << 16 = 0x33440000.
  MOV R5, R1, LSL #6 shifts by 6 bits; 0x11223344 << 6 = 0x488CD100. (convert to binary and back)
Notes: Compute register values:
  LDR R1, =0x11223344
  MOV R2, R1, LSL #4
  MOV R3, R1, LSL #8
  MOV R4, R1, LSL #16
  MOV R5, R1, LSL #6

## Slide 24: Shift LSLS ANS
Compute register values, and NZCV flags after execution of each instruction, assuming all flags are initially 0.
  LDR R1, =0x11223344
  MOVS R2, R1, LSL #4
  MOVS R3, R1, LSL #8
  MOVS R4, R1, LSL #16
ANS:
  Pseudo-instruction LDR R1, =0x11223344 loads 32-bit constant 0x11223344 into R1.
  LSL performs a logical left shift of Rm by the immediate count and writes the result to Rd, zero-filling low bits and discarding overflow in 32-bit registers
  MOVS R2, R1, LSL #4 performs a logical left shift of R1 by 4 bits, inserting zeros; 0x11223344 << 4 = 0x12233440.
    NZCV = 0010 (last bit shifted out was 1, LSB of 0x1)
  MOVS R3, R1, LSL #8 shifts by 8 bits; 0x11223344 << 8 = 0x22334400.
    NZCV = 0010 (last bit shifted out was 1, LSB of 0x11)
  MOVS R4, R1, LSL #16 shifts by 16 bits; 0x11223344 << 16 = 0x33440000.
    NZCV = 0000 (last bit shifted out was 0, LSB of 0x1122)
  MOVS R5, R1, LSL #6 shifts by 6 bits; 0x11223344 << 6 = 0x488CD100. (convert to binary and back)
    NZCV = 0000 (last bit shifted out 0, LSB of 000100)

## Slide 25: Shift ASR ANS
Compute register values:
LDR R1, =0x81223344
MOV R2, R1, ASR #4
MOV R3, R1, ASR #8
MOV R4, R1, ASR #16
ANS:
  R2 = R1 ASR #4 = 0xF8122334 (right shift 4; top nibble becomes F due to sign extension).
  R3 = R1 ASR #8 = 0xFF812233 (right shift 8; top byte becomes FF).
  R4 = R1 ASR #16 = 0xFFFF8122 (right shift 16; top halfword becomes FFFF)

## Slide 26: Shift LSR ASR ANS
Compute register values:
  LDR R1, =0X11223344
  MOV R2, R1, LSR #4
  MOV R3, R1, LSR #8
  MOV R4, R1, LSR #16
  MOV R5, R1, ASR #4
  MOV R6, R1, ASR #8
  MOV R7, R1, ASR #16
ANS:
  Pseudo-instruction LDR R1, =0x11223344 loads 32-bit constant 0x11223344 into R1.
  LSR #4: R2 = 0x11223344 >> 4 = 0x01122334.
  LSR #8: R3 = 0x11223344 >> 8 = 0x00112233.
  LSR #16: R4 = 0x11223344 >> 16 = 0x00001122.
  ASR #4: R5 = 0x11223344 >> 4 = 0x01122334.
  ASR #8: R6 = 0x11223344 >> 8 = 0x00112233.
  ASR #16: R7 = 0x11223344 >> 16 = 0x00001122.
  ASR (arithmetic shift right) replicates the sign bit; for a positive value like 0x11223344 (bit 31 is 0), ASR behaves exactly like LSR and shifts in zeros.
Notes: R2 = 0x01122334, R3 = 0x00112233, R4 = 0x00001122, R5 = 0x01122334, R6 = 0x00112233, R7 = 0x00001122.

## Slide 27: Shift LSRS ASR ANS
Compute register values, and NZCV flags after execution of each instruction, assuming all flags are initially 0.
  LDR R1, =0X11223344
  MOVS R2, R1, LSR #4
  MOVS R3, R1, LSR #8
  MOVS R4, R1, LSR #16
  MOVS R5, R1, ASR #4
  MOVS R6, R1, ASR #8
  MOVS R7, R1, ASR #16
ANS:
  Pseudo-instruction LDR R1, =0x11223344 loads 32-bit constant 0x11223344 into R1.
  LSR #4: R2 = 0x11223344 >> 4 = 0x01122334.
    NZCV = 0000 (last bit shifted out was 0, MSB of 0x4)
  LSR #8: R3 = 0x11223344 >> 8 = 0x00112233.
    NZCV = 0000 (last bit shifted out was 0, MSB of 0x44)
  LSR #16: R4 = 0x11223344 >> 16 = 0x00001122.
    NZCV = 0000 (last bit shifted out was 0, MSB of 0x3344)
  ASR #4: R5 = 0x11223344 >> 4 = 0x01122334.
  ASR #8: R6 = 0x11223344 >> 8 = 0x00112233.
  ASR #16: R7 = 0x11223344 >> 16 = 0x00001122.
    NZCV = 0000 (ASR has the same flag settings as LSR, since they both shift out the same bits)
  ASR (arithmetic shift right) replicates the sign bit; for a positive value like 0x11223344 (bit 31 is 0), ASR behaves exactly like LSR and shifts in zeros.
Notes: R2 = 0x01122334, R3 = 0x00112233, R4 = 0x00001122, R5 = 0x01122334, R6 = 0x00112233, R7 = 0x00001122.

## Slide 28: Multiply without MUL
Without using MUL instruction, give instructions that multiply a register, r3 by
  135
  153
  255
  18
  1025

## Slide 29: Multiply without MUL ANS
Without using MUL instruction, give instructions that multiply a register, r3 by:
  135
  153
  255
  18
  1025
ANS: Decompose 135 = 128 + 4 + 2 + 1
  MOV r0, r3, LSL #7 @ 128*r3
  ADD r0, r0, r3, LSL #2 @ +4*r3 -> 132*r3
  ADD r0, r0, r3, LSL #1 @ +2*r3 -> 134*r3
  ADD r0, r0, r3 @ +1*r3 -> 135*r3
Decompose 153 = (8 + 1) * (16 + 1)
  ADD r0, r3, r3, LSL#3 @ r0 = r3 + 8*r3 = 9*r3 ADD r0, r0, r0, LSL#4 @ r0 = 9*r3 + 16*9*r3 = 153*r3
Decompose 255 = 256 - 1
  RSB r0, r3, r3, LSL#8 @ r0 = 256*r3 - r3 = 255*r3
Decompose 1025=2^10+1:
  ADD r0, r3, r3, LSL#10 @ r0 = r3 + 1024*r3 = 1025*r3
Decompose 18 = (16 + 1) + 1
  ADD r0, r3, r3, LSL#4 @ r0 = r3 + 16*r3 = 17*r3 ADD r0, r0, r3 @ r0 = 17*r3 + r3 = 18*r3

## Slide 30: Count number of ones
Write a program to count the number of ones in a 32-bit register r0.

## Slide 31: Count the number of ones ANS
Write a program to count the number of ones in a 32-bit register r0.
ANS:
  @ Count ones in r0, result in r3
  MOV r3, #0 @ Initialize counter
  count_loop:
  CMP r0, #0
  BEQ count_end
  AND r1, r0, #1 @ Check LSB
  ADD r3, r3, r1 @ Add to counter
  LSR r0, r0, #1 @ Shift right
  B count_loop
  count_end:

## Slide 32: Count the number of zeros
Based on the program that counts 1’s, modify it to count the number of zeros in a 32-bit register r0.
Notes: ANS: count ones, then subtract from 32
Or Invert r0 to get r4, then count 0’s in r4

## Slide 33: Count the number of zeros ANS
Based on the program that counts 1’s, modify it to count the number of zeros in a 32-bit register r0.
ANS: count ones, then subtract from 32
  @ Count zeros in r0, result in r3
  MOV r3, #0 @ Initialize counter
  count_loop:
  CMP r0, #0
  BEQ count_end
  AND r1, r0, #1 @ Check LSB
  ADD r3, r3, r1 @ Add to counter
  LSR r0, r0, #1 @ Shift right
  B count_loop
  count_end:
  RSB r3, r3, #32 @ zeros = 32 – ones
Or Invert all bits of r0, then count 1’s
  @ Count zeros in r0, result in r3
  MVN r0, r0
  MOV r3, #0 @ Initialize counter
  count_loop:
  CMP r0, #0
  BEQ count_end
  AND r1, r0, #1 @ Check LSB
  ADD r3, r3, r1 @ Add to counter
  LSR r0, r0, #1 @ Shift right
  B count_loop
  count_end:
Note that SUB r3, #32, r3 is not valid ARM syntax,
Since the middle operand cannot be an immediate.
You can load 32 into a register and subtract:
MOV r2, #32 SUB r3, r2, r3

## Slide 34: Compute Polynomial
Write a program that computes 6x^2 – 9x + 2 and stores the result in register r2. Assume x is stored in register r3.

## Slide 35: Compute Polynomial
Option A: Direct Translation
// r3 = x, result -> r2 MUL r0, r3, r3 @ r0 = x² MOV r1, #6 MUL r0, r0, r1 @ r0 = 6x² MOV r1, #9 MUL r1, r1, r3 @ r1 = 9x SUB r2, r0, r1 @ r2 = 6x² - 9x ADD r2, r2, #2 @ r2 = 6x² - 9x + 2
Note that MUL r0, r0, #6 is not a valid instruction.

## Slide 36: Compute Polynomial
Option C: Horner form 6x^2 − 9x + 2 = x(6x − 9) + 2
// r3 = x, result -> r2 ADD r0, r3, r3, LSL #1 // r0 = 3x ADD r0, r0, r0 // r0 = 6x SUB r0, r0, #9 // r0 = 6x - 9 MUL r2, r3, r0 // r2 = x*(6x - 9) ADD r2, r2, #2 // r2 = 6x^2 - 9x + 2
Option B: Minimal multiplies with a single MUL and shift-adds
// r3 = x, result -> r2 MUL r0, r3, r3 // r0 = x*x ADD r0, r0, r0, LSL #1 // r0 = 3*x*x ADD r0, r0, r0 // r0 = 6*x*x ADD r1, r3, r3, LSL #3 // r1 = x + 8x = 9x SUB r2, r0, r1 // r2 = 6x^2 - 9x ADD r2, r2, #2 // r2 = 6x^2 - 9x + 2
Option D: Use MLA (multiply-accumulate) and Horner form x(6x − 9) + 2
MOV r1, #2 // r3 = x, r1 = 2, result -> r2 ADD r0, r3, r3, LSL #1 // r0 = 3x ADD r0, r0, r0 // r0 = 6x SUB r0, r0, #9 // r0 = 6x - 9 MLA r2, r3, r0, r1 // r2 = r3*r0 + r1 = x(6x - 9) + 2

## Slide 37: Flags ANDS
What are value of r2, and NZCV flags after execution, assuming all flags are initially 0.
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ANDS r2, r1, r0, LSL #1

## Slide 38: Flags ANDS ANS
What are value of r2, and NZCV flags after execution, assuming all flags are initially 0.
ANS: r2 = 0x00000000
NZCV = 0110
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ANDS r2, r1, r0, LSL #1
ANS:
Left shift (LSL #1) moves the bits in r0 left by 1 bit. The bitwise AND is then computed: r2 = r1 & (r0 << 1).
N (Negative flag): Set to 0 because result r2 = 0x00000000, which is not negative.
Z (Zero flag): Set to 1 because the result is zero (r2 = 0).
C (Carry flag): Set to 1. The last bit shifted out was 1. (ANDS does not affect C flag.)
V (Overflow flag): Unchanged by AND operation.

## Slide 39: Flags ADDS
What are value of r2, and NZCV flags after execution, assuming all flags are initially 0.
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ADDS r2, r1, r0, LSL #1

## Slide 40: Flags ADDS ANS
What are value of r2, and NZCV flags after execution, assuming all flags are initially 0.
ANS: r2 = 0xFFFFFE01
NZCV = 1000
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ADDS r2, r1, r0, LSL #1
ANS: Left shift (LSL #1) moves the bits in r0 left by 1 bit, so r0 = 0xFFFFFE00. ADDS is then computed: r2 = r1 + (r0 << 1) = 0xFFFFFE01
  LSL does not update flags; ADDS updates flags
N (Negative): Since result r2 = 0xFFFFFE01 when interpreted as signed 32-bit (two's complement) is negative (most significant bit is 1), N = 1.
Z (Zero): Result is not zero, Z = 0.
C (Carry): for ADDS, C is the carry-out from the addition (unsigned overflow). Since 0x0000_0001 + 0xFFFF_FE00 < 2^32, there is no carry-out → C = 0.
  Note: the shift’s carry-out was 1, but ADDS overwrites the flags; the final C is the addition carry-out (0).
V (Overflow): Overflow is set if there is a signed overflow. Here:
  is positive; is negative since high bit is set; 2 operands have different signs, no overflow, so V = 0.
  Recall “Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign. ”
Notes: Here, adding a small positive number to a large value didn't overflow beyond 32 bits. So
, i.e., signs of inputs are same, but result sign differs.
Here, adding a small positive number 1 to a large value didn't overflow beyond 32 bits. So
, i.e., signs of inputs are same, but result sign differs.

## Slide 41: Flags
Suppose registers have the following values:
What are value of r4, and NZCV flags after execution, assuming all flags are initially 0. (Assume each instruction runs individually, not sequentially.)
  (a) ADD r4, r0, r2, ASR #3
  (b) ADDS r4, r0, r1
  (c) LSRS r4, r0, #1
  (d) ANDS r4, r0, r3
  (e) CMP r2, #3
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000003
r3 | 0xFFFFFFF0
Notes:   r0 = 0xFFFFFFFF
  r1 = 0x00000001
  r2 = 0x00000003
  r3 = 0xFFFFFFF0
The N, Z, C, and V flags start out as zero.
After the execution of the following instructions, fill in the flag values.

## Slide 42: Flags ANS
(a) ADD r4, r0, r2, ASR #3
  First, r2 ASR #3: 0x00000003 >> 3 = 0x00000000 (arithmetic shift preserves sign)
    Carry bit is 0 (last bit shifted out was 0, the first bit of 011)
  Then: r4 = r0 + 0 = 0xFFFFFFFF + 0 = 0xFFFFFFFF
  Result: r4 = 0xFFFFFFFF, NZCV = 0000
    ADD does not affect flags
(b) ADDS r4, r0, r1
  r4 = 0xFFFFFFFF + 0x00000001 = 0x00000000 (truncated to 32-bit)
  N = 0 (result bit 31 = 0, not negative)
  Z = 1 (result is zero)
  C = 1 (carry out from bit 31: 0xFFFFFFFF + 1 produces carry)
  V = 0 (no signed overflow: -1 + 1 = 0, valid in 32-bit signed range)
  Result: r4 = 0x00000000, NZCV = 0110
(c) LSRS r4, r0, #1
  Logical shift right with flag update: 0xFFFFFFFF >> 1 = 0x7FFFFFFF
  N = 0 (result bit 31 = 0)
  Z = 0 (result is not zero)
  C = 1 (last bit shifted out was 1)
  V = 0 (logical shifts don't affect overflow flag)
  Result: r4 = 0x7FFFFFFF, NZCV = 0010
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000003
r3 | 0xFFFFFFF0

## Slide 43: Flags ANS
(d) ANDS r4, r0, r3
  Bitwise AND with flag update: 0xFFFFFFFF & 0xFFFFFFF0 = 0xFFFFFFF0
  N = 1 (result MSB = 1, negative)
  Z = 0 (result is not zero)
  C = previous value, assumed to be 0 (C is unaffected by ANDS)
  V = previous value, assumed to be 0 (V is unaffected by ANDS)
  Result: r4 = 0xFFFFFFF0, NZCV = 1000
(e) CMP r2, #3
  Compare operation: r2 - 3 = 3 - 3 = 0 (result not stored, only flags updated)
  N = 0 (subtraction result is 0, bit 31 = 0)
  Z = 1 (subtraction result is 0)
  C = 1 (no borrow: 3 ≥ 3, so C = 1 = not borrow)
  V = 0 (no signed overflow in 3 - 3)
  Result: NZCV = 0110
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000003
r3 | 0xFFFFFFF0

## Slide 44: Flags
Suppose registers have the following values:
What are value of r3, and NZCV flags after execution, assuming all flags are initially 0. (Assume each instruction runs individually, not sequentially.)
  (a) ADD r3, r0, r2
  (b) ADDS r3, r0, r2
  (c) SUBS r3, r0, r0
  (d) LSL r3, r0, #1
  (e) LSRS r3, r1, #1
  (f) ANDS r3, r0, r2
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000000
Notes: Suppose
  r0 = 0xFFFFFFFF, r1 = 0x00000001, r2 = 0x00000000,
  NZCV = 0000 initially

## Slide 45: Flags ANS
(a) ADD r3, r0, r2
  r3 = 0xFFFFFFFF
  NZCV = 0000 (ADD without S does not update flags)
(b) ADDS r3, r0, r2
  r3 = 0xFFFFFFFF, NZCV = 1000
    N = 1 (MSB = 1)
    Z = 0 (nonzero)
    C = 0 (no carry out)
    V = 0 (no signed overflow)
(c) SUBS r3, r0, r0
  r3 = 0x00000000 (r0 − r0 = 0), NZCV = 0110
    N = 0 (MSB = 0)
    Z = 1 (result == 0)
    C = 1 (no borrow: unsigned r0 ≥ r0)
    V = 0 (no signed overflow)
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000000

## Slide 46: Flags ANS
(d) LSL r3, r0, #1
  r3 = 0xFFFFFFFE (logical left shift: 0xFFFF_FFFF << 1), NZCV = 0000
    LSL without S does not update flags
(e) LSRS r3, r1, #1
  r3 = 0x00000000 (0x0000_0001 >> 1 = 0), NZCV = 0110
    N = 0
    Z = 1 (result zero)
    C = 1 (bit shifted out = original bit0 = 1)
    V = 0 (shifts do not set V)
(f) ANDS r3, r0, r2
  r3 = 0x00000000 (0xFFFF_FFFF & 0x0000_0000 = 0), NZCV = 0100
    N = 0
    Z = 1 (result zero)
    C = 0 (unchanged)
    V = 0 (unchanged)
r0 | 0xFFFFFFFF
r1 | 0x00000001
r2 | 0x00000000

## Slide 47: Addition & Subtraction
For a 4-bit system, calculate the result of summation, setting C and V flags
Expression | Result | C | V | Correct? Unsigned/ Signed | Decimal Unsigned (GT: Ground Truth) | Decimal Signed (GT: Ground Truth)
0100 + 0010 | 0110 |  |  |  |  | 
0100 + 0110 | 1010 |  |  |  |  | 
1100 + 1110 | 1010 |  |  |  |  | 
1100 + 1010 | 0110 |  |  |  |  | 
0100 - 0010 | 0010 |  |  |  |  | 
0100 - 0110 | 1110 |  |  |  |  | 
1100 - 0110 | 0110 |  |  |  |  | 
0100 - 1110 | 0110 |  |  |  |  | 

## Slide 48: Addition & Subtraction ANS
Expression | Result | C | V | Correct? Unsigned/ Signed | Decimal Unsigned (GT: Ground Truth) | Decimal Signed (GT: Ground Truth)
0100 + 0010 | 0110 | 0 | 0 | Y / Y | 4 + 2 = 6 | 4 + 2 = 6
0100 + 0110 | 1010 | 0 | 1 | Y / N | 4 + 6 = 10 | 4 + 6 = -6 (GT 10)
1100 + 1110 | 1010 | 1 | 0 | N / Y | 12 + 14 = 10 (GT 26) | -4 + (– 2) = -6
1100 + 1010 | 0110 | 1 | 1 | N / N | 12 + 10 = 6 (GT 22) | -4 + (–6) = 6 (GT -10)
0100 - 0010 | 0010 | 1 | 0 | Y / Y | 4 – 2 = 2 | 4 – 2 = 2
0100 - 0110 | 1110 | 0 | 0 | N / Y | 4 – 6 = 14 (GT -2) | 4 – 6 = -2
1100 - 0110 | 0110 | 1 | 1 | Y / N | 12 – 6 = 6 | -4 – 6 = 6 (GT -10)
0100 - 1110 | 0110 | 0 | 0 | N / Y | 4 – 14 = 6 (GT -10) | 4 – (-2) = 6
For a 4-bit system, calculate the result of summation, setting C and V flags
  For a 4-bit system, unsigned range is [0, 15], signed range is [-8, 7]

## Slide 49: Addition & Subtraction ANS
0 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
C = 0
V = 0
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
C = 0
V = 1
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1 | 0 | 1 | 0
C = 1
V = 0
0 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 0
C = 1
V = 1
Carry
Carry
Carry
Carry

## Slide 50: Addition & Subtraction ANS
1 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 1 | 1 | 0
0 | 0 | 1 | 0
C = 1
V = 0
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
C = 0
V = 0
0 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 0
C = 1
V = 1
0 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
C = 0
V = 0
0100 – 0010 = 0100 + 1110
0100 – 0110 = 0100 + 1010
1100 – 0110 = 1100 + 1010
0100 – 1110 = 0100 + 0010
Carry
Carry
Carry
Carry