## Slide 1: Z. Gu
Fall 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Control Flow in Assembly
Exercises ANS
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Pseudocode to Assembly
Write assembly program for pseudocode, one version without Conditional Execution instructions, one version with Conditional Execution.
Pseudocode | Assembly Program
if (r0 != r1) r2 = r2 + r2 | 
Pseudocode | Assembly Program w/Conditional Execution
if (r0 != r1) r2 = r2 + r2 | 
Notes: Compare r0 and r1
; Branch to skip if r0 == r1 (skip the addition)
; r2 = r2 + r2 (only executed if r0 != r1)
; Compare r0 and r1
ANS A:
  CMP r0, r1
  BEQ skip
  ADD r2, r2, r2
  skip:
ANS B:

## Slide 3: Pseudocode to Assembly ANS
Write assembly program for pseudocode, one version without Conditional Execution instructions, one version with Conditional Execution.
  if (r0 != r1) r2 = r2 + r2
Pseudocode | Assembly Program
if (r0 != r1) r2 = r2 + r2 | CMP r0, r1 BEQ skip ADD r2, r2, r2 skip:
Pseudocode | Assembly Program w/Conditional Execution
if (r0 != r1) r2 = r2 + r2 | CMP r0, r1 ADDNE r2, r2, r2
Notes: Compare r0 and r1
; Branch to skip if r0 == r1 (skip the addition)
; r2 = r2 + r2 (only executed if r0 != r1)
; Compare r0 and r1
ANS A:
  CMP r0, r1
  BEQ skip
  ADD r2, r2, r2
  skip:
ANS B:

## Slide 4: Pseudocode to Assembly
Write assembly program for pseudocode.
Pseudocode | Assembly Program 1
r1 = (r0 >> 4) & 15 | 
Notes: Alternative solution:

## Slide 5: Pseudocode to Assembly ANS
Write assembly program for pseudocode.
Pseudocode | Assembly Program 1
r1 = (r0 >> 4) & 15 | MOV r1, r0, LSR #4 AND r1, r1, #0x0F %AND r1, r1, #15 is also OK
Pseudocode | Assembly Program 2
r1 = (r0 >> 4) & 15 | AND r1, r0, #0xF0 MOV r1, r1, LSR #4
Assembly Program 1: It computes r1 = (r0 >> 4) & 15 shifting it down by 4 bits, then masking the low nibble (4 bits) with 0x0F (or 0xF).
Assembly Program 2: It computes r1 = (r0 >> 4) & 15 by first masking the high nibble with 0xF0 and then shifting it down by 4 bits.
  AND r1, r0, #0xF0 keeps only bits [7:4] of r0, clearing all others.
  MOV r1, r1, LSR #4 performs a logical right shift by 4 on the masked value, moving those bits into positions [3:0].
Notes: Alternative solution:

## Slide 6: Assembly Program Understanding
What is r0 equal to after running this program:
  MOV r0, #10
  MOV r1, #7
  MOV r2, #5
  CMP r1, r2
  ADDGT r0, r0, #100

## Slide 7: Assembly Program Understanding ANS
What is r0 equal to after running this program:
  MOV r0, #10 ; Load immediate value 10 into r0
  MOV r1, #7 ; Load immediate value 7 into r1
  MOV r2, #5 ; Load immediate value 5 into r2
  CMP r1, r2 ; Compare r1 and r2 (compute r1-r2, set flags)
  ADDGT r0, r0, #100 ; Add 100 to r0 only if r1 > r2 (Greater Than)
This code sets r0 to 10, compares 7 and 5. Since 7 > 5, adds 100 to the base value of 10 to get 110
What about:
  MOV r0, #10
  MOV r1, #7
  MOV r2, #5
  SUBS r1, r1, r2
  ADDGE r0, r0, #100
Here r0 = 110, since SUBS sets flags and ADDGE is executed
Notes: bx lr ; Branch and exchange, return to caller

## Slide 8: C to Assembly
save[] is an array of 32-bit integers. Assume that i and k correspond to registers r1 and r2, and the base of the array save is in r0. Write assembly code corresponding to this C code.
C code | Assembly Program
while (save[i] == k) i += 1; | ; r0 = &save[0] (base address of array) ; r1 = i (index) ; r2 = k (value to compare) ...

## Slide 9: C to Assembly ANS
C code | Assembly Program
i = 0; while (save[i] == k) i += 1; | ; r0 = &save[0] (base address of array) ; r1 = i (index) ; r2 = k (value to compare) loop: LDR r3, [r0, r1, LSL #2] ; r3 = save[i], 32-bit loads with index scaled by 4, so r3 is loaded from mem address r0+4*r1 CMP r3, r2 ; compare save[i] with k BNE done ; exit loop if save[i] != k ADD r1, r1, #1 ; i += 1 B loop ; repeat done:
save[] is an array of 32-bit integers. Assume that i and k correspond to registers r1 and r2, and the base of the array save is in r0. Write assembly code corresponding to this C code. (This program is not perfect, since the array size of save[] is not considered, so the while loop may never terminate)
Notes: ; while (save[i] == k) i += 1;
loop:
LDR r3, [r0, r1, LSL #2] ; r3 = save[i] (index scaled by 4 bytes) [98][121]
CMP r3, r2 ; compare save[i] with k [109]
BNE done ; exit loop if not equal [93]
ADD r1, r1, #1 ; i += 1 [109]
B loop ; repeat [93]
done:

## Slide 10: C to Assembly ANS 2
C code | Assembly Program
i = 0; while (save[i] == k) i += 1; | ; r0 = &save[0] ; pointer to current element ; r2 = k ; value to compare loop: LDR r3, [r0], #4 ; load current save[i], advance pointer CMP r3, r2 BNE done B loop done:
This version removes r1, and uses post-index addressing to increment the array pointer r0, adding 4 to r0 in every loop iteration
Notes: ; while (save[i] == k) i += 1;
loop:
LDR r3, [r0, r1, LSL #2] ; r3 = save[i] (index scaled by 4 bytes) [98][121]
CMP r3, r2 ; compare save[i] with k [109]
BNE done ; exit loop if not equal [93]
ADD r1, r1, #1 ; i += 1 [109]
B loop ; repeat [93]
done:

## Slide 11: C to Assembly
Write the equivalent assembly program for this piece of code in C.
C code | Assembly Program
for (i=0; i<8; i++){ a[i] = b[7-i]; } | ; Assume r0 = base address of a, r1 = base address of b
Notes:   for (i=0; i<8; i++){
  a[i] = b[7-i];
  }
ANS:
  ; for (i=0; i<8; i++) { a[i] = b[7-i]; }
  ; Assume r0 = base address of a, r1 = base address of b
  MOV r2, #0 ; i = 0
  loop_start:
  …
  loop_end:

## Slide 12: C to Assembly ANS
Write the equivalent assembly program for this piece of code in C.
C code | Assembly Program
for (i=0; i<8; i++){ a[i] = b[7-i]; } | ; Assume r0 = base address of a, r1 = base address of b MOV r2, #0 ; i = 0 loop_start: CMP r2, #8 BGE loop_end RSB r3, r2, #7 ; r3 = 7 – i ;Note that SUB r3, #7, r2 is incorrect, since operand 1 cannot be an immediate value LDR r4, [r1, r3, LSL#2] ; Load b[7-i] from mem address r1 + 4*r3 STR r4, [r0, r2, LSL#2] ; Store to a[i] to mem address r0 + 4*r2 ADD r2, r2, #1 ; i++ B loop_start loop_end:

## Slide 13: C to Assembly: What is wrong?
C Program | Assembly Program
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #10 ; Compare r0 with 10 while r0 <=10 BEQ done ; If cnt == 10, branch to done ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUB r0, r0, #1 ; cnt--; sets flags BNE loop ; repeat until cnt == 0 (10 times) done:

## Slide 14: C to Assembly: What is wrong? ANS (cnt declared as signed int)
C Program (int) | Assembly Program 1
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #11 ; Compare r0 with 11 (exit when cnt reaches 11) BEQ done ; If cnt == 11, branch to done ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:
The loop checks CMP r0, #10 and exits immediately if they are equal (BEQ done). Because it exits before executing the loop body when cnt == 10, the loop body only executes for 9 iterations, r0 values 1 through 9.
Option 1: Compare against 11: CMP r0, #11 and branch on equal BEQ done.
Option 2: Keep the comparison with 10 but change the branch logic to branch out if greater than 10: BGT done.
C Program (int) | Assembly Program 2
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #10 ; Compare r0 with 10 while r0 <= 10 BGT done ; If cnt > 10, branch to done ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:
Notes: Loop runs for 9 iterations, not 10
Option 1 (CMP r0, #11): By changing the comparison to 11 and keeping BEQ done, the loop will now execute when r0 is 10, and only exit when r0 finally increments to 11.
Option 2 (BGT done): By keeping the comparison at 10 but changing the branch instruction to Branch if Greater Than (BGT), the loop will execute when r0 is 10 (since 10 is not greater than 10) and will only branch out when r0 hits 11.

## Slide 15: C to Assembly: What is wrong? ANS (cnt declared as unsigned int)
C Program (uint) | Assembly Program
uint cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #11 ; Compare r0 with 11 (exit when cnt reaches 11) BEQ done ; If cnt == 11, branch to done ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:
C Program (uint) | Assembly Program
uint cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #10 ; Compare r0 with 10 while r0 <= 10 BHI done ; If cnt > 10, branch to done ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:

## Slide 16: C to Assembly: What is wrong? ANS
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: SUB r0, r0, #1 ; cnt-- (no S suffix: flags not updated) BNE loop ; repeat until cnt == 0 (10 times) done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations B check loop: SUBS r0, r0, #1 ; cnt--; sets flags check: BNE loop ; repeat until cnt == 0 (10 times) done:
Error: BNE tests stale condition flags (typically an infinite loop) because SUB without the S suffix does not update the CPU condition flags.
ANS: use SUBS to set flags; (optionally) add a B check before loop body
(With or without “B check”, program behavior is the same if cnt = r0 = 10 initially, but different if cnt = r0 = 0 initially. c.f. pp 22-25 in Ch6 lecture on while loop and do-while loop. )

## Slide 17: C to Assembly, fill in blank
C Program | Assembly Program
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: ; loop body ADD ??? ; cnt++ CMP ??? BLE ??? ; while (cnt <= 10) continue done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS ??? ; cnt--; sets Z flag if r0=0 BNE ??? ; repeat until cnt == 0 (10 times) done:
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS ???; cnt--; sets Z flag if r0=0 BGT ??? ; repeat until cnt == 0 (10 times) done:

## Slide 18: C to Assembly ANS (assuming cnt is signed int)
C Program | Assembly Program
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: ; loop body ADD r0, r0, #1 ; cnt++ CMP r0, #10 BLE loop ; while (cnt <= 10) continue done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BNE loop ; repeat until cnt == 0 (10 times) done:
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BGT loop ; repeat until cnt == 0 (10 times) done:

## Slide 19: C to Assembly ANS (assuming cnt is unsigned int)
C Program | Assembly Program
uint cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: ; loop body ADD r0, r0, #1 ; cnt++ CMP r0, #10 BLS loop ; while (cnt <= 10) continue done:
C Program | Assembly Program
uint cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BNE loop ; repeat until cnt == 0 (10 times) done:
C Program | Assembly Program
uint cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BHI loop ; repeat until cnt == 0 (10 times) done:

## Slide 20: C to Assembly: What is wrong?
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BPL loop ; repeat until cnt == 0 (10 times) done:
Notes: No—do not replace BNE with BPL in that loop.image.jpg
Why BNE is correct
After SUB r0, r0, #1, the Zero flag Z is set only when r0 becomes 0, so BNE (“branch if not equal to zero”) repeats exactly until the counter hits 0, giving 10 iterations from an initial value of 10.image.jpg
Why BPL is wrong here
BPL tests the Negative flag N=0 (i.e., “plus/non‑negative”), not whether the value is nonzero. Starting from 10 and decrementing, N stays 0 for 10 down to 0, so BPL would still branch at r0=0 and continue into −1
If using “plus” logic
To stop before going negative, the condition would need to be “branch while r0 > 0,” which is achieved with BGT after a CMP r0,#0 or by keeping BNE after SUBS. Using BPL alone does not encode “greater than zero.”

## Slide 21: C to Assembly: What is wrong? ANS
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BPL loop ; repeat until cnt == 0 (10 times) done:
BPL, Branch if PLus (Positive or Zero, N = 0), tests the Negative flag N=0 (i.e., r0 >=0). Starting from 10 and decrementing, N stays 0 for 10 down to 0, so BPL would still branch at r0 = 0. Then SUBS makes r0 = −1, which sets N = 1, so BPL does not branch and the loop exits. Hence BPL allows the loop to run at 0 and overshoot by one iteration.
What’s wrong: BPL tests for ≥ 0, not > 0 → extra iteration. How to fix: Replace BPL loop with BGT loop.
If the loop variable were unsigned, you’d instead use BHI (“branch if higher”) for the same effect.
Quiz: is BPL same as BGE?
ANS: No. PL checks N == 0; GE checks N == V. In this program BGE and BPL have the same behavior, since you never have signed overflow. But in general not, in case of signed overflow V = 1, c.f. p. 16 in Ch6 lecture “Signed Comparison Examples”
Notes: No—do not replace BNE with BPL in that loop.image.jpg
Why BNE is correct
After SUB r0, r0, #1, the Zero flag Z is set only when r0 becomes 0, so BNE (“branch if not equal to zero”) repeats exactly until the counter hits 0, giving 10 iterations from an initial value of 10.image.jpg
Why BPL is wrong here
BPL tests the Negative flag N=0 (i.e., “plus/non‑negative”), not whether the value is nonzero. Starting from 10 and decrementing, N stays 0 for 10 down to 0, so BPL would still branch at r0=0 and continue into −1
If using “plus” logic
To stop before going negative, the condition would need to be “branch while r0 > 0,” which is achieved with BGT after a CMP r0,#0 or by keeping BNE after SUBS. Using BPL alone does not encode “greater than zero.”

## Slide 22: C to Assembly
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i = i - 1) { array[i] = array[i] * 8; } | % R0 = base address of array, R1 = i MOV R0, #0x60000000 ; base address where array resides MOV R1, #199 ; i = 199 …

## Slide 23: C to Assembly ANS
For an array of 32‑bit ints, each element is 4 bytes, so element i lives at base + i*4, which is implemented as base + (i << 2) via LSL #2 in the addressing mode
BPL “Branch if PLus” branches when the N (negative) flag N == 0, meaning the prior result was positive or zero
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i = i - 1) array[i] = array[i] * 8; | ; R0 = array base address, R1 = i MOV R0, #0x60000000 MOV R1, #199 FOR LDR R2, [R0, R1, LSL #2] ;R2 = array(i) LSL R2, R2, #3 ; R2 = R2<<3 = R2*8 STR R2, [R0, R1, LSL #2] ;array(i) = R2 SUBS R1, R1, #1 ; i=i-1 and set flags BPL FOR ; if (i >= 0) repeat loop

## Slide 24: C to Assembly
C Program | Assembly Program
//Calculate x such that 2^x=128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE DONE

## Slide 25: C to Assembly ANS
C Program | Assembly Program
//Calculate x such that 2^x = 128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE CMP r0, #128 ; r0-128 BEQ DONE ; if (pow==128) exit loop LSL r0, r0, #1 ; pow = pow * 2 ADD r1, r1, #1 ; x = x + 1 B WHILE ; repeat loop DONE

## Slide 26: C to Assembly ANS
Edge case: If r0 starts as 128 (zero-iteration case), this version will execute the body once (doubling to 256 and incrementing r1) before checking — i.e., wrong for that initial condition, c.f. pp 22-25 in Ch6 lecture on while loop and do-while loop. To handle the edge case, add a branch to “CMP r0, #128” before the WHILE (adding a label to the CMP instruction)
C Program | Assembly Program
//Calculate x such that 2^x = 128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE LSL r0, r0, #1 ; pow = pow * 2 ADD r1, r1, #1 ; x = x + 1 CMP r0, #128 ; r0-128 BNE WHILE ; repeat loop DONE

## Slide 27: C to Assembly
C Program | Assembly Program
int i; int sum = 0; for (i = 1; i <= 22; i++) sum += i; | 
Notes: bx lr

## Slide 28: C to Assembly ANS
C Program | Assembly Program 1
int i; int sum = 0; for (i = 1; i <= 22; i++) sum += i; | mov r1, #0 /* r1 ← 0 */ mov r2, #1 /* r2 ← 1 */ loop: cmp r2, #22 /* compare r2 and 22 */ bgt end /* branch if r2 > 22 to end */ add r1, r1, r2 /* r1 ← r1 + r2 */ add r2, r2, #1 /* r2 ← r2 + 1 */ b loop end:
C Program | Assembly Program 2
int i; int sum = 0; for (i = 1; i <= 22; i++) sum += i; | mov r1, #0 /* r1 ← 0 */ mov r2, #1 /* r2 ← 1 */ b check_loop /* unconditionally jump at the end of the loop */ loop: add r1, r1, r2 /* r1 ← r1 + r2 */ add r2, r2, #1 /* r2 ← r2 + 1 */ check_loop: cmp r2, #22 /* compare r2 and 22 */ ble loop /* branch if r2 <= 22 to the beginning of the loop */ end:
Notes: bx lr

## Slide 29: C to Assembly ANS
Assembly Program 1:
  Two branches per iteration in the steady state: a conditional (cmp + bgt) and an unconditional b loop. That increases dynamic branch count.
Assembly Program 2:
  Only one conditional branch per iteration (the ble), after the body — fewer dynamic branches overall. In steady-state this is usually faster.
  Better steady-state throughput and fewer branch misprediction opportunities in hot loops (one backward taken conditional is a canonical, well-predicted pattern).
Notes: https://thinkingeek.com/2013/01/20/arm-assembler-raspberry-pi-chapter-6/

## Slide 30: Assembly Programming
Write a program that reverses the bits in a register, such that the register containing d31,d30,d29...d1,d0 now contains d0,d1,...d29,d30,d31.

## Slide 31: Assembly Programming ANS
ANS:
  ; Reverse bits in r0, result in r1
  MOV r1, #0 ; Initialize result
  MOV r2, #32 ; Bit counter
  reverse_loop:
  CMP r2, #0
  BEQ reverse_end
  LSL r1, r1, #1 ; Shift result left
  AND r3, r0, #1 ; Get LSB of r0
  ORR r1, r1, r3 ; Add to result
  LSR r0, r0, #1 ; Shift r0 right
  SUB r2, r2, #1 ; Decrement counter
  B reverse_loop
  reverse_end:
Example with 8 bits:
Let input r0 = 0b1011_0010
Initialize r1 = 0, r2 = 8 (bit counter) for illustration purpose, and r3 is the scratch for the extracted bit; the loop body runs 8 times.
Iteration 1
LSL r1, r1, #1: r1 = 0 << 1 = 0.
AND r3, r0, #1: r3 = 0b1011_0010 & 1 = 0 (LSB of r0 is 0).
ORR r1, r1, r3: r1 = 0 | 0 = 0.
LSR r0, r0, #1: r0 = 0b0101_1001 (shift right, next LSB becomes current).
SUB r2, r2, #1: r2 = 7.
Effect: The first output bit appears at the LSB of r1 and equals original d0.
Iteration 2
LSL r1: r1 = 0 << 1 = 0.
AND r3, r0, #1: r3 = 0b0101_1001 & 1 = 1 (new LSB is 1).
ORR r1, r1, r3: r1 = 0 | 1 = 1 (now r1 = 0b0000_0001).
LSR r0: r0 = 0b0010_1100.
SUB r2: r2 = 6.
Effect: r1 now holds 01, which are the bits “d0 d1”.
On each subsequent iteration, r1 is shifted left before inserting the next bit, so earlier bits move toward the MSB while the newly inserted bit always starts at the LSB; over the whole loop, this builds the reversed word with the earliest extracted bits ending up toward the MSB by the end.

## Slide 32: Test for Equal
Give the different methods to test if two values held in registers r0 and r1 are equal.

## Slide 33: Test for Equal ANS
Give the different methods to test if two values held in registers r0 and r1 are equal.
ANS:
  ; Method 1: Compare instruction
  CMP r0, r1
  ; Method 2: Exclusive OR
  EORS r2, r0, r1 ; If equal, result is zero and Z flag set
  ; Method 3: Subtract and test
  SUBS r2, r0, r1 ; If equal, result is zero and Z flag set
  The effect on flags are the same for CMP and SUBS, except CMP discards the result of the subtraction

## Slide 34: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 35: Conditional Instructions
Write the following ARMv7 instructions:
  Add registers r3 and r6 only if N is clear (from a previous instruction). Store the result in register r7.
  Multiply registers r7 and r12, put the results in register r3 only if C is set and Z is clear (from a previous instruction)
  Compare registers r6 and r8 only if Z is clear (from a previous instruction)
Notes: After a CMP/CMN or SUBS/ADDS used as an unsigned compare where the first operand is strictly greater than the second; for example, after CMP r0, r1, HI means r0 > r1 when treated as unsigned.

## Slide 36: Conditional Instructions ANS
Write the following ARMv7 instructions:
  Add registers r3 and r6 only if N is clear. Store the result in register r7.
  Multiply registers r7 and r12, put the results in register r3 only if C is set and Z is clear
  Compare registers r6 and r8 only if Z is clear
ANS:
  ; Plus, Positive or Zero, (N=0). Add r3 and r6 only if N is clear, store in r7
  ADDPL r7, r3, r6
  ; HI, Unsigned Higher, (C=1 & Z=0). Multiply r7 and r12, put result in r3 only if C is set and Z is clear
  MULHI r3, r7, r12
  ; NE, Not equal (Z=0). Compare r6 and r8 only if Z is clear
  CMPNE r6, r8
Notes: After a CMP/CMN or SUBS/ADDS used as an unsigned compare where the first operand is strictly greater than the second; for example, after CMP r0, r1, HI means r0 > r1 when treated as unsigned.

## Slide 37: Assembly to C
Write the equivalent C program for the following assembly code, assuming registers and C variables are related as (x=r0, y=r1). ( Variables in C are in memory, and load/store assembly instructions are omitted here for brevity.) For example:
Assembly Program | C Program
CMP r0, #5 MOVEQ r0, #10 BLEQ fn | if (x == 5) { x = 10; fn(x); }
Assembly Program | C Program
CMP r0, #0 MOVLE r0, #0 MOVGT r0, #1 | 
Assembly Program | C Program
CMP r0, #'A’ CMPNE r0, #'B' MOVEQ r1, #1 | 

## Slide 38: Assembly to C ANS
Assembly Program | C Program
CMP r0, #5 MOVEQ r0, #10 BLEQ fn | if (x == 5) { x = 10; fn(x); }
Assembly Program | C Program
CMP r0, #0 MOVLE r0, #0 MOVGT r0, #1 | if (x <= 0) x = 0; else x = 1;
Assembly Program | C Program
CMP r0, #'A’ CMPNE r0, #'B' MOVEQ r1, #1 | if (x == ‘A’ ¦¦ x == 'B') y = 1;
Assembly Program | C Program
CMP r0, #'A’ CMP r0, #’B’ %incorrect, since the 1st CMP sets flags that are overwritten by the 2nd CMP MOVEQ r1, #1 | if (x == ‘A’ ¦¦ x == 'B') y = 1;

## Slide 39: Conditional Execution
Rewrite the assembly program to use conditional execution statements.
Assembly Program | Assembly Program with Cond. Exec
CMP r3, #0 BEQ next ADD r0, r0, r1 SUB r0, r0, r2 next ... | 

## Slide 40: Conditional Execution ANS
Rewrite the assembly program to use conditional execution statements.
Assembly Program | Assembly Program with Cond. Exec
CMP r3, #0 BEQ next ADD r0, r0, r1 SUB r0, r0, r2 next ... | CMP r3, #0 ADDNE r0, r0, r1 SUBNE r0, r0, r2 ...