## Slide 1: Z. Gu
Fall 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises ANS

## Slide 2: Stack
PUSH {Rd} == STMDB SP!, {Rd} == STMFD SP!, {Rd}
  SUB SP, SP, #4 @ SP = SP-4 (descending stack)
  STR Rd, [SP] @ (*SP) = Rd (full stack)
Push multiple registers
PUSH {r1, r2, r3, r7}
They are equivalent.
PUSH {r7}
PUSH {r3}
PUSH {r2}
PUSH {r1}
PUSH {r7, r2, r3, r1}
SP is decremented before PUSH (pre-decrement).
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. r1 is stored last.
Review
Notes: PUSH => SUB SP, SP, #4 STR RN, [SP]
POP => LDR RN, [SP] ADD SP, #4
PUSH {R1, R2} ==
STMFD SP!, {R1, R2} ; or STMDB SP!, {R1, R2}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).

## Slide 3: Stack
POP {Rd} == LDMIA SP!, {Rd} == LDMFD SP!, {Rd}
  LDR Rd, [SP] @ Rd = (*SP) (full stack)
  ADD SP, #4 @ SP = SP + 4 (Stack shrinks)
Pop multiple registers
POP {r7, r3, r2, r1}
They are equivalent.
POP {r1}
POP {r2}
POP {r3}
POP {r7}
POP {r1, r2, r3, r7}
SP is incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. r1 is loaded first.
Review

## Slide 4: Stack
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=?, r1=?

## Slide 5: Stack ANS
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
r2=2
r1=1
SP
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=1, r1=2
Stack contains only values like 2, 1… I write r2=2, r1=1 in the figures for illustration purposes only.

## Slide 6: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3} (same as POP {r0, r1, r2, r3})
Draw stack after each instruction. What is in registers after execution?
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
After POP {r0-r3}
r0=?, r1=?, r2=?, r3=?

## Slide 7: Stack ANS
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2} @ Equiv. to PUSH r2 \n PUSH r1
PUSH {r3,r0} @ Equiv. to PUSH r3 \n PUSH r0
POP {r0-r3} @ Equiv. to POP r0 \n POP r1 \n POP r2 \n POP r3
SP
r2=2
r1=1
SP
r2=2
r1=1
r3=3
r0=0
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
SP
After POP {r0-r3}
r0=0, r1=3, r2=1, r3=2

## Slide 8: Stack
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx
R1=0x11111111
R2=0x22222222
Before execution
What is content of stack, and position of SP, after PUSH {R2,R1}?
What are the values of R1/R2 after POP {R2}?
What are the correct instructions for swapping R1 and R2?

## Slide 9: Stack ANS
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
0x22222222
0x11111111
R1=0x11111111
R2=0x22222222
Before execution
Stack content and SP shown in figure
After POP {R2}, R1=0x11111111, R2=0x22222222

## Slide 10: Instructions for swapping R1 and R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 11: Program Understanding
0x10000200 | 60 | 1B | 11 | 12 | EE | FF | 11 | 22 | 33 | 44 | 55 | 66 | 77 | 88 | 99 | 92
0x100001F0 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B | 1C | 1D | 1E | 1F
0x100001E0 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 0A | 0B | 0C | 0D | 0E | 0F
R0 | 0x00000000
R1 | 0x10000200
R2 | 0x0000FFFF
R3 | 0x18675309
R4 | 0x00000000
R5 | 0x00000000
… | 
R13 | 0x10000200
PUSH {R1, R3}
POP {R5}
Compute register and memory values at each step of this program, given initial register values and memory contents, assuming little-endian memory ordering.
Initial Register Values
Initial Memory Contents

## Slide 12: Program Understanding ANS
0x10000200 | 60 | 1B | 11 | 12 | EE | FF | 11 | 22 | 33 | 44 | 55 | 66 | 77 | 88 | 99 | 92
0x100001F0 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 00 | 02 | 00 | 10 | 09 | 53 | 67 | 18
0x100001E0 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 0A | 0B | 0C | 0D | 0E | 0F
R0 | 0x00000000
R1 | 0x10000200
R2 | 0x0000FFFF
R3 | 0x18675309
R4 | 0x00000000
R5 | 0x10000200
… | 
R13 | 0x100001FC
R13 is SP = 0x10000200. Recall:
After two PUSHes, SP = 0x10000200 – 8 = 0x100001F8. Each PUSH is:
  SUB SP, SP, #4 @ SP = SP-4 (descending stack)
  STR Rd, [SP] @ (*SP) = Rd (full stack)
After one POP, SP = 0x100001F8 + 4 = 0x100001FC:
  LDR Rd, [SP] @ Rd = (*SP) (full stack)
  ADD SP, #4 @ SP = SP + 4 (Stack shrinks)
R5 = 0x10000200 (value of R1)
Final Register Values
Initial Memory Contents
PUSH {R1, R3}
POP {R5}
SP
SP after 2 PUSHes
SP after 1 POP

## Slide 13: Passing arguments and Returning Value
a64
b8
c16
d16
Subroutine
Register:
Register;
Register:
Return Value
Register R1:R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack
Fill in register names.
Register:

## Slide 14: Passing arguments and Returning Value ANS
a64
b8
c16
d16
Subroutine
Register r1:r0
Register r2
Register r3
Return Value
Register R1:R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack
Fill in register names.

## Slide 15: Argument Passing
Which registers are used to pass the arguments and return the result?
long fun (short a1, char a2, double a3, int a4, char a5)
R0 | R1 | R2 | R3
Registers
Stack in Memory

## Slide 16: Argument Passing ANS
Which registers are used to pass the arguments and return the result?
Each argument of 8-bit char, or 16-bit short, is passed in one 32-bit register; cannot use 1 register to pass more than one argument
  a1 (short) in R0.
  a2 (char) in R1.
  a3 (double) in R2 and R3.
  a4 (int) on the stack.
  a5 (char) on the stack. The result (long, 32 bits) is returned in R0.
long fun (short a1, char a2, double a3, int a4, char a5)
a1 | a2 | a3
a4 | a5 | 
Registers
Stack in Memory

## Slide 17: What’s wrong? Passing arguments and Returning Value
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOV r0, #5 ; e32
MOV r0, #1 ; a8
MOV r1, #2 ; b8
MOV r2, #3 ; c16
MOV r3, #4 ; d16
BL sum
...
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
ADD r0, r0, r1 ; add e32
BX LR
ENDP

## Slide 18: What’s wrong? Passing arguments and Returning Value ANS
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOV r0, #5 ; e32
PUSH {r0}
MOV r0, #1 ; a8
MOV r1, #2 ; b8
MOV r2, #3 ; c16
MOV r3, #4 ; d16
BL sum
...
ADD sp, sp, #4
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
LDR r1, [sp, #0] ; read argument e32
ADD r0, r0, r1 ; add e32
BX LR
ENDP
The caller is responsible to pop extra arguments out of the stack after the subroutine returns.

## Slide 19: What is Wrong?
Caller Program
extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s; ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 20: What is Wrong? ANS
Return result should be put into r0, not r1; also ADD r3, r3, r2 (not r0)
BX lr returns to caller
BX pc is not a return and will re-execute at the PC value
Caller Program
extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s; ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r3, r2 ; sum += a3 MOV r0, r3 BX lr ENDP

## Slide 21: Program Understanding
Write out the sequence of values of r0 and r7 after running this program.
start:
mov r0, #1
main:
add r0, r0, #1
cmp r0, #5
bne skip
bl call
skip:
b main
call:
add r7, r7, #255
mov r0, #1
bx lr
Notes: Here’s what the program does in practice:
It starts with x0 = 1.
It loops, incrementing x0 each time.
When x0 reaches 5, it calls call.
call adds 255 to x7 and resets x0 to 1.
Control returns to main, and the cycle repeats.
So the pattern goes like this:
x0: 1 → 2 → 3 → 4 → 5 → (call resets to 1)
x7: +255 each time x0 reaches 5

## Slide 22: Program Understanding ANS
It starts with r0 = 1. It loops, incrementing r0 each time. When r0 reaches 5, it calls subroutine call, which adds 255 to r7 and resets r0 to 1. Control returns to main, and the cycle repeats. So the pattern goes like this:
r0: 1 → 2 → 3 → 4 → 5 → (call resets to 1)
r7: +255 each time r0 reaches 5
start:
mov r0, #1 @ start: r0 = 1
main:
add r0, r0, #1 @ increment r0
cmp r0, #5 @ compare r0 to 5
bne skip @ if not equal, go to skip
bl call @ if equal, branch-and-link to call
skip:
b main @ unconditional branch back to main
call:
add r7, r7, #255 @ add 255 to r7 (side-effect)
mov r0, #1 @ reset r0 to 1
bx lr @ return (branch to link register)
Notes: Here’s what the program does in practice:
It starts with x0 = 1.
It loops, incrementing x0 each time.
When x0 reaches 5, it calls call.
call adds 255 to x7 and resets x0 to 1.
Control returns to main, and the cycle repeats.
So the pattern goes like this:
x0: 1 → 2 → 3 → 4 → 5 → (call resets to 1)
x7: +255 each time x0 reaches 5

## Slide 23: toLower
Caller Program
#include <stdio.h> extern int toLower(int); /* assembler routine */ int main(void) { static const char str[] = "Hello, World!"; const int len = sizeof(str)/sizeof(str[0]); char newstr[len]; int i; for (i = 0; i < len; i++) newstr[i] = toLower (str[i]); printf("%s\n", newstr); return 0; }
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 32; /*'a' - ‘A’ = 32 */ return c; }
Consider the following C program that converts all ASCII letters to lower case. Write the toLower function in ARMv7 assembly code.
Callee Program Assembly
.text .global toLower toLower:
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 24: toLower ANS
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 32; return c; }
Callee Program Assembly
.text .global toLower toLower: cmp r0, #'A' @ if c < 'A' -> skip_adjust blt skip_adjust cmp r0, #'Z' @ if c > 'Z' -> skip_adjust bgt skip_adjust add r0, r0, #32 @ c += 32 = 'a' - 'A' skip_adjust: bx lr
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 25: Program Understanding
Given the following code, fill in the blanks listed next to each instruction with the values that would be in each register or status bit after each instruction executes. Instruction addresses are given to the left of each assembly instruction (not part of the code). Assume that SP = 0x10000200 at the start of the program.
AREA mycode, CODE, READONLY
EXPORT __main
__main PROC
0x250 MOV R0, #5
0x254 MOV R1, #10
0x258 CMP R0, R1 ; NZCV = ______
0x25A BGE loop ; PC = ______(after this instruction)
0x25C BL foo ; LR = ______, PC = ____(after this inst.)
0x260 loop B loop
ENDP
foo PROC
0x262 PUSH{R0, R1} ; SP = ____________
0x264 POP{R1}
0x266 POP{R0} ; R0 = __________, SP = ____________
0x268 BX LR ; LR = ___________, PC = ____________
ENDP

## Slide 26: Program Understanding ANS
Given the following code, fill in the blanks listed next to each instruction with the values that would be in each register or status bit after the instruction executes. Instruction addresses are given to the left of each assembly instruction (not part of the code). Assume that SP = 0x10000200 at the start of the program.
AREA mycode, CODE, READONLY
EXPORT __main
__main PROC
0x250 MOV R0, #5
0x254 MOV R1, #10
0x258 CMP R0, R1 ; NZCV = 1000
0x25A BGE loop ; PC = 0x25C (after this instruction)
0x25C BL foo ; LR = 0x260, PC = 0x262 (after this inst.)
0x260 loop B loop
ENDP
foo PROC
0x262 PUSH{R0, R1} ; SP = 0x100001F8
0x264 POP{R1} ; R1 = 5
0x266 POP{R0} ; R0 = 10, SP = 0x10000200
0x268 BX LR ; LR = 0x260, PC = 0x260 (after this inst.)
ENDP

## Slide 27: Detailed Explanations
1. CMP R0, R1 (0x258)
  Performs: 5 - 10 = -5
  NZCV = 1000 (Negative=1, Zero=0, Carry=0, Overflow=0)
2. BGE loop (0x25A)
  BGE checks if N == V (Greater or Equal in signed comparison)
  Since N=1 and V=0, condition is FALSE
Branch NOT taken, continues to next instruction
  PC = 0x25C
3. BL foo (0x25C)
  Saves return address in LR and branches to foo
  LR = 0x260 (next instruction after BL)
  PC = 0x262 (address of foo)
4. PUSH {R0, R1} (0x262)
  Stack is descending and full, so SP decrements by 8 bytes (2 registers × 4 bytes)
  SP = 0x10000200 - 8 = 0x100001F8
5. POP {R0} (0x266)
  After popping both registers, R0 and R1 are swapped
  R0 = 10 (original R1 value)
  SP = 0x10000200 (back to original)
6. BX LR (0x268)
  Returns to address stored in LR
  LR = 0x260 (unchanged)
  PC = 0x260 (returns to caller)

## Slide 28: Separator Page
The following slides will not be covered in the exam

## Slide 29: If Then Else
Translate the following program into ARMv7 assembly.
C Program | Assembly Program
int foo(int x, int y) { if (x+y < 0) return 0; else return 1; } | @ int foo(int x, int y) - returns 0 if (x+y) < 0, else 1 @ x in r0, y in r1, return in r0 foo: … BX lr

## Slide 30: If Then Else ANS
Straight-line with conditional execution
foo: ADD r2, r0, r1 ; r2 = x + y CMP r2, #0 ; sets N,Z,V,C for signed compare to 0 MOVLT r0, #0 ; if (x+y) < 0 -> r0 = 0 MOVGE r0, #1 ; else r0 = 1 BX lr
Conditional branch to label w/ CMP
foo: ADD r2, r0, r1 CMP r2, #0 BLT .Lneg MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Combine add and compare with ADDS
foo: ADDS r2, r0, r1 ; r2 = x + y, sets flags from the sum MOVMI r0, #0 ; MI means N=1 (negative) MOVPL r0, #1 ; PL means N=0 (non-negative) BX lr
No temp register r2, reuse r0
foo: ADDS r0, r0, r1 ; r0 = x + y, flags set MOVMI r0, #0 MOVPL r0, #1 BX lr
Conditional branch to label w/ ADDS
foo: ADDS r2, r0, r1 BMI .Lneg ; if negative MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Notes: Straight-line with conditional execution
foo: ADD r2, r0, r1 ; r2 = x + y CMP r2, #0 ; sets N,Z,V,C for signed compare to 0 MOVLT r0, #0 ; if (x+y) < 0 -> r0 = 0 MOVGE r0, #1 ; else r0 = 1 BX lr
Conditional branch to label
foo: ADD r2, r0, r1 CMP r2, #0 BLT .Lneg MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Calling convention: inputs x,y in r0,r1; result in r0; lr holds return address; no callee-saved registers are clobbered.
Choose MI/PL (based on N) or LT/GE (signed) consistently; both are correct when flags come from the sum or a compare to zero.
For Thumb-2, prefer conditional branches or the IT block variant if permitted by assembler; for classic ARM state, full conditional MOVs avoid branches.

## Slide 31: Factorial
Fill in the blanks (marked TODO) for the assembly programs for calculating the factorial of a number, corresponding to the following C programs. One iterative version, one recursive version.
//Recursive version
#include <stdint.h>
uint32_t fact_rec(uint32_t n) {
if (n <= 1) {
return 1;
}
return n * fact_rec(n - 1);
}
//Iterative version
#include <stdint.h>
uint32_t fact_iter(uint32_t n) {
uint32_t acc = 1;
if (n <= 1) {
return 1;
}
while (n > 1) {
acc *= n;
n -= 1;
}
return acc;
}
Notes: (In the exams, I may provide most of the code and let you fill in the blanks.)

## Slide 32: Factorial
@ uint32_t fact_iter(uint32_t n); iterative version
@ r0 = n, returns r0 = n!
.global fact_iter
fact_iter:
PUSH {r4, lr} @ save callee-saved we’ll use and return addr
MOV r1, r0 @ r1 = n (loop counter)
MOV r0, #1 @ r0 = acc = 1
CMP r1, #1
BLS .Ldone_iter @ if n <= 1, return 1
@(unsigned compare)
.Lloop_iter:
@ TODO
.Ldone_iter:
POP {r4, lr}
BX lr
@ uint32_t factorial(uint32_t n); Recursive version
@ r0: n
@ returns r0: n!
factorial:
CMP r0, #1 @ if (n <= 1) ...
BLS base_case @ ... return 1
PUSH {lr} @ save return address for this frame
PUSH {r0} @ save current n on stack (we'll need it after the recursive call)
SUB r0, r0, #1 @ r0 = n - 1 (argument for recursive call)
BL factorial @ r0 = factorial(n - 1)
POP {r1} @ r1 = saved n (restore caller's n)
MUL r0, r0, r1 @ r0 = factorial(n - 1) * n
POP {lr} @ restore return address
BX lr @ return with result in r0
base_case:
@ TODO

## Slide 33: Factorial ANS
@ uint32_t fact_iter(uint32_t n); iterative version
@ r0 = n, returns r0 = n!
.global fact_iter
fact_iter:
PUSH {r4, lr} @ save callee-saved we’ll use and return addr
MOV r1, r0 @ r1 = n (loop counter)
MOV r0, #1 @ r0 = acc = 1
CMP r1, #1
BLS .Ldone_iter @ if n <= 1, return 1
@ (unsigned compare)
.Lloop_iter:
MUL r0, r0, r1 @ acc *= i
SUBS r1, r1, #1 @ i--
BHI .Lloop_iter @ continue while i > 1
@ (unsigned compare)
.Ldone_iter:
POP {r4, lr}
BX lr
@ uint32_t factorial(uint32_t n); Recursive version
@ r0: n
@ returns r0: n!
factorial:
CMP r0, #1 @ if (n <= 1) ...
BLS base_case @ ... return 1
PUSH {lr} @ save return address for this frame
PUSH {r0} @ save current n on stack (we'll need it after the recursive call)
SUB r0, r0, #1 @ r0 = n - 1 (argument for recursive call)
BL factorial @ r0 = factorial(n - 1)
POP {r1} @ r1 = saved n (restore caller's n)
MUL r0, r0, r1 @ r0 = factorial(n - 1) * n
POP {lr} @ restore return address
BX lr @ return with result in r0
base_case:
MOV r0, #1 @ factorial(n) = 1 for n <= 1
BX lr @ return
POP is used here because the function previously PUSHed registers that must be restored before returning; POP both restores those registers and fixes the stack pointer in one instruction.

## Slide 34: What is wrong?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0, r2, LSL #1]
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3 ; return result in r0
BX lr
ENDP

## Slide 35: What is wrong? ANS
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0, r2, LSL #1]
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3, LSL #16
MOV r0, r0, ASR #16 ; r0 = (short) r3
BX lr
ENDP
0x12345678
0x00005678
0x1234ABCD
0xFFFFABCD
int32_t x = 0x12345678;
int16_t y = (int16_t) x;
C function returns int16_t, but the assembly code puts the return in r0 as a 32-bit word, so that 16-bit value in r3 must be sign-extended to 32 bits before returning
  While r3 is 32 bits, the meaningful 16-bit result is in r3[15:0]
  r3[31:16] may contain carry-over bits and must be replaced by copies of the sign bit before returning.
  Casting an int32_t to int16_t keeps only the low 16 bits and produces 32-bit sign-extended result in r0 (e.g. with SXTH)
Notes: C function returns an int16_t, but the assembly returns the full 32-bit sum in r0. Caller will see a 32-bit value; the correct behavior when the C function is declared to return int16_t is to return the 16-bit value sign-extended to 32 bits.

## Slide 36: Explanations
These two lines sign-extend the lower 16 bits of r3 into a full 32-bit value in r0.
MOV r0, r3, LSL #16
  Shifts the value in r3 left by 16 bits.
  The lower 16 bits of r3 (the part we care about) move up into the upper 16 bits of r0.
  The bottom 16 bits of r0 become 0.
MOV r0, r0, ASR #16
  Shifts the value right by 16 bits, but preserves the sign (arithmetic shift).
  That means if bit 31 (the sign bit after the first shift) is 1, it fills with 1s; if 0, it fills with 0s.
  The result is a sign-extended 16-bit value from the original lower half of r3.
Examples:
r3 = 0x00001234
  LSL #16 → 0x12340000
  ASR #16 → 0x00001234
r3 = 0x0000ABCD
  LSL #16 → 0xABCD0000
  ASR #16 → 0xFFFFABCD
Can be replaced with a single instruction:
  SXTH r0, r3 ; r0 = (int16_t) r3, sign-extend
    Take the low 16 bits of r3, sign-extend them to 32 bits, and store the result in r0.