## Slide 1: Zonghua Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 4
ARM Arithmetic and Logic Instructions
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Signed Integer Representation Method 3: Two’s Complement
Expression | Result | Carry? | Overflow? | Correct Result?
0100 + 0010 | 0110 | No | No | Yes
0100 + 0110 | 1010 | No | Yes | No
1100 + 1110 | 1010 | Yes | No | Yes
1100 + 1010 | 0110 | Yes | Yes | No
Assume a four-bit system:

## Slide 3: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 4: Signed Comparison
 | N = 0 | N = 1
V = 0 | No overflow, implying the result is correct. The result is non-negative, Thus r0 – r1 ≥ 0, i.e., r0 ≥ r1 | No overflow, implying the result is correct. The result is negative. Thus r0 – r1 < 0, i.e., r0 < r1
V = 1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as non-negative and in fact it should be negative. Thus r0 – r1 < 0 in reality, i.e., r0 < r1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as negative and in fact it should be non-negative. Thus r0 – r1 ≥ 0 in reality., i.e. r0 ≥ r1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)
Notes: CMP a, b computes a - b and sets flags without keeping the result.
For unsigned subtraction, borrow happens when a < b. ARM encodes “no borrow” (a ≥ b) as C=1, and “borrow” (a < b) as C=0, while Z distinguishes equality.
  HI (unsigned higher >): the subtraction needs no borrow, so C=1, and it’s not equal, so Z=0.
  HS/CS (higher or same/carry set ≥) : no borrow → C=1; equality allowed.
  LO/CC (unsigned lower/carry clear <): subtraction borrows → C=0.
  LS (unsigned lower or same ≤): “lower or same” means either borrowed or equal → C=0 or Z=1.
For signed subtraction a - b, the sign bit N is correct if a ≥ b (no overflow, V = 0); the sign bit N is incorrect if a < b (overflow, V = 1).
  GE (signed greater or equal ≥): N == V. If there’s no overflow (V=0), non‑negative (N=0) means ≥; if there is overflow (V=1), N=1 (incorrect) also indicates the ≥ relation.
  LT (signed less than <): N != V. If there’s no overflow (V=0), negative (N=1) means <; if there is overflow (V=1), N=0 (incorrect) also indicates the < relation.
  GT (signed greater than >): N==V and Z=0. Strictly greater excludes equality, so combine GE with not equal.
  LE (signed less or equal ≤): N != V or Z=1. Either strictly less, or equal.

## Slide 5: Signed Comparison
 | N = 0 | N = 1
V = 0 | r0 ≥ r1 CMP returns 1 | r0 < r1 CMP returns 0
V = 1 | r0 < r1 CMP returns 0 | r0 ≥ r1 CMP returns 1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 6: Summary of Carry and Overflow Flags
6
Carry flag C = 1 upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Bit | Name | Meaning after add or sub
N | negative | result is negative
Z | zero | result is zero
V | overflow | signed overflow
C | carry | unsigned overflow
31
0
N
Z
C
V
CPSR (Current Program Status Register)
Review
Notes: C is cleared upon an unsigned subtract if the answer is wrong

## Slide 7: NZCV Flags in xPSR
N (negative) – set (1) when a signed result is negative, otherwise cleared (0).
Z (zero) – set (1) when a result is 0, otherwise cleared (0).
C (carry) – set (1) when an add-based operation produces an overflow, when a subtract-based operation doesn’t require a borrow; when shifting, holds the last bit that’s been shifted out; otherwise cleared (0).
V (overflow) – set (1) when an add- or subtract-based operation generates a signed overflow, otherwise cleared (0).
Review
Notes: https://eclecticlight.co/2021/06/23/code-in-arm-assembly-controlling-flow/
N (Negative): Copies the most significant bit of the last result; 1 means the result’s sign bit is 1, which for two’s‑complement indicates a negative value in signed interpretation.
Z (Zero): 1 if the result was exactly zero; otherwise 0.
C (Carry): For addition, 1 means an unsigned carry out; for subtraction (a − b or CMP), 1 means “no borrow,” and 0 means a borrow occurred. For shifts/rotates, it holds the last bit shifted out.
V (oVerflow): 1 when signed overflow occurred, i.e., the true signed result didn’t fit in the destination width (e.g., positive + positive → negative, or negative + negative → positive in 32‑bit two’s‑complement).
Why C=1 and Z=0 corresponds to “unsigned higher” (HI):
After a CMP a, b (which computes a − b for flags), C=1 means the subtraction needed no borrow, so a ≥ b in unsigned arithmetic; Z=0 rules out equality, leaving a > b. That composite condition is named HI.

## Slide 8: Example 1: Greatest Common Divider (GCD)
; suppose r0 = a and r1 = b
gcd CMP r0, r1 ; a > b?
BEQ end ; if a = b, done
BLO less ; a < b
SUB r0, r0, r1 ; a = a – b
B gcd
less SUB r1, r1, r0 ; b = b – a
B gcd
end
Euclid’s Algorithm
gcd CMP r0, r1
SUBHI r0, r0, r1
SUBLO r1, r1, r0
BNE gcd
uint32_t a, b;
while (a != b ) {
if (a > b)
a = a – b;
else
b = b – a;
}
CMP r0, r1 compares r0 and r1, setting Z=1 if r0 == r1, which is the termination condition when tested by BNE later.
SUBHI r0, r0, r1 executes only if the previous compare set HI (unsigned “higher”), i.e., r0 > r1 for unsigned ints r0 and r1. Flags C=1 and Z=0 (“no borrow” and “not equal”).
SUBLO r1, r1, r0 executes only if the previous compare of unsigned ints set LO (unsigned “lower”), i.e., r0 < r1 for unsigned ints r0 and r1. Flag C=0 (“borrow”).
BNE gcd branches back to the label if Z=0 from the CMP, i.e., while r0 != r1; when they become equal, Z=1 and the loop falls through, leaving r0 == r1 == gcd(a, b).

## Slide 9: GCD

## Slide 10: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a word at address 0x20000002.
  Word-address mod 4 = 0
  Can we store a word anywhere in memory?
  NO on most computers!
  A word can only be stored at an address that's divisible by 4.

## Slide 11: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a halfword at address 0x20000001.
  Can you store a halfword anywhere? NO.
  A halfword can only be stored at an address that's divisible by 2.
  Memory address of a halfword is the lowest address of its two bytes.
  Halfword-address mod 2 = 0

## Slide 12: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Typically, Barrel shifters are implemented as a cascade of parallel 2-to-1 multiplexers.

## Slide 13: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
Example: S1S0 = 00
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3

## Slide 14: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
Example: S1S0 = 01
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3

## Slide 15: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Example: S1S0 = 10

## Slide 16: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Example: S1S0 = 11

## Slide 17: ADR Pseudo-instruction
ADR: loads a program-relative or register-relative address into a register
start MOV r0,#10 ; 32-bit instruction
ADR r4,start ; 32-bit instruction
; => SUB r4,pc,#0xc

## Slide 18: 64-bit Logic Shift Left

## Slide 19: 64-bit Logic Shift Left
Example of Logic Shift Left by 3

## Slide 20: 64-bit Logic Shift Right

## Slide 21: 64-bit Logic Shift Right
Example of Logic Shift Right by 3

## Slide 22: ARM Register Conventions (APCS-Application Procedure Call Standard)
Reg. # | APCS Name | Role in Procedure Calls | Comments
r0 - r3 | a1 - a4 | First 4 arguments into a procedure / Scratch pad / Return result(s) from a function (not preserved across call) | Caller-saved registers - subprogram can use them as scratch registers, but it must also save any needed values before calling another subprogram.
r4 - r8 | v1 - v5 | Register Variables (preserved across call | Callee-saved registers - it can rely on an subprogram it calls not to change them (so a subprogram wishing to use these registers must save them on entry and restore them before it exits)
r9 – r12 | Omitted | Details omitted | Details omitted
r11 | fp | Frame pointer (if used) / Register Variable (preserved across call) | Callee-saved register - pointer to bottom of call-frame
r13 | sp | Stack pointer - points to the top of the stack | 
r14 | lr | Link register - holds the return address | Receives return address on BL call to procedure
r15 | pc | Program counter | 

## Slide 23: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Caller
MOVS r0, #5
MOVS r1, #6
MOVS r2, #7
MOVS r3, #8
PUSH {r0, r1, r2, r3}
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum
...
POP {r0, r1, r2, r3}
Old SP | <xxxxxxxx>
SP+12 | 0x00000008
SP+8 | 0x00000007
SP+4 | 0x00000006
SP | 0x00000005
Stack

## Slide 24: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Callee
sum PROC
EXPORT sum
PUSH {r5, r6, lr}
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r5,r6, [sp, #12] ; r5=mem[sp+12],r6=mem[sp+16]
ADD r0, r0, r5 ; add h
ADD r0, r0, r6 ; add i
LDRD r5,r6, [sp, #20] ; r5=mem[sp+20],r6=mem[sp+24]
ADD r0, r0, r5 ; add j
ADD r0, r0, r6 ; add k
POP {r5, r6, pc}
ENDP
Old SP | <xxxxxxxx>
SP+24 | 0x00000008
SP+20 | 0x00000007
SP+16 | 0x00000006
SP+12 | 0x00000005
SP+8 | lr
SP+4 | r6
SP | r5
Stack