## Slide 1: Z. Gu
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 5
Memory Access
Fall 2026
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Overview
How data is organized in memory?
  Big-Endian vs Little-Endian
How data is addressed?
  Register offset
    LDR r1, [r0, r3] ; offset = r3
    LDR r1, [r0, r3, LSL #2] ; offset = r3 * 4
  Immediate offset
    Pre-index: LDR r1, [r0, #4]
    Post-index: LDR r1, [r0], #4
    Pre-index with update: LDR r1, [r0, #4]!

## Slide 3: Logic View of Memory
By grouping bits together we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From software perspective, memory is an addressable array of bytes.
  The byte stored at the memory address 0x20000004 (hex, 4 bytes) is 0b10000100 (binary, 1 byte)
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
0b10000100
0x84
132
Binary
Hexadecimal
Decimal
Computer memory is byte-addressable!
Notes: By grouping bits together we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From software perspective, memory is an addressable array of bytes.
  The byte stored at the memory address 0x20000004 is 0b10000100
  A word can only be stored at an address that‘s divisible by 4 （Word-address mod 4 = 0, binary address ends with 00）
  Memory address of a word is the lowest address of all 4 bytes in that word.
  A halfword can only be stored at an address that‘s divisible by 2 （Halfword-address mod 2 = 0, binary address ends with 0）
  Memory address of a halfword is the lowest address of all 2 bytes in that halfword.

## Slide 4: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Architecturally aligned addresses are required for efficient access; unaligned access may require multiple cycles
  A word should be stored at an address that‘s divisible by 4 (Word-address mod 4 = 0, binary address ends with 00)
    Memory address of a word is the lowest address of all four bytes in that word.
    Two words at addresses: 0x20000000 and 0x20000004
  A halfword should be stored at an address that‘s divisible by 2 (Halfword-address mod 2 = 0, binary address ends with 0)
    Memory address of a halfword is the lowest address of all 2 bytes in that halfword.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
Notes: 32 bits = 4 bytes = 1 word = 2 halfwords
By grouping bits together we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From software perspective, memory is an addressable array of bytes.
  The byte stored at the memory address 0x20000004 is 0b10000100
  A word can only be stored at an address that‘s divisible by 4 （Word-address mod 4 = 0, binary address ends with 00）
  Memory address of a word is the lowest address of all 4 bytes in that word.
  A halfword can only be stored at an address that‘s divisible by 2 （Halfword-address mod 2 = 0, binary address ends with 0）
  Memory address of a halfword is the lowest address of all 2 bytes in that halfword.

## Slide 5: Logic View of Memory
Halfwords
  16 bits = 2 bytes = 1 halfword
  The right diagram has four halfwords at addresses of:
    0x20000000
    0x20000002
    0x20000004
    0x20000006
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits

## Slide 6: Data Alignment and Performance
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand.

## Slide 7: Quiz
Memory
What are their memory address offsets?
X[3]
X[2]
X[1]
X[0]
uint32_t X[4];
0x000F
0x000E
0x000D
0x000C
0x000B
0x000A
0x0009
0x0008
0x0007
0x0006
0x0005
0x0004
0x0003
0x0002
0x0001
0x0000
1 byte
Offset of bytes
Offset = ???
Offset = ???
Offset = ???
Offset = ???
Low
Address
High
Address

## Slide 8: Quiz ANS
What are their memory address offsets?
uint32_t X[4];
Offset = 12
Offset = 8
Offset = 4
Offset = 0
If the array starts at address pAddr = 0x0000,
Memory address of X[0] is pAddr = 0x0000
Memory address of X[1] is pAddr + 4 = 0x0004
Memory address of X[2] is pAddr + 8 = 0x0008
Memory address of X[3] is pAddr + 12 = 0x000C (12 in dec.)
Sequential words are at addresses incrementing by 4, since each array element of type uint32_t is 4 bytes (32 bits)
Memory
X[3]
X[2]
X[1]
X[0]
0x000F
0x000E
0x000D
0x000C
0x000B
0x000A
0x0009
0x0008
0x0007
0x0006
0x0005
0x0004
0x0003
0x0002
0x0001
0x0000
1 byte
Offset of bytes
Low
Address
High
Address

## Slide 9: Endianess
High address
Low address
Little-Endian
MSB
LSB
Big-Endian
LSB
MSB
LSB is at lower address
MSB is at lower address
byte 0
byte 1
byte 2
byte 3
Gulliver’s Travels (by Jonathan Swift, published in 1726):
Two religious sects of Lilliputians
The Little-Endians crack open their eggs from the little end
The Big-Endians break their eggs on the big end
High address
Low address
byte 3
byte 2
byte 1
byte 0

## Slide 10: Endianess
uint32_t a = 0x87654321
0x87
0x65
0x43
0x21
byte 3 byte 2 byte 1 byte 0
Little-Endian
0x21
0x43
0x65
0x87
High address
Low address
byte 0 byte 1 byte 2 byte 3
Big-Endian
0x87
0x65
0x43
0x21
High address
Low address
Endian: byte order, not bit order!
Reading from the top
Reading from the bottom
High address
Low address
Little-Endian
MSB
LSB
Big-Endian
LSB
MSB
LSB is at lower address
MSB is at lower address
byte 0
byte 1
byte 2
byte 3
High address
Low address
byte 3
byte 2
byte 1
byte 0

## Slide 11: Endianess
Little-Endian
  Least significant byte (LSB) is stored at lowest (least) address of a word
Big-Endian
  Most significant byte (MSB) is stored at lowest (least) address of a word
Regardless of endianness, the address of a word is defined as the lowest address of all bytes it occupies.
ARM is Little-Endian by default.
  It can be made Big-Endian by configuration.
Reading from
the top
Reading from
the bottom
Notes: Two possible byte orderings:
  Little-endian: the LSB (Least Significant Byte) is stored at the lowest address.
  Big-endian: the LSB (Least Significant Byte) is stored at the highest address.
  Intel processors use Little-Endian; ARM processors can be configured as either Little- or Big-endian; STM32 microcontrollers based on ARM Cortex-M3 use little-endian

## Slide 12: Endianness Example
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 FF 00
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 78 56 34 12
Little-Endian
  LSB is at lower address
Big-Endian
  MSB is at lower address
Memory Value
Offset (MSB) (LSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 00 FF
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 12 34 56 78
For uint8_t a and b, each with size of 1 Byte: No difference
Little-endian:
  For uint16_t c with size of 2 Bytes: LSB FF is at lower address and MSB 00 is at higher address
  For uint32_t d with size of 4 Bytes: LSB 78 is at lower address and MSB 12 is at higher address.
Big-endian:
  For uint16_t c with size of 2 Bytes: LSB FF is at higher address and MSB 00 is at lower address
  For uint32_t d with size of 4 Bytes: LSB 78 is at higher address and MSB 12 is at lower address.
Increasing mem. addr.
Increasing mem. addr.
Notes:   the LSB (Least Significant Byte) is stored at the lowest address.
  Big-endian: the LSB (Least Significant Byte) is stored at the highest address.
  Intel processors use Little-Endian; ARM processors can be configured as either Little- or Big-endian; STM32 microcontrollers based on ARM Cortex-M3 use little-endian

## Slide 13: Example
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
If Big-Endian is used, the word stored at address 0x20008000 is
If Little-Endian is used, the word stored at address 0x20008000 is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 14: Example
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
0xEE8C90A7
If Big-Endian is used, the word stored at address 0x20008000 is
If Little-Endian is used, the word stored at address 0x20008000 is
0xA7908CEE
Endianness specifies byte order, not bit order in a byte!
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 15: Load-Modify-Store
; Assume the memory address of x is stored in r1
LDR r0, [r1] ; load value of x from memory
ADD r0, r0, #1 ; x = x + 1
STR r0, [r1] ; store x into memory
x = x + 1;
C statement
Assume variable X resides in memory and is a 32-bit integer
Notes: Assume x is a 32-bit integer stored in the memory

## Slide 16: 3 Steps: Load, Modify, Store
ALU
Registers
Memory
Modify
Load
1
2
Store
3
x = x + 1;
Variable x resides in memory!
ALU cannot directly operate memory data!

## Slide 17: Load Instructions
LDR rt, [rs]
  Read from memory
  Mnemonic: LoaD to Register (LDR)
  rs specifies the memory address
  rt holds the 32-bit value fetched from memory
  For Example:
; Assume r0 = 0x08200004
; Load a word:
LDR r1, [r0] ; r1 = Memory.word[0x08200004]

## Slide 18: Store Instructions
STR rt, [rs]
  Write into memory
  Mnemonic: STore from Register (STR)
  rs specifies memory address
  Save the content of rt into memory
  For Example:
; Assume r0 = 0x08200004
; Store a word
STR r1, [r0] ; Memory.word[0x08200004] = r1

## Slide 19: Load/Store a Byte, Halfword, Word
LDR | Load Word | uint32_t/int32_t | unsigned or signed int
LDRB | Load Byte | uint8_t | unsigned char
LDRH | Load Halfword | uint16_t | unsigned short int
LDRSB | Load Signed Byte | int8_t | signed char
LDRSH | Load Signed Halfword | int16_t | signed short int
STR | Store Word | uint32_t/int32_t | unsigned or signed int
STRB | Store Lower Byte | uint8_t/int8_t | unsigned or signed char
STRH | Store Lower Halfword | uint16_t/int16_t | unsigned or signed short
LDRxxx R0, [R1]
; Load data from memory into a 32-bit register
STRxxx R0, [R1]
; Store data extracted from a 32-bit register into memory

## Slide 20: Load a Byte, Half-word, Word (Little-Endian)
0x87
0x02000003
0x02000002
0x02000001
0x02000000
0xE1
0xE3
0x65
LDRB r1, [r0]
Load a Byte
0x00
0x00
0x00
0xE1
0
31
LDRH r1, [r0]
Load a Halfword
0x00
0x00
0xE3
0xE1
0
31
LDR r1, [r0]
Load a Word
0x87
0x65
0xE3
0xE1
0
31
Little-Endian
Assume
r0 = 0x02000000
LDRH "Load Register Halfword“: it loads a 16-bit halfword value from the memory address pointed to by register r0 into register r1. The loaded 16-bit value is zero-extended to fill the 32-bit register r1. This means the upper 16 bits of r1 will be set to zero regardless of the halfword data.
LDRB "Load Register Byte“: it loads 8-bit byte value from the memory address pointed to by register r0 into register r1, and zero-extends it.

## Slide 21: Sign Extension (Little-Endian)
0x87
0x20000003
0x20000002
0x20000001
0x20000000
0xE1
0xE3
0x65
LDRSB r1, [r0]
Load a Signed Byte
0xFF
0xFF
0xFF
0xE1
0
31
LDRSH r1, [r0]
Load a Signed Halfword
0xFF
0xFF
0xE3
0xE1
0
31
Little-Endian
LDRSH "Load Register Signed Halfword“
LDRSB "Load Register Signed Byte“
Similar to LDRH and LDRB, except each sign-extends the value to fill the 32-bit register, not zero-extend. Facilitate subsequent 32-bit signed arithmetic.
Assume
r0 = 0x20000000
Notes: different from LDRH, which loads a halfword as unsigned and fills the upper bits with zeros, regardless of sign

## Slide 22: Address Modes: Offset in Register
Address accessed by LDR/STR is specified by a base register plus an offset
Offset can be held in a register
  LDR r0,[r1,r2]
  Base memory address held in register r1
  Offset held in r2
  Target address = r1 + r2
  LDR r0,[r1,r2,LSL #2]
  Base memory address held in register r1
  Offset = r2, LSL #2
  Target address = r1 + r2 * 4

## Slide 23: Address Modes: Immediate Offset
Address accessed by LDR/STR is specified by a base register plus an offset
Offset can be an immediate value
LDR r0,[r1,#8]
  Base memory address held in register r1
  Offset is an immediate value
  Target address = r1 + 8
Three modes for immediate offset:
  Pre-index,
  Post-index,
  Pre-index with Update

## Slide 24: Addressing Mode: Pre-index vs Post-index
Pre-index
LDR r1, [r0, Offset]
Post-index
LDR r1, [r0], Offset
Pre-index with Update
LDR r1, [r0, Offset]!
Mode | Address used for Load | Base register update | Example (r0=0x100)
Pre-index LDR r1, [r0, #4] | r0 + offset (0x104) | No | r1 = data[0x104]; r0 = 0x100
Post-index LDR r1, [r0], #4 | r0 (0x100) | Yes, after load | r1 = data[0x100]; r0 = 0x104
Pre-index w/ Update LDR r1, [r0, #4]! | r0 + offset (0x104) | Yes, before load | r1 = data[0x104]; r0 = 0x104
The table assumes r0 = 0x100, offset = 4 bytes (#4)

## Slide 25: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
Calculates address by adding the offset (here, #4) to the base register (r0) before the load. Loads data from the resulting address r0+4 into r1. The base register (r0) is not updated.
Example: instruction accesses memory at r0 + 4 = 0x20008004, but r0 remains to be 0x20008000 after execution.

## Slide 26: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
0x20008000
0x88796A5B
r1
r0
offset=4
r0 + offset
0x20008004
Assume Little-Endian
r0 remains the same after reading memory

## Slide 27: Accessing an Array
Pre-index
uint32_t array[10];
array[0] += 5;
array[1] += 5;
C code
LDR r1, [r0] ; Read array[0]
ADD r1, r1, #5
STR r1, [r0] ; Write to array[0]
LDR r1, [r0, #4] ; Read array[1]
ADD r1, r1, #5
STR r1, [r0, #4] ; Write to array[1]
Assume the memory address of the array starts at 0x20008000.
Assume r0 = 0x20008000.

## Slide 28: Post-index
Post-Index: LDR r1, [r0], #4
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
Loads data from the address currently in r0 into r1. After the load, updates the base register (r0) by adding the offset (#4).
Example: instruction accesses memory at r0 = 0x20008000, then increments r0 by the offset of 4 to r0 + 4 = 0x20008004 after execution.

## Slide 29: Post-index
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008004
0x4C3D2E1F
r1
r0
Assume Little-Endian
r0 = r0 + offset
Increment r0 by offset
after reading memory
Post-Index: LDR r1, [r0], #4
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 30: Pre-index with Update
Pre-Index with Update: LDR r1, [r0, #4]!
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
First, adds the offset (#4) to the base register (r0), then loads from this updated address r0 + 4. Base register r0 is set to r0 + 4 afterwards.
Example: instruction accesses memory at r0 + 4 = 0x20008004, and also sets r0 to 0x20008004 after execution.
Notes: First, adds the offset (#4) to the base register (r0), then loads from this updated address.
Updates the base register: r0 is set to r0 + 4 after execution.
Example:
  If r0 = 0x100, instruction accesses memory at 0x104 and also sets r0 to 0x104 afterward.

## Slide 31: Pre-index with Update
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008004
0x88796A5B
r1
r0
0x20008004
Assume Little-Endian
Pre-Index with Update: LDR r1, [r0, #4]!
Offset: range is -255 to +255
Assume: r0 = 0x20008000
Increment r0 by offset
before reading memory
r0 = r0 + offset

## Slide 32: Summary of Pre-index and Post-index
Index Format | Example | Equivalent
Pre-index | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Post-index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4
Pre-index with update | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Pre-index: use (base + offset), don’t change base Post-index: use base, then change base Pre-index with update: change base, then use it
For the pre-/post-indexed (writeback) forms in the Cortex‑M/Thumb‑2 instruction set (and for halfword and signed byte/halfword load/store in A32), the offset is an unsigned 8‑bit immediate 0–255, and the U bit selects addition or subtraction, yielding an effective signed range of [−255, +255] around the base register.
In ARM (A32) instruction set, for word and unsigned byte LDR/STR, the immediate has an effective signed range of [−4095, +4095]
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 33: Example (Little-Endian ordering)
LDRH r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 34: Example ANS (Little-Endian ordering)
LDRH r1, [r0]
; r0 = 0x20008000
r1 before load (r1 is
Overwritten by LDR)
0x12345678
r1 after load
0x0000CDEF
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 35: Example (Endianness does not matter for single byte)
LDRSB r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 36: Example ANS (Endianness does not matter for single byte)
LDRSB r1, [r0]
; r0 = 0x20008000
0x12345678
r1 after load
0xFFFFFFEF
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
r1 before load (r1 is
Overwritten by LDR)
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 37: Example (Little-Endian ordering)
STR r1, [r0, #4]
; r0 = 0x20008000, r1=0x76543210
r0 before the store
0x20008000
r0 after the store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 38: Example ANS (Little-Endian ordering)
STR r1, [r0, #4]
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008000
Memory Address | Memory Data
0x20008007 | 0x76
0x20008006 | 0x54
0x20008005 | 0x32
0x20008004 | 0x10
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 39: Example (Little-Endian ordering)
STR r1, [r0], #4
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0

## Slide 40: Example ANS (Little-Endian ordering)
STR r1, [r0], #4
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008004
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x76
0x20008002 | 0x54
0x20008001 | 0x32
0x20008000 | 0x10
r0
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 41: Example (Little-Endian ordering)
STR r1, [r0, #4]!
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 42: Example ANS (Little-Endian ordering)
STR r1, [r0, #4]!
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008004
Memory Address | Memory Data
0x20008007 | 0x76
0x20008006 | 0x54
0x20008005 | 0x32
0x20008004 | 0x10
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 43: Addressing Modes for Load/Store Multiple Registers
STMxx rn{!}, {register_list}
LDMxx rn{!}, {register_list}
xx = IA or DB (IB, DA: A32 only)
Addressing Modes | Description | Instructions
IA | Increment After | STMIA, LDMIA
IB (A32 only) | Increment Before | STMIB, LDMIB
DA (A32 only) | Decrement After | STMDA, LDMDA
DB | Decrement Before | STMDB, LDMDB
IA: address is incremented by 4 after a word is loaded or stored.
IB: address is incremented by 4 before a word is loaded or stored. (A32 only)
DA: address is decremented by 4 after a word is loaded or stored. (A32 only)
DB: address is decremented by 4 before a word is loaded or stored.
A32 only: IB and DA modes (STMIB/LDMIB, STMDA/LDMDA). Cortex-M (Thumb-2) supports only IA and DB.

## Slide 44: Load/Store Multiple Registers
The following are synonyms.
  STM = STMIA (Increment After) = STMEA (Empty Ascending)
  LDM = LDMIA (Increment After) = LDMFD (Full Descending)
  Two independent switches:
    Increment or decrement?
    Before or after?
The order in which registers are listed does not matter
  For STM/LDM, the lowest-numbered register is stored/loaded at the lowest memory address.
A32 only: IB and DA modes (STMIB/LDMIB, STMDA/LDMDA). Cortex-M (Thumb-2) supports only IA and DB.
Notes: FD = Full Descending
  STMFD/LDMFD = STMDB/LDMIA
ED = Empty Descending (A32 only)
  STMED/LDMED = STMDA/LDMIB (A32 only)
FA = Full Ascending (A32 only)
  STMFA/LDMFA = STMIB/LDMDA (A32 only)
EA = Empty Ascending
  STMEA/LDMEA = STMIA/LDMDB
IB and DA exist only in ARM (A32) state. Cortex-M (Thumb-2) supports only IA and DB, i.e. FD (STMDB/LDMIA = PUSH/POP) and EA (STMIA/LDMDB) stacks.

## Slide 45: Store Multiple Registers
A32 only: IB and DA modes (STMIB/LDMIB, STMDA/LDMDA). Cortex-M (Thumb-2) supports only IA and DB.

## Slide 46: Load Multiple Registers
A32 only: IB and DA modes (STMIB/LDMIB, STMDA/LDMDA). Cortex-M (Thumb-2) supports only IA and DB.

## Slide 47: Cortex-M3 & Cortex-M4 Memory Map
32-bit Memory Address
232 bytes of memory space (4 GB)
Harvard architecture: physically separated instruction memory and data memory
Van Neumann architecture: unified instruction and data memory
Code
SRAM
Peripheral
External RAM
External Device
Vendor Specific
External Peripheral Bus
Internal Peripheral Bus
0x00000000
0x20000000
0x40000000
0x60000000
0xA0000000
0xE0040000
0xE0000000
0xE0100000
0xFFFFFFFF
0.5GB
1GB
1GB
0.5GB
0.5GB
0.5GB

## Slide 48
Cortex-M3 Fixed Memory Map

## Slide 49
Cortex-M4 Fixed Memory Map

## Slide 50: Pseudo-instructions
Pseudo instruction: available to use in an assembly program, but not directly supported by hardware.
Pseudo → not real
Compilers translate it to one or multiple actual machine instructions
Pseudo instructions are provided for the convenience of programmers.

## Slide 51: LDR Pseudo-instruction
LDR Rt, =expr
LDR Rt, =label
If the value of expr can be loaded with MOV, MVN (16-bit instruction) or MOVW (32-bit instruction), the assembler uses that instruction.
  MOV supports all 8-bit immediate numbers ranging in [0, 255]. For numbers out of this range, some patterns can be encoded.
If a valid MOV, MVN, MOVW instruction cannot be used (due to out of range), or if the label_expr syntax is used, the assembler places the constant in a literal pool and generates a PC-relative LDR instruction that reads the constant from the literal pool.
LDR r1,=0xFF0 ; loads 0xFF0 into R1
; => MOV r1,#0xFF0
LDR r2,=0xFFF ; loads 0xFFF into R2
; => MOVW r2, #0xFFF
LDR r3,=array ; loads the address of array into R3
; => LDR r3,[pc, offset_to_litpool]
; ...
; litpool DCD array
Software uses this pseudo instruction to set a register to some value without worrying about the size of the value.
Notes: MOV supports all 8-bit immediate numbers
Range of 8-bit immediate number: 0 – 255
Numbers out of this range but with some patterns can be encoded. Refer to the Slide Summary of Pre-index and Post-index

## Slide 52: Summary
Memory address is always in terms of bytes.
How data is organized in memory?
How data is addressed?
Addressing Format | Example | Equivalent
Pre-index | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Pre-index with update | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Post-Index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4

## Slide 53: References
Lecture 22. Big-Endian and Little-Endian
  https://www.youtube.com/watch?v=T1C9Kj_78ek&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=22
Lecture 23. Load and Store Instructions
  https://www.youtube.com/watch?v=CtfV3HsHwk4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=23
Lecture 24. Addressing mode: pre-index, post-index, and pre-index with update
  https://www.youtube.com/watch?v=zgkxPdPkxa8&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=24
ARM Instruction Set - Stack Instructions STMFD, STMFA , STMED, STMEA, Vishal Gaikwad (STMFA and STMED: A32 only)
  https://www.youtube.com/watch?v=H4xoaOlNSJo