## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 2
Data Representation

## Slide 2: Bit, Byte, Half-word, Word, Double-Word

## Slide 3: Binary, Octal, Decimal and Hex
Decimal | Binary | Octal | Hex
0 | 0000 | 00 | 0x0
1 | 0001 | 01 | 0x1
2 | 0010 | 02 | 0x2
3 | 0011 | 03 | 0x3
4 | 0100 | 04 | 0x4
5 | 0101 | 05 | 0x5
6 | 0110 | 06 | 0x6
7 | 0111 | 07 | 0x7
8 | 1000 | 010 | 0x8
9 | 1001 | 011 | 0x9
10 | 1010 | 012 | 0xA
11 | 1011 | 013 | 0xB
12 | 1100 | 014 | 0xC
13 | 1101 | 015 | 0xD
14 | 1110 | 016 | 0xE
15 | 1111 | 017 | 0xF
0x: Hex
0: Octal

## Slide 4: Magic 32-bit Numbers
Used as a special pattern for debug
Used as a special pattern of memory values during allocation and de-allocation
0xDEADBEEF | Dead Beef
0xBADDCAFE | Bad Cafe
0xFEE1DEAD | Feel Dead
0x8BADF00D | Ate Bad Food
0xBAADF00D | Bad Food
0xDEADC0DE | Dead Code
0xFACEB00C | Facebook
0xDEADD00D | Dead Dude

## Slide 5: Unsigned Integers
Convert from Binary to Decimal:
Five-bit binary integers

## Slide 6: Range of Unsigned Integers
Storage Size | Range | Powers of 2
Unsigned Byte | 0 to 255 | 0 to 28-1
Unsigned Halfword | 0 to 65,535 | 0 to 216-1
Unsigned Word | 0 to 4,294,967,295 | 0 to 232-1
Unsigned Double-word | 0 to 18,446,744,073,709,551,615 | 0 to 264-1

## Slide 7: Unsigned Integers
Convert Decimal to Binary
5210 = 1101002
Example 1
3210 = 1000002
Example 2

## Slide 8: Carry/borrow flag bit for unsigned numbers
Given unsigned integers and
  Carry happens if c is too big to fit in n bits (i.e., ).
  Borrow happens if .
On ARM Cortex-M processors, the carry flag and the borrow flag are physically the same flag bit in the status register.
  For an unsigned subtraction, Carry = NOT Borrow

## Slide 9: Carry/borrow flag bit for unsigned numbers
A carry occurs when adding 28 and 6
If the traverse crosses the boundary between 0 and , the carry flag is set on addition and is cleared on subtraction.
Carry flag = 1, indicating carry has occurred on unsigned addition.
Carry flag is 1 because the result crosses the boundary between 31 and 0.
Notes: For unsigned numbers, the carry flag is set when adding two numbers and the result is larger than the maximum that can represented. For subtraction, the borrow bit is set when the result is positive, representing no borrowing occurs. The borrow bit is cleared when the result is negative. On the ARM processor, the carry bit and borrow bit are the same flag bit in the status register.

## Slide 10: Carry/borrow flag bit for unsigned numbers
A borrow occurs when subtracting 5 from 3.
If the traverse crosses the boundary between 0 and , the carry flag is set on addition and is cleared on subtraction.
Carry flag = 0, indicating borrow has occurred on unsigned subtraction.
For subtraction, carry = NOT borrow.
Notes: For unsigned numbers, the carry flag is set when adding two numbers and the result is larger than the maximum that can represented. For subtraction, the borrow bit is set when the result is positive, representing no borrowing occurs. The borrow bit is cleared when the result is negative. On the ARM processor, the carry bit and borrow bit are the same flag bit in the status register.

## Slide 11: Signed Integer Representation
Three ways to represent signed binary integers:
  Signed magnitude
  One’s complement ()
  Two’s complement ()
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero | Two zeroes () | Two zeroes () | One zero
Unique Numbers |  |  | 
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero |  |  | One zero
Unique Numbers |  |  | 

## Slide 12: Signed Integers Method 1: Signed Magnitude
Example: in a 5-bit system
  +710 = 001112
  -710 = 101112
Two ways to represent zero
  +010 = 000002
  -010 = 100002
Not used in modern systems
  Hardware complexity
  Two zeros
Sign-and-Magnitude:
The most significant bit is the sign.
The rest bits are magnitude.

## Slide 13: Signed Integers Method 2: One’s Complement
One’s Complement ():
Example: in a 5-bit system
  +710 = 001112
  -710 = 110002
The one's complement representation of a negative binary number is the bitwise NOT of its positive counterpart.
  +710 + (-710) = 001112 + 110002
  = 111112
  = 25 - 1

## Slide 14: Signed Integers Method 3: Two’s Complement (TC)
Two’s Complement ():
TC of a negative number can be obtained by the bitwise NOT of its positive counterpart plus one.
 | Binary | Decimal
Original number | 0b00011 | 3
Step 1: Invert every bit | 0b11100 | 
Step 2: Add 1 | + 0b00001 | 
Two’s complement | 0b11101 | -3
Example 1: TC(3)

## Slide 15: Signed Integers Method 3: Two’s Complement (TC)
Two’s Complement (TC)
TC of a negative number can be obtained by the bitwise NOT of its positive counterpart plus one.
Example 2: TC(-3)
 | Binary | Decimal
Original number | 0b11101 | -3
Step 1: Invert every bit | 0b00010 | 
Step 2: Add 1 | + 0b00001 | 
Two’s complement | 0b00011 | 3

## Slide 16: Comparison
One’s complement representation
Negative = invert all bits of a positive
Two’s Complement representation
TC = invert all bits, then plus 1
Signed magnitude representation
0 = positive
1 = negative
Used in modern computers!

## Slide 17: Range of Signed Integers (Two’s Complement)
Storage Size | Range | Powers of 2
Signed Byte | -128 to +127 | -27 to 27-1
Signed Halfword | -32,768 to +32,767 | -215 to 215-1
Signed Word | -2,147,483,648 to +2,147,483,647 | -231 to 231-1
Signed Double-word | -9,223,372,036,854,775,808 to +9,223,372,036,854,775,807 | -263 to 263-1

## Slide 18: Overflow for Signed Add/Sub
When adding signed numbers represented in two’s complement, overflow occurs only in two scenarios:
  adding two positive numbers but getting a non-positive result, or
  adding two negative numbers but yielding a non-negative result.
Similarly, when subtracting signed numbers, overflow occurs in two scenarios:
  subtracting a positive number from a negative number but getting a positive result, or
  subtracting a negative number from a positive number but producing a negative result.
Overflow cannot occur when adding operands with different signs or when subtracting operands with the same signs.

## Slide 19: Overflow for Signed Add
Overflow occurs when adding two positive integers but getting a negative result.
On addition, overflow occurs if when adding two positives.
Overflow never occurs when adding two numbers with different signs.
Notes: For signed numbers represented in two’s complement, an overflow occurs only in two scenarios:
Add two positive numbers and get a negative result
Add two negative numbers and get a positive result

## Slide 20: Overflow for Signed Add
Overflow occurs when adding two negative integers but getting a positive result.
On addition, overflow occurs if when adding two negatives.
Notes: For signed numbers represented in two’s complement, an overflow occurs only in two scenarios:
Add two positive numbers and get a negative result
Add two negative numbers and get a positive result

## Slide 21: Signed or Unsigned
  CPU does not know the answer at all.
  Therefore, the hardware sets up both the carry flag and the overflow flag.
  It is software’s (programmers’/compilers’) responsibility to interpret the flags.
a = 0b10000
b = 0b10000
c = a + b
Are a and b signed or unsigned numbers?

## Slide 22: Signed or unsigned
Whether the carry flag or the overflow flag should be used depends on the programmer’s intention.
When programming in high-level languages such as C, the compiler automatically chooses to use the carry or overflow flag based on how this integer is declared in source code (“int” or “unsigned int”).

## Slide 23: Signed or Unsigned
uint a;
uint b;
…
c = a + b
…
C Program
Check the carry flag!
a = 0b10000
b = 0b10000
c = a + b
Are a and b signed or unsigned numbers?

## Slide 24: Signed or Unsigned
int a;
int b;
…
c = a + b
…
C Program
Check the overflow flag!
a = 0b10000
b = 0b10000
c = a + b
Are a and b signed or unsigned numbers?

## Slide 25: Signed Integer Representation Method 3: Two’s Complement
Expression | Result | Carry? | Overflow? | Correct Result?
0100 + 0010 | 0110 |  |  | 
0100 + 0110 | 1010 |  |  | 
1100 + 1110 | 1010 |  |  | 
1100 + 1010 | 0110 |  |  | 
Assume a four-bit system:

## Slide 26: Signed Integer Representation Method 3: Two’s Complement
Expression | Result | Carry? | Overflow? | Correct Result?
0100 + 0010 | 0110 | No | No | Yes
0100 + 0110 | 1010 | No | Yes | No
1100 + 1110 | 1010 | Yes | No | Yes
1100 + 1010 | 0110 | Yes | Yes | No
Assume a four-bit system:

## Slide 27: Why use Two’s Complement
Operation | Are signed and unsigned operations the same?
Addition | Yes
Subtraction | Yes
Multiplication | Yes if the product is required to keep the same number of bits as operands
Division | No
Two’s complement simplifies hardware
Notes: Why do we use two’s complement? {{Pause=0.5}} One of the advantages is that two’s complement can simplify the hardware implementation of arithmetic functions. If signed integers are represented in two’s complement, the hardware can ignore the sign of operands for addition or subtraction. If the product is required to keep the same number of bits as operands, the multiplication hardware can also ignore the sign of operands. This property of two’s complement simplifies the hardware design for addition, subtraction and multiplication. Note that this property does not hold true for division.

## Slide 28: Adding two signed integers: (-9) + 6
-9
6
-3
01001
10110
10111
flip
+1
9
-9
00010
00011
flip
+1
3
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1
Simple Hardware Adder
23
6
29
+
Two’s Complement Counterpart
Notes: {{Pause=1}} We will use a very simple example to show that, the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers. {{Pause=0.5}}
Suppose we are adding negative nine and six. {{Pause=0.5}} These two signed numbers are represented in two’s complement in computers. {{Pause=0.5}}
Specifically, we can obtain the two’s complement representation of negative nine by flipping all bits and adding one. {{Pause=0.5}} The two’s complement of a positive number is itself. {{Pause=0.5}}
Let’s see what will happen if the hardware treats these two inputs as unsigned numbers. If these binary bits represent unsigned numbers, they are 23 and 6, respectively. Therefore, the hardware adds 23 and 6, and produces 29, in decimal, {{Pause=0.3}} or one, one, one, zero, one, in binary. {{Pause=0.5}}
If the output represents a signed integer in two’s complement, it actually represents negative 3. This can be proved by inverting all the bits and adding one. The result, negative three, is exactly the sum of the original signed inputs. {{Pause=0.5}}
This example shows that, without any modification, the hardware adder designed for adding unsigned numbers, works correctly for adding signed numbers.

## Slide 29: Subtracting two signed integers: (-9) - 6
-9
6
-15
01001
10110
10111
flip
+1
9
-9
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
Simple Hardware Subtractor
23
6
17
-
01111
10000
10001
flip
+1
15
-15
1 | 0 | 0 | 0 | 1
Notes: {{Pause=1}} Similarly, the same subtraction hardware works correctly for both signed and unsigned subtraction, even though the sign of input operands is not examined. {{Pause=0.3}} This example subtracts 6 from negative 9. The hardware ignores the sign of the inputs, and subtracts 6 from 23. The result is 17, in decimal, {{Pause=0.3}} or one, zero, zero, zero, one, in binary. If the result represents a signed integer in two’s complement, then the result is negative 15. This is exactly the result of subtracting the original signed integers.

## Slide 30: Two’s Complement Simplifies Hardware Implementation
In two’s complement, the same hardware works correctly for both signed and unsigned addition/subtraction.
If the product is required to keep the same number of bits as operands, unsigned multiplication hardware works correctly for signed numbers.
However, this is not true for division.

## Slide 31: Condition Codes
31
C is set upon an unsigned addition if the answer is wrong
C is cleared upon an unsigned subtract if the answer is wrong
V is set upon a signed addition or subtraction if the answer is wrong
Why do we care about these bits?
Bit | Name | Meaning after add or sub
N | negative | result is negative
Z | zero | result is zero
V | overflow | signed arithmetic out of range
C | carry | signed arithmetic out of range

## Slide 32: Carry and Overflow
 | Carry (for unsigned) | Overflow (for signed)
Add | if is too large to fit in. | if is too large or too small to fit in
Subtract | , i.e. if . | 
 | Carry (for unsigned) | Overflow (for signed)
Add |  | 
Subtract |  | 
ARM Cortex-M has no dedicated borrow flag, carry flag is reused.
For unsigned subtract,
Signed Subtraction is converted to sign addition

## Slide 33: Formal Representation for Addition
R = X + Y
When adding two 32-bit integers X and Y, the flags are
N = R31
Z is set if R is zero.
C is set if the result is incorrect for an unsigned addition
V is set if the result is incorrect for a signed addition.

## Slide 34: Formal Representation for Subtraction
R = X - Y
When subtracting two 32-bit integers X and Y, the flags are
N = R31
Z is set if R is zero.
C is clear if the result is incorrect for an unsigned subtraction
V is set if the result is incorrect for an signed subtraction.

## Slide 35: Characters
Dec | Hex | Char | Dec | Hex | Char | Dec | Hex | Char | Dec | Hex | Char
0 | 00 | NUL | 32 | 20 | SP | 64 | 40 | @ | 96 | 60 | ‘
1 | 01 | SOH | 33 | 21 | ! | 65 | 41 | A | 97 | 61 | a
2 | 02 | STX | 34 | 22 | " | 66 | 42 | B | 98 | 62 | b
3 | 03 | ETX | 35 | 23 | # | 67 | 43 | C | 99 | 63 | c
4 | 04 | EOT | 36 | 24 | $ | 68 | 44 | D | 100 | 64 | d
5 | 05 | ENQ | 37 | 25 | % | 69 | 45 | E | 101 | 65 | e
6 | 06 | ACK | 38 | 26 | & | 70 | 46 | F | 102 | 66 | f
7 | 07 | BEL | 39 | 27 | ’ | 71 | 47 | G | 103 | 67 | g
8 | 08 | BS | 40 | 28 | ( | 72 | 48 | H | 104 | 68 | h
9 | 09 | HT | 41 | 29 | ) | 73 | 49 | I | 105 | 69 | i
10 | 0A | LF | 42 | 2A | * | 74 | 4A | J | 106 | 6A | j
11 | 0B | VT | 43 | 2B | + | 75 | 4B | K | 107 | 6B | k
12 | 0C | FF | 44 | 2C | , | 76 | 4C | L | 108 | 6C | l
13 | 0D | CR | 45 | 2D | - | 77 | 4D | M | 109 | 6D | m
14 | 0E | SO | 46 | 2E | . | 78 | 4E | N | 110 | 6E | n
15 | 0F | SI | 47 | 2F | / | 79 | 4F | O | 111 | 6F | o
16 | 10 | DLE | 48 | 30 | 0 | 80 | 50 | P | 112 | 70 | p
17 | 11 | DC1 | 49 | 31 | 1 | 81 | 51 | Q | 113 | 71 | q
18 | 12 | DC2 | 50 | 32 | 2 | 82 | 52 | R | 114 | 72 | r
19 | 13 | DC3 | 51 | 33 | 3 | 83 | 53 | S | 115 | 73 | s
20 | 14 | DC4 | 52 | 34 | 4 | 84 | 54 | T | 116 | 74 | t
21 | 15 | NAK | 53 | 35 | 5 | 85 | 55 | U | 117 | 75 | u
22 | 16 | SYN | 54 | 36 | 6 | 86 | 56 | V | 118 | 76 | v
23 | 17 | ETB | 55 | 37 | 7 | 87 | 57 | W | 119 | 77 | w
24 | 18 | CAN | 56 | 38 | 8 | 88 | 58 | X | 120 | 78 | x
25 | 19 | EM | 57 | 39 | 9 | 89 | 59 | Y | 121 | 79 | y
26 | 1A | SUB | 58 | 3A | : | 90 | 5A | Z | 122 | 7A | z
27 | 1B | ESC | 59 | 3B | ; | 91 | 5B | [ | 123 | 7B | {
28 | 1C | FS | 60 | 3C | < | 92 | 5C | \ | 124 | 7C | ¦
29 | 1D | GS | 61 | 3D | = | 93 | 5D | ] | 125 | 7D | }
30 | 1E | RS | 62 | 3E | > | 94 | 5E | ^ | 126 | 7E | ~
31 | 1F | US | 63 | 3F | ? | 95 | 5F | _ | 127 | 7F | DEL
American
Standard
Code for
Information
Interchange
Standard ASCII: Encoding 128 characters
Standard ASCII
  0 - 127
Extended ASCII
0 - 255
ANSI
0 - 255
Unicode
0 - 65535

## Slide 36: Null-terminated String
Memory Address | Memory Content | Letter
str + 12  | 0x00 | \0
str + 11  | 0x79 | y
str + 10  | 0x6C | l
str + 9  | 0x62 | b
str + 8  | 0x6D | m
str + 7  | 0x65 | e
str + 6  | 0x73 | s
str + 5  | 0x73 | s
str + 4  | 0x41 | A
str + 3  | 0x20 | space
str + 2  | 0x4D | M
str + 1  | 0x52 | R
str  | 0x41 | A
char str[13] = “ARM Assembly”; // The length has to be at least // 13 even though it has 12 // letters. The NULL terminator // should be included. or simply char str[] = “ARM Assembly”;

## Slide 37: String Comparison
Strings are compared based on their ASCII values
“j” < “jar” < “jargon” < “jargonize”
“CAT” < “Cat” < “DOG” < “Dog” < “cat” < “dog”
“12” < “123” < “2”< “AB” < “Ab” < “ab” < “abc”

## Slide 38: String Length
Array subscript operator [ ]
int strlen (char *pStr){ int i = 0; // loop until pStr[i] is NULL while( pStr[i] ) i++; return i; }
Pointer dereference operator *
int strlen (char *pStr){ int i = 0; // loop until *pStr is NULL while( *pStr ) { i++; pStr++; } return i; }
Stings are terminated with a null character (NUL, ASCII value 0x00)

## Slide 39: Convert to Upper Case
Pointer dereference operator *
void toUpper(char *pStr){ char *p; for(*p = pStr; *p; ++p){ if(*p >= ’a’ && *p <= ’z’) *p -= ‘a’ – ‘A’; //or: *p -= 32; } }
Array subscript operator [ ]
void toUpper(char *pStr){ int i; char c = pStr[0]; for(i = 0; c; i++, c = pStr[i];) { if(c >= ’a’ && c <= ’z’) pStr[i] -= ‘a’ – ‘A’; // or: pStr[i] -= 32; } }
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 4A | 4B | 4C | 4D | 4E | 4F | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 5A
a | b | c | d | e | f | g | h | i | j | k | l | m | n | o | p | q | r | s | t | u | v | w | x | y | z
61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 6A | 6B | 6C | 6D | 6E | 6F | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 7A
‘a’ – ‘A’ = 0x61 – 0x41 = 0x20 = 32