## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Passing Parameters to Subroutines via Registers

## Slide 2: Overview
How to call a subroutine?
How to return the control back to the caller?
How to pass arguments into a subroutine?
How to return a value in a subroutine?
How to preserve the running environment for the caller?

## Slide 3: Link Register (LR)
Link Register (LR) holds the return address of a subroutine
The processor copies LR to PC after the program is finished.
Link Register
Register Bank
Special Registers

## Slide 4: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller

## Slide 5: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller
Transfer control to callee
Resume suspended caller
PROC and ENDP are assembler directives, not instructions..
PROC declares a procedure (subroutine) symbol.
ENDP marks the end of that procedure.

## Slide 6: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
r0 | 
r1 | 
r2 | 
r3 | 
. . . | . . .
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Registers
32 bits
Notes: Suppose PC current represents the memory address of the Branch and Link instruction BL. Since the BL instruction takes four bytes in memory, the memory of the next instruction immediately after BL is PC current plus 4.

## Slide 7: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
r0 | 
r1 | 
r2 | 
r3 | 
. . . | . . .
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Registers
32 bits
0x08000214
0x08000210
0x08000214
0x08000280
0x08000280
Transfer control to callee
LR = PCcurrent + 4
PC = Mem Addr of foo()
PCcurrent
Notes: Suppose PC current represents the memory address of the Branch and Link instruction BL. Since the BL instruction takes four bytes in memory, the memory of the next instruction immediately after BL is PC current plus 4.

## Slide 8: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
r0 | 
r1 | 
r2 | 
r3 | 
. . . | . . .
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Registers
32 bits
0x08000214
0x08000210
0x08000214
0x08000280
PC = LR
PCcurrent
Resume suspended caller
0x08000214
Notes: Suppose PC current represents the memory address of the Branch and Link instruction BL. Since the BL instruction takes four bytes in memory, the memory of the next instruction immediately after BL is PC current plus 4.

## Slide 9: Procedure Call Standard
What is it?
  Contract between a calling subroutine (caller) and a called subroutine (callee)
Why need it?
  Allows subroutines to be separately written, compiled, assembled but work together
  Allows C program calls an assembly function, or vice versa
This talk focuses on
  How to pass arguments to a subroutine?
  How to return a result from a subroutine?
Notes: The AAPCS defines how subroutines can be separately written, separately compiled, and separately
assembled to work together.

## Slide 10: Passing Arguments and Returning Value

## Slide 11
r0 | a8
r1 | b8
r2 | c16
r3 | d16
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Register

## Slide 12
r0 | sum
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Return the sum in register r0
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Register

## Slide 13: Passing Arguments and Returning Value
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Caller
s = sum(1, 2, 3, 4);
MOVS r0, #1 ; a8
MOVS r1, #2 ; b8
MOVS r2, #3 ; c16
MOVS r3, #4 ; d16
BL sum
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
BX LR
ENDP

## Slide 14: Returning Value
int32_t s32;
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
s32 = sum(1, 2, 3, 4) + 100;
MOVS r0, #1 ; 1st argument a8
MOVS r1, #2 ; 2nd argument b8
MOVS r2, #3 ; 3rd argument c16
MOVS r3, #4 ; 4th argument d16
BL sum ; result is returned in r0
ADDS r0, r0, #100

## Slide 15
r0 | a[31:0]
r1 | a[63:32]
r2 | b[31:0]
r3 | b[63:32]
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int64_t sum(int64_t a, int64_t b);
Callee
sum PROC
ADDS r0, r2, r0 ; Adding lower 32 bits
ADC r1, r3, r1 ; Adding upper 32 bits
BX LR ; Return in r1:r0
ENDP
r1
r0
r3
r2
r1
r0
Addend1
Addend2
Sum
Upper 32 bits
Lower 32 bits
Carry out
Register

## Slide 16
r0 | sum[31:0]
r1 | sum[63:32]
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Returning sum from a subroutine
int64_t sum(int64_t a, int64_t b);
Callee
sum PROC
ADDS r0, r2, r0 ; Adding lower 32 bits
ADC r1, r3, r1 ; Adding upper 32 bits
BX LR ; Return in r1:r0
ENDP
r1
r0
r3
r2
r1
r0
Addend1
Addend2
Sum
Upper 32 bits
Lower 32 bits
Carry out
Register

## Slide 17
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADDS sp, sp, #8 ; pop a4, a6
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP
sp | xxxx
Memory
Register

## Slide 18
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADDS sp, sp, #8 ; pop a4, a6
sp+8 | xxxx
sp+4 | a6
sp | a5
Memory
Register
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP

## Slide 19
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADDS sp, sp, #8 ; pop a4, a6
sp | xxxx
 | a6
 | a5
Memory
Register
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP

## Slide 20: Returning Value
uint32_t s32;
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16);
s32 = sum(1, 2, 3, 4) + 100;
MOVS r0, #1 ; 1st argument a8
MOVS r1, #2 ; 2nd argument b8
MOVS r2, #3 ; 3rd argument c16
MOVS r3, #4 ; 4th argument d16
BL sum ; result is returned in r0
ADDS r0, r0, #100
LDR r4, =s32 ; Get memory address of s32
STR r0, [r4] ; Save returned result to s32

## Slide 21: Calling Assembly Subroutine in C
If your assembly code follows the procedure call standard, a C code can call an assembly subroutine, and vice versa.
extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3);
int main(void){
int32_t s
...
s = sum3(-1, -2, -3) + sum3(4, 5, 6);
...
}
sum3 PROC
EXPORT sum3
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
BX LR ; return in r0
ENDP

## Slide 22: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | Yes | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 23: Callee Saved Registers vs Caller Saved Registers
Callee can freely modify R0, R1, R2, and R3
If caller expects their values are retained, caller should push them onto the stack before calling the callee
Caller expects these values are retained .
If Callee modifies them, callee must restore their values upon leaving the function.
Caller Saved Registers
Callee Saved Registers

## Slide 24: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | Yes | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes/No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 25: Example: SSQ(3, 4)
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
...
int SSQ(int x, int y){
int z;
z = x*x + y*y;
return z;
}
R0: first argument
R1: second argument
R0: Return Value
Sum of Square:

## Slide 26: Example: SSQ(3, 4)
R0
R1
0x08000128
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...

## Slide 27: Example: SSQ(3, 4)
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
3
R0
R1
0x08000128
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 28: Example: SSQ(3, 4)
3
R0
4
R1
0x0800012C
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 29: Example: SSQ(3, 4)
3
R0
4
R1
0x08000130
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 30: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
0x08000134
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
Address of the next instruction after the branch is saved into LR.
In fact, LR is 0x08000135 because bit 0 of PC should always be 1 for ARM Cortex-M to indicate thumb mode.
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 31: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 32: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013C
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 33: Example: SSQ(3, 4)
3
R0
4
R1
0x08000140
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 34: Example: SSQ(3, 4)
25
R0
4
R1
0x08000142
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 35: Example: SSQ(3, 4)
25
R0
4
R1
0x08000144
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 36: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
Copy LR to PC when returning from a subroutine!
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 37: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 38: Example: SSQ(3, 4)
25
R0
4
R1
0x08000136
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 39: Realities
In the previous example,
  PC is incremented by 2 or 4.
  The least significant bit of LR is always 0.
  Well, I lied!

## Slide 40: Realities
PC is always incremented by 4.
  Each time, 4 bytes are fetched from the instruction memory
  It is either two 16-bit instructions or one 32-bit instruction
    If bit [15-11] = 11101, 11110, or 11111, then, it is the first half-word of a 32-bit instruction. Otherwise, it is a 16-bit instruction.
The least significant bit of LR is always 1 for ARM Cortex-M
  This bit is used to control the processor mode:
    0 = ARM, 1 = THUMB
  Cortex-M only supports THUMB.

## Slide 41: Summary
How to call a subroutine?
  Branch with link: BL subroutine
How to return the control back to the caller?
  Branch and exchange: BX LR
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
How to return a value in a subroutine?
  Value is returned in r0
How to preserve the running environment for the caller?
  (to be covered)

## Slide 42: Quiz: What is wrong with the assembly implementation?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0], #2
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3 ; return result in r0
BX lr
ENDP

## Slide 43: Quiz: What is wrong with the assembly implementation?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0], #2
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3, LSL #16
MOV r0, r0, ASR #16 ; r0 = (short) r3
BX lr
ENDP
The sum is limited to 16 bits!
0x12345678
0x00005678
0x1234ABCD
0xFFFFABCD
int32_t x = 0x12345678;
int16_t y = (int16_t) x;

## Slide 44: Quiz: What is wrong with the assembly implementation?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0], #2
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
SXTH r0, r3 ; r0 = (short) r3
BX lr
ENDP
The sum is limited to 16 bits!
SXTH Sign extend Halfword