## Slide 1: Dr. Yifeng Zhu
ARM Cortex-M
Memory Mapped I/O
Embedded Systems with ARM Cortex-M
Microcontrollers in Assembly Language and C
Visit book website: web.eece.maine.edu/~zhu/book/
Notes: This short video explains what is memory mapped I/O.

## Slide 2: Interfacing Peripherals
Port-mapped I/O
  Use special CPU instructions: Special_instruction Reg, Port
Memory-mapped I/O
  A simpler and more convenient way to interface I/O devices
  Each device registers is assigned to a memory address in the address space of the microprocessor
  Use native CPU load/store instructions: LDR/STR Reg, [Reg, #imm]
Core
0x48000024 | 
0x48000020 | 
0x4800001C | 
0x48000018 | 
0x48000014 | GPIO Data Output Register
0x48000010 | 
Memory Address
GPIO Output
Pin output
STR
ARM Cortex-M microprocessors use memory-mapped I/O.
32-bit Memory Data
Notes: Usually, each on-chip peripheral device has a few registers, such as control registers, status registers, data input registers, and data output registers. In general, there are two approaches to exchange data between the processor core, and a peripheral device, including {{Pause=0.5}} port-mapped I/O, and {{Pause=0.5}} memory-mapped I/O. Port-mapped I/O uses special CPU instructions, which are designed specifically for I/O operations. {{Pause=0.5}} On the other hand, memory-mapped I/O does not need any special instructions. Each register is assigned to a memory address, in the memory address space of the microprocessor. Memory-mapped I/O is performed by the native load and store instructions of the processor. Therefore, memory-mapped I/O is a more convenient way to interface I/O devices.
Here is an example of memory mapped I/O. Suppose we want to set the output of a G P I O pin to high, software can use the store instruction STR to set the corresponding bit in G P I O data output register to 1. When you write to this “special memory location”, the data you write, is sent to, the corresponding I/O device. {{Pause=0.5}} ARM Cortex-M microprocessors use memory-mapped I/O.

## Slide 3: Memory Map of Cortex-M4
Flash
SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
4 GB
On-chip Flash, for code & data
On-chip RAM, for heap, stack, & code
AHB & APB, such as timers, GPIO
Such as SD card
Off-chip memory for data
NVIC, System Timer, SCB, vendor-specific memory
Notes: The memory address of ARM Cortex-M has a total of 32 bits, supporting 4 gigabytes of memory space. The memory space is divided into six different pre-defined regions. Each region is given for recommended usage. {{Pause=0.5}} The first region is code region. It is primarily used to store program code. It can also store data. The code region is on-chip memory, typically on-chip flash. The size of on-chip flash is limited to half a gigabyte. The actual size of the on-chip flash varies based on different venders and different chips. {{Pause=0.5}} The second region is SRAM. It is primarily used to store data, such as heaps and stacks. We can also put code here. It supports half a gigabyte. {{Pause=0.5}} The third region is peripheral. These peripherals include Advanced High Performance Bus peripherals, such as G P I O, and A D C, or Advanced Peripheral Bus peripherals, such as timers, and USART. {{Pause=0.5}} The next region is for external device, such as SD card. {{Pause=0.5}} The next is external RAM, which is executable region for data. It is off-chip memory, primarily used to store large data blocks. It has a total of 1 gigabyte. {{Pause=0.5}} The last region is system region, which includes the N V I C, system timer, system control block, and vendor-specific memory.

## Slide 4: Memory Map of STM32L4
Flash
SRAM
Peripheral
External Device
External RAM
System
0x00000000
GPIO A (1 KB)
GPIO B (1 KB)
0x48000000
0x48000400
0x48000800
0x48000C00
GPIO C (1 KB)
GPIO D (1 KB)
0x48001000
0x40000000
0x60000000
…
…
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Notes: {{Pause=0.5}} Let’s take a look at the peripheral region. This region covers the memory addresses of all on-chip peripherals, such as G P I O, timers, USART, S P I, and A D C. {{Pause=0.5}} Specific mapping addresses are dependent on vendors and chips. We will use G P I O on STM 32 L4 as an example to illustrate the concept of memory-mapped I/O. For instance, on STM 32 L4, the registers of G P I O Port A, are mapped to a small memory region starting at, 48000000 in hex.

## Slide 5: GPIO Memory Map
GPIO A (1 KB)
0x48000000
0x48000400
IDR
ODR
BSRR
LCKR
MODER
OTYPER
OSPEEDR
PUPDR
AFR[0]
AFR[1]
BRR
ASCR
0x48000000
0x48000004
0x48000008
0x4800000C
0x48000010
0x48000014
0x48000018
0x4800001C
0x48000020
0x48000024
0x48000028
0x4800002C
48 bytes
0x48000400
Each register has 4 bytes
Notes: Let’s take a closer look at the memory map, for G P I O Port A. {{Pause=0.5}} Each port has 12 registers, and each register has 4 bytes. While a total of 1 kilobyte space is reserved for Port A, only 48 bytes are used. Within this 48-byte memory region, the G P I O mode register MODE R, is mapped to the lowest memory address, and the G P I O analog switch control register, A S C R, is mapped to the highest memory address.

## Slide 6: GPIO Memory Map
GPIO A (1 KB)
0x48000000
0x48000400
IDR
ODR
BSRR
LCKR
MODER
OTYPER
OSPEEDR
PUPDR
AFR[0]
AFR[1]
BRR
ASCR
0x48000000
0x48000004
0x48000008
0x4800000C
0x48000010
0x48000014
0x48000018
0x4800001C
0x48000020
0x48000024
0x48000028
0x4800002C
48 bytes
0x48000400
Set pin A.8 to high
Set bit 8 of ODR to high
Notes: Suppose we want to set the output of pin 14 of Port A to high. To achieve this, we need to set bit 14 of the output data register (ODR) of G P I O, A, to 1.

## Slide 7: Output Data Register (ODR)
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ODR
0x48000014
1 word (i.e. 32 bits)
0x48000014
0x48000015
0x48000016
0x48000017
4 bytes
Little Endian
0x48000017
Notes: As discussed previously, each register has 32 bits, that is, 4 bytes. The output data register (ODR) of Port, A, on STM 32 L4, are mapped to the memory addresses from 48000014 to 48000017, in hex. If little endian is used, the highest memory address holds the most significant 8 bits, and the lowest memory address holds the least significant 8 bits.

## Slide 8: Output Data Register (ODR)
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 
0x48000014
1 word (i.e. 32 bits or 4 bytes)
0x48000014
0x48000015
0x48000016
0x48000017
4 bytes
Little Endian
0x48000017
*((uint32_t *) 0x48000014) |= 1UL<<8;
Bitwise OR
Dereferencing a pointer
ODR
Notes: We use this C statement to set, bit 14, of ODR to 1, by using bitwise OR. This C statement also uses dereferencing to access the memory. Dereferencing a pointer means, getting the value that is stored in the memory location pointed by the pointer. The operator asterisk is used to do this. The asterisk is called the dereferencing operator. A sequence of load, modify, and store operations are performed in this statement. This statement casts the memory address to a memory pointer, which points to an 32-bit unsigned integer. First, the dereference operator retrieves the ODR register value, as a 32-bit unsigned integer. Then, a bit-wise operation is performed to modify this unsigned integer value. Finally, the updated value is stored back to the ODR register, via the dereferencing operation. However, directly dereferencing a numeric memory address, is inconvenient to use in practice. The code uses numeric addresses directly. Accordingly, it is not very readable. The next slide will present a new approach, which uses register names instead of memory addresses, thus greatly improving the code readability.

## Slide 9: Dereferencing a Memory Address
typedef struct {
volatile uint32_t MODER; // Mode register
volatile uint32_t OTYPER; // Output type register
volatile uint32_t OSPEEDR; // Output speed register
volatile uint32_t PUPDR; // Pull-up/pull-down register
volatile uint32_t IDR; // Input data register
volatile uint32_t ODR; // Output data register
volatile uint32_t BSRR; // Bit set/reset register
volatile uint32_t LCKR; // Configuration lock register
volatile uint32_t AFR[2]; // Alternate function registers
volatile uint32_t BRR; // Bit Reset register
volatile uint32_t ASCR; // Analog switch control register
} GPIO_TypeDef;
// Casting memory address to a pointer
#define GPIOA ((GPIO_TypeDef *) 0x48000000)
GPIOA->ODR |= 1UL<<8;
IDR
ODR
BSRR
LCKR
MODER
OTYPER
OSPEEDR
PUPDR
AFR[0]
AFR[1]
BRR
ASCR
0x48000000
0x48000004
0x48000008
0x4800000C
0x48000010
0x48000014
0x48000018
0x4800001C
0x48000020
0x48000024
0x48000028
0x4800002C
or
(*GPIOA).ODR |= 1UL<<8;
Notes: In memory-mapped I/O, all registers of a G P I O port, are mapped to a contiguous block of physical memory. This memory block can be represented by using a struct, as defined in this slide. A struct in C defines a physically grouped list of variables under one name. Note that we put volatile qualifier on each register. It informs the compiler that the variable might change spontaneously. When a variable is declared as volatile, the compiler is informed that even though no statements in the program appear to change it, the value might still change. Typically, compilers minimize the number of memory accesses, by storing the memory value in a register, and then repeatedly using it without accessing the memory. The volatile qualifier on a variable, prevents the compiler from making such optimization, on this variable.
{{Pause=0.5}} We use a macro definition here to give a name to the struct pointer. Let's name the macro G P I O A. {{Pause=0.5}} To set bit 14, we can use the membership operator to access the data output register ODR. We can either use the arrow operator, or the dot operator, to access the output data register ODR. These two C statements are equivalent. The asterisk G P I O A gets the structure that G P I O A points to.

## Slide 10: Programming in Assembly
GPIOA->ODR |= 1UL<<8; // Set bit 8 to 1
GPIOA_BASE EQU 0x48000000
GPIO_ODR EQU 0x14
LDR r7, =GPIOA_BASE ; Load GPIO port A base address
LDR r1, [r7, #GPIO_ODR] ; r1 = GPIOA->ODR
ORR r1, r1, #(1<<8) ; Set output of pin 8 to high
STR r1, [r7, #GPIO_ODR] ; Write the output data register
In C
In Assembly
Notes: If the program has to be written in assembly, we can use the EQN directive to define two constants. The first constant is the base memory address for Port A. The second constant is the offset of the ODR register. First, we load the base memory address into register r7. Then we load the ODR value into register r1. Next, we modify r1. Finally, we store the modified value back to the ODR register.