## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 16
Real-time Clock (RTC)

## Slide 2: Real-Time Clock (RTC)
RTC is a digital clock that provides calendar time and date.
Typical requirements:
  Low power consumption
  Separately powered by a battery
  Accurate
  Run independently from the processor core

## Slide 3: UNIX Epoch Time
Definition: number of seconds that have elapsed since 00:00:00 UTC, Thursday, 1 January 1970
Example:
  Converting 2:07:39am, April 21, 2014 (UTC) to Unix Epoch number
Note a day has 86400 seconds ()

## Slide 4: UNIX Epoch Time
Use a signed 32-bit integer to hold the UNIX Epoch Time
  Covers a time span of 136 years.
  Minimum representable time is 1901-12-13
  Maximum representable time is 2038-01-19
Year 2038 Problem (also called Unix Millennium Bug)
  The second after 03:14:07 UTC 2038-01-19 is an overflow (which became 1901-12-13).
  Use a signed 64-bit integer to fix the problem
  A challenge in embedded systems

## Slide 5: Crystal Inaccuracy: PPM
Parts Per Million (PPM) = 10-6
Crystal Inaccuracy
  1 PPM ⟶ ±1.1 seconds per year
  A typical watch crystal has 20 PPM
    Error per day: 86400 seconds × 20 × 10-6 = 1.728 seconds/day
    Error per month: 30 days × 1.728 seconds/day = 51 seconds/month
STM32 RTC
  At 25°C, HSI and MSI have an accuracy of 1000 ppm (not accurate enough for RTC)
  LSI, 32KHz, 10% accuracy
  Need to use external LSE crystal, typically 32.768 kHz (215 Hz), 20 ppm
  Why 32.768 kHz?
    Tradeoff
      Low frequency crystals → large physical size
      High frequency crystals → large current drain

## Slide 6: Frequency Setting

## Slide 7: Frequency Setting
If is 32.768 kHz, i.e. 215 Hz, then is 27-1, i.e. 127, and is set as 28-1, i.e. 255, in many applications, as shown below.