## Slide 1: Dr. Yifeng Zhu
ARM Cortex-M
Booting Process
Embedded Systems with ARM Cortex-M
Microcontrollers in Assembly Language and C
(Second Edition)
Visit book website: web.eece.maine.edu/~zhu/book/
Notes: {{Pause=3}} In this short video, let’s understand the booting sequence of ARM Cortex-M processors.

## Slide 2: External Reset
Reset
Button
Manually pull NRST pin low
ARM
Cortex-M4
NRST
Reset Button
STM32L4 Discovery Kit
Vdd
Improve EMS
Pull-up
Resistor
(40KΩ)
Notes: {{Pause=2}} A system reset, sets all registers to their reset values, except for the reset flags in the clock controller register (CSR), and the registers in the backup domain. A system reset can be generated by hardware or software. For example, if the NRST pin is pulled low, a system reset takes place. NRST pin is pulled, up, internally within the processor chip. If the reset button is pressed down, NRST pin is pulled low. When the reset button is released, the NRST pin becomes high again. A pulldown capacitor is added, in parallel with the reset button. This bypass capacitor is to improve the level of electromagnetic susceptibility (EMS) . Electromagnetic susceptibility of a device, is defined as, the ability to operate without fault, under electrical disturbances and noise. In other words, EMS is the level of tolerance to various forms of electromagnetic radiation. The bypass capacitor can remove high-frequency voltage signal from NRST pin, and thus reduce the transient circuit demand on the power supply unit.

## Slide 3
Booting Sequence:
1. Read pins BOOT0 and BOOT1
and determine boot mode
2. Fetch MSP from address
0x00000000
3. Fetch PC from address
0x00000004
Booting Process
Notes: {{Pause=2}} Let’s quickly review the interrupt vector table. {{Pause=1}} The first word in the memory contains the value to initialize the Main Stack Pointer (MSP). {{Pause=1}} The second word in the memory is a pointer to the function reset handler, which is the starting memory address, or called entry point, of the function reset handler. {{Pause=2}} Here is the booting process. When the processor boots, it first reads two pins, including pin boot 0, and pin boot 1. The processor determines the boot mode based on these two pins. {{Pause=1}} In the second step, the processor copies the value stored at the memory address 0 to the main stack pointer (MSP). Basically, the main stack pointer (MSP) is initialized in this step. {{Pause=1}} In the third step, the processor copies the value stored at the memory address 4 to the program counter (PC). Note that the program counter always holds the memory address of the next instruction to be executed by the processor. Therefore, immediately after the processor boots, the processor will start to execute the function reset handler. Typically, the reset handler performs some hardware initialization first, such as initialization of data segment and bss segment. Then, the reset handler calls the main() function and transfers the control to the main() function.

## Slide 4: Booting Process
...
void Reset_Handler() {
...
main();
...
}
0x08000268
0x20001BB0
0x00000008
0x00000004
0x00000000
0x20001BB0
0x08000269
Stack
Memory
address
Memory
content
Initialize MSP
Initialize PC
Bit 0 is 1, indicating Thumb state.
0x08001384
void main() {
...
}
R8
R9
R5
R7
R10
R11
R0
R1
R2
R3
R4
R6
R12
R13 (SP)
R14 (LR)
R15 (PC)
0x20001BB0
0x08000269
Registers
Booting Sequence:
1. Read pins BOOT0 and BOOT1
and determine boot mode
2. Fetch MSP from address
0x00000000
3. Fetch PC from address
0x00000004
Notes: {{Pause=2}} Here is a specific example. Suppose the word stored at the memory address 0 is, 2 0 0 0 1 B B 0, in hex, and the word stored at the memory address 4 is, 0 8 0 0 0 2 6 9, in hex. {{Pause=1}} The second word holds the memory address of the function reset handler. The memory address of the reset handler function in fact is 0 8 0 0 0 2 6 8, in hex, which is different from the second word stored in the memory. The least significant bit of the memory address of the reset handler function is, 0, however, the least significant bit of the second word in the memory is, 1. This is because ARM uses the least significant bit of the program counter to indicate whether the processor run in the Thumb mode or the ARM mode. Because ARM Cortex-M processors only support the Thumb mode, the least significant bit of the program counter should always be 1.
{{Pause=2}} After the processor determines the boot mode by reading pin boot 0 and pin boot 1, the processor copies the first word to the stack pointer register (SP). {{Pause=0.5}} Then, the processor copies the second word to the program counter register (PC).

## Slide 5: Boot Mode
Boot1 | Boot0 | Boot Mode
x | 0 | Boot from main flash memory
0 | 1 | Boot from system memory (bootloader)
1 | 1 | Boot from embedded SRAM
Notes: {{Pause=2}} Most Cortex-M processors support at least three different boot modes. The processor can boot from the in-chip flash memory, the system memory, or the in-chip SRAM. The code stored in the system memory is called bootloader. The bootloader is usually provided by chip manufacturers. A bootloader can upgrade the firmware inside the internal flash memory. {{Pause=0.5}} All STM32 microprocessors come with a pre-programmed bootloader, in a ready-only memory region (ROM). This ROM region is called system memory. However, sometimes, you want to develop a custom bootloader. For example, you may want to, encrypt the firmware, and put it on the internet so that customers can upgrade the firmware. In this case, you have to write a custom bootloader to decode the encrypted firmware.

## Slide 6: Boot Mode
Code
Internal SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
ROM region reserved to bootloaders
Boot1 | Boot0 | Boot Mode
x | 0 | Boot from main flash memory
0 | 1 | Boot from system memory
1 | 1 | Boot from embedded SRAM
Alias to flash, system memory or SRAM
Reserved
Internal Flash
System memory
(bootloader)
Reserved
Option Bytes
0x00000000
0x08000000
0x1FFFFFFF
0x1FFF0000
0x080X0000
0x1FFF77FF
Notes: {{Pause=2}} Here is the memory map of ARM Cortex-M processors. The address range of each memory region is fixed. Let’s take a look at the code region. {{Pause=0.5}} The code region ranges from 0 to 1FFFFFFF, in hex. The top area is the ROM region reserved to store bootloaders. {{Pause=1}} The middle area is the in-chip flash memory. {{Pause=1}} The bottom area is an area that can be physically mapped to the internal flash, system memory, and internal SRAM. The starting address of internal flash memory, the system memory, and internal SRAM is also fixed. Specifically, the starting address of internal flash is 0 8 0 0 0 0 0 0, in hex, and the address of the system memory starts at 1 F F F 0 0 0 0, in hex.
{{Pause=1}} Now, let’s look at the boot mode. The boot mode are determined by the voltage applied to pin boot 1 and pin boot 0.

## Slide 7: Boot Mode
Code
Internal SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Alias to flash
Reserved
Internal Flash
System memory
(bootloader)
Reserved
Option Bytes
0x00000000
0x08000000
0x1FFFFFFF
0x1FFF0000
0x080X0000
ROM region reserved to bootloaders
Boot1 | Boot0 | Boot Mode
x | 0 | Boot from main flash memory
0 | 1 | Boot from system memory
1 | 1 | Boot from embedded SRAM
Physical remap:
e.g. map 0x08000000 to 0x00000000
0x1FFF77FF
Notes: {{Pause=2}} If pin boot 0, is connected to the ground, the processor will boot from the internal flash memory. If pin boot 0 is grounded, the processor will physically map the internal flash memory to the button area. {{Pause=1}} For example, the memory address 8000000 is physically mapped to the memory address 0. In other words, the Flash memory contents can be accessed starting from address 0 or, 8000000. {{Pause=1}} As discussed previously, when the processor boots, it always fetch the value of the stack pointer and program counter from the memory address 0 and 4, respectively. Because the internal flash memory is physically remapped to the starting address 0, the flash memory is in fact the boot memory.

## Slide 8: Boot Mode
Code
Internal SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Alias to system memory
Reserved
Internal Flash
System memory
(bootloader)
Reserved
Option Bytes
0x00000000
0x08000000
0x1FFFFFFF
0x1FFF0000
0x080X0000
ROM region reserved to bootloaders
Boot1 | Boot0 | Boot Mode
x | 0 | Boot from main flash memory
0 | 1 | Boot from system memory
1 | 1 | Boot from embedded SRAM
Physical remap:
e.g. map 0x1FFFX000 to 0x00000000
0x1FFF77FF
Notes: {{Pause=2}} When pin boot 1 is low, and pin boot 0 is high, the system memory is physically mapped to the bottom area. {{Pause=1}} When the processor fetches the value of the program counter from memory address 4, the processor in fact fetches the value from the system memory. As result, the system memory is chosen as the boot memory. In this boot mode, processor can reprogram the flash memory or perform the device firmware upgrade.

## Slide 9: Boot Mode
Code
Internal SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Alias to SRAM
Reserved
Internal Flash
System memory
(bootloader)
Reserved
Option Bytes
0x00000000
0x08000000
0x1FFFFFFF
0x1FFF0000
0x080X0000
ROM region reserved to bootloaders
Boot1 | Boot0 | Boot Mode
x | 0 | Boot from main flash memory
0 | 1 | Boot from system memory
1 | 1 | Boot from embedded SRAM
Physical remap:
e.g. map 0x20000000 to 0x00000000
0x1FFF77FF
Notes: {{Pause=2}} When both pin boot 1 and pin boot 0 are high, the internal SRAM is physically mapped to the bottom area. {{Pause=0.5}} The memory address 20000000 is physically mapped to the memory address 0. {{Pause=0.5}} Therefore, the processor boots from SRAM.

## Slide 10: FAQ
How to set up the boot mode?
  PCB design
How to place the code to the boot memory (internal flash, system memory, internal SRAM)
  Linker Script
    How are data and code sections merged?
    Where should each section be placed in the memory?
How to set values in memory address 0 and address 4?
  startup_xxx.s
Stack_Size EQU 0x00000400
AREA STACK, NOINIT, READWRITE, ALIGN=3
Stack_Mem SPACE Stack_Size
__initial_sp
...
__Vectors DCD __initial_sp ; Top of Stack
DCD Reset_Handler ; Reset Handler
startup_stm32lxx_md.s
Notes: {{Pause=2}} Here, we answer three frequently asked questions. First, how to set up the boot mode? The boot mode is determined by the PCB design, not by the processor. For the STM32L4 discovery kit, the default boot memory is the internal flash because pin boot 0 is connected to the ground. {{Pause=1}} Second, how to place code to the boot memory? When the linker combines object and library files into a single executable, a linker script provides the linker two critical types of instructions regarding, how data and code sections are merged, and where each section should be placed in the memory. Programmers can modify the linker script to place the code in the target boot memory. {{Pause=1}} Third, how to set values stored at memory address 0 and 4? The short answer is the startup code. The startup code, such as the start up assembly file, sets these values. For example, the STM32 startup assembly file defines the stack size, the stack pointer’s initial value, and the program counter’s initial value.

## Slide 11: What does the startup code do?
Assume the project runs in flash
The bootloader (startup_xxxx.s) will perform the following:
  Set up the stack and heap region
  Pace the memory address of the stack at the beginning of the interrupt vector
  Set up the rest of the interrupt vector
  Copy RW data session from Flash to SRAM
  Copy ZI data session from Flash to SRAM

## Slide 12: Flash Memory Layout
Code
Internal SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
Alias to flash, system memory or SRAM
Reserved
Internal Flash
System memory
(bootloader)
Reserved
Option Bytes
0x00000000
0x08000000
0x1FFFFFFF
0x1FFF0000
0x080X0000
0x1FFF77FF
0x08000000
0x080XFFFF
Internal Flash
MSP
Reset_Handler
NMI_Handler
…
Code
RO Data
RW Data
Interrupt vector
ZI Data
Zero Initialized
Read-Write
Read-only

## Slide 13: Memory Layout of Code
Section | Content | Memory Region at Run-time
.isr_vector | Stack address, interrupt address vector | Code (Flash)
.text | Program code, some constants | Data (Flash)
.rodata | Constant data, strings | Code (Flash)
.data | Global initialized variables, local initialized static variables | Data (RAM) and Code (Flash)
.bss | Global un-initialized/zero-initialized variables, local un-initialized/zero-initialized static variables | Data (RAM)
heap | Dynamically allocated variables | Data (RAM)
stack | Local non-static variables | Data (RAM)

## Slide 14: Execution Image
0x08000000
0x080XFFFF
Internal Flash
MSP
Reset_Handler
NMI_Handler
…
Code
RO Data
RW Data
Interrupt vector
ZI Data
int a, b;
int c = 271, d = 275;
int f[] = {10,11,12,13}
int main (void){
uint32_t i;
char str1[32];
char str2[] = "0123456789";
int32_t sum = -1;
uint32_t array[] = {1, 2, 3, 4, 5};
uint32_t e = 12345;
for (i = 0; i < 5; i++){
sum += array[i]*2 + f[i] + e;
str2[i] = str1[i];
}
while(1);
}
represented by a register
Program are stored in the code section.
Constants/literals are in Read-Only section following the code.
Global initialized variables are in Read-Write section.
Global uninitialized variables are in Zero-Initialized section.
Some variables are stored in processor’s registers for performance.

## Slide 15: Execution Image
int a, b;
int c = 271, d = 275;
int f[] = {10,11,12,13}
int main (void){
uint32_t i;
char str1[32];
char str2[] = "0123456789";
int32_t sum = -1;
uint32_t array[] = {1, 2, 3, 4, 5};
uint32_t e = 12345;
for (i = 0; i < 5; i++){
sum += array[i]*2 + f[i] + e;
str2[i] = str1[i];
}
while(1);
}
0x08000000
0x080XFFFF
Internal Flash
MSP
Reset_Handler
NMI_Handler
…
Code
RO Data
RW Data
Interrupt vector
Internal SRAM
0x20000000
0x3FFFFFFF
RW Data
Heap
Stack
Reset_Handler() copies data from Flash to SRAM.
Free Space
ZI Data
ZI Data
represented by a register

## Slide 16: Execution Image
int a, b;
int c = 271, d = 275;
int f[] = {10,11,12,13}
int main (void){
uint32_t i;
char str1[32];
char str2[] = "0123456789";
int32_t sum = -1;
uint32_t array[] = {1, 2, 3, 4, 5};
uint32_t e = 12345;
for (i = 0; i < 5; i++){
sum += array[i]*2 + f[i] + e;
str2[i] = str1[i];
}
while(1);
}
0x08000000
0x080XFFFF
Internal Flash
MSP
Reset_Handler
NMI_Handler
…
Code
RO Data
RW Data
Interrupt vector
Internal SRAM
0x20000000
0x3FFFFFFF
RW Data
Heap
Stack
Reset_Handler() copies data from Flash to SRAM.
Free Space
ZI Data
ZI Data
represented by a register
Subroutine copies data from RO to initialize stack.
Most local variables are stored in the stack
Subroutine is responsible for initialize local variables in stack

## Slide 17: A Word of Warning
Image could be different due to the optimization made by compiler
Compiler often optimize the code to improve the computation efficiency or reduce the code size
  Using registers to replace some variables
  Remove declared but unused variables
  Constant folding and propagation (replacing 5 + 3 with 8)
  Register allocation
  Dead code elimination
  Loop unrolling