## Slide 1: Dr. Yifeng Zhu
ARM Cortex-M
Pointer
Embedded Systems with ARM Cortex-M
Microcontrollers in Assembly Language and C
(Second Edition)
Visit book website: web.eece.maine.edu/~zhu/book/
Notes: {{Pause=3}} This short video will explain, what is a pointer, in the C programming language.

## Slide 2: Memory Address
Memory is byte addressable
  Memory is an array of bytes
  Each byte has a memory address
  Smallest data that can be addressed is a byte
  Each address has 32 bits (ARM Cortex-M)
An object may occupy multiple bytes
  A word has four bytes
  Word: Little endian vs Big endian
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
One Byte
High address
Low address
Little Endian
MSB
LSB
Big Endian
LSB
MSB
Notes: {{Pause=2}} First, let’s review what is a memory address. We can view computer memory as an array of bytes, and each byte has an unique address. That is why we call computer memory is byte addressable. In other word, the smallest data object that can be addressed is a byte. For ARM Cortex-M microprocessors, each memory address has 32 bits, which can address a total of 4 GB.
{{Pause=1}} A data object may take multiple bytes in memory. For example, a word occupies four bytes in memory. There are two different formats to store a word. When storing a word in little endian format, the most significant byte, is stored at, a high address, and the least significant bye, is stored at, a low address. On the other hand, when storing a word in big endian format, the most significant byte, is stored at, a low address, and the least significant bye, is stored at, a high address.

## Slide 3: Pointer
The value of a pointer is simply the memory address of some variable
  If a variable occupies multiple bytes in memory, its address is the lowest address of all bytes it occupies.
  Address of the integer = 0x20000004, regardless of the endian
Define pointers
int * ip; // ip can hold the address of an integer
float * fp; // fp can hold the address of a float
double * dp; // dp can hold the address of a double
char * cp; // cp can hold the address of a character
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
One Byte
An integer
(4 bytes)
Address of this integer
Notes: {{Pause=2}} What is a pointer? {{Pause=1}} The value of a pointer is simply, the memory address of some variable stored in computer memory. If a variable occupies multiple bytes in memory, the address of this variable is defined as, the lowest address of all bytes it occupies. {{Pause=1}} Let me give you an example. Suppose a 32-bit integer takes these four bytes in memory, starting from 20000004 to 20000007, in hex. Then, the address of this integer is 20000004, regardless of the endian. No matter what endian format is used, little endian, or big endian, the memory address of this 32-bit integer does not change.
{{Pause=2}} What is the basic syntax to define pointers in C? {{Pause=1}} The basic syntax is: type, asterisk (*), pointer name. Here are four examples. These examples define a pointer, which can hold the address of the memory location, that contains an integer, {{Pause=0.5}} a float, {{Pause=0.5}} a double, {{Pause=0.5}} and a character, respectively.

## Slide 4: Reference and Dereference Operators
Reference Operator (&)
Expression &x returns the address of variable x
Ampersand (&) is called reference operator or address-of operator
Dereference Operator (*)
Expression *p returns the value of the variable to which p points
The asterisk (*) is called dereference operator
int x = 1;
0x0000.0001
x
0x2000.0004
memory
Notes: {{Pause=2}} For C pointers, there are two important operators, including {{Pause=0.5}} reference operator, and {{Pause=0.5}} dereference operator. Let's look at reference operator first. The expression, ampersand x, returns the memory address of variable x. The ampersand is called, reference operator, or, address-of operator. {{Pause=1}} The expression, asterisk p, returns the value of, the variable to which the pointer p points. The asterisk (*) is called, dereference operator. The symbol, asterisk, has different meaning, in a declaration statement, and in an expression.
{{Pause=1}} Let me show you how the reference and dereference operators are used. Suppose we declare an integer variable x. Assume this integer variable is stored in memory address 20000004, in hex. The variable x has an initial value of 1.

## Slide 5: Reference and Dereference Operators
Reference Operator (&)
Expression &x returns the address of variable x
Ampersand (&) is called reference operator or address-of operator
Dereference Operator (*)
Expression *p returns the value of the variable to which p points
The asterisk (*) is called dereference operator
int x = 1;
int * ptr; // Define a pointer that
// can point to an integer
ptr
0x2000.0008
0x0000.0001
x
xxxx.xxxx
0x2000.0004
memory
Notes: {{Pause=2}} Then, we define a pointer variable, named p t r. The pointer p t r can point to a memory location, at which an integer is stored. {{Pause=1}} Suppose the pointer p t r is stored at the memory address 20000008, in hex. When we declare a pointer variable, its content is not initialized. In other words, the content of the pointer variable is not an valid memory location.

## Slide 6: Reference and Dereference Operators
Reference Operator (&)
Expression &x returns the address of variable x
Ampersand (&) is called reference operator or address-of operator
Dereference Operator (*)
Expression *p returns the value of the variable to which p points
The asterisk (*) is called dereference operator
int x = 1;
int * ptr; // Define a pointer that
// can point to an integer
ptr = & x; // Make the pointer points
// to variable x
ptr
0x2000.0008
0x0000.0001
x
0x2000.0004
0x2000.0004
memory
Notes: {{Pause=2}} We can initialize a pointer variable by using the reference operator. Specifically, we can use the reference operator to obtain the memory address of a variable, and assign the address to a pointer variable. This statement assigns the memory address of variable x to the pointer variable p t r. {{Pause=0.5}} Let’s take a look at the memory content. As you can see, the 32-bit value 20000004, in hex, is stored at the memory location 20000008. In fact, this value is the memory address of variable x. As result, p t r points to x. As illustrated in this statement, the reference operator generates a pointer that points to a variable.

## Slide 7: Reference and Dereference Operators
Reference Operator (&)
Expression &x returns the address of variable x
Ampersand (&) is called reference operator or address-of operator
Dereference Operator (*)
Expression *p returns the value of the variable to which p points
The asterisk (*) is called dereference operator
int x = 1;
int * ptr; // Define a pointer that
// can point to an integer
ptr = & x; // Make the pointer points
// to variable x
*ptr = 5; // Dereferencing
ptr
0x2000.0008
0x0000.0005
x
0x2000.0004
0x2000.0004
memory
Notes: {{Pause=2}} This expression, asterisk, p t r, represents the value pointed by p t r. This C statement stores 5 to the memory location pointed by p t r. As result, we indirectly set the value of variable x to 5.

## Slide 8: Reference and Dereference Operators
Reference Operator (&)
Expression &x returns the address of variable x
Ampersand (&) is called reference operator or address-of operator
Dereference Operator (*)
Expression *p returns the value of the variable to which p points
The asterisk (*) is called dereference operator
& var: address of var
* ptr: value pointed by ptr
Summary:
Notes: {{Pause=2}} Here is the summary. The reference operator works on variables, and it can be read as, “address {{Pause=0.1}} of”. Therefore, Ampersand v a r, can be read as, address of v a r. At the same time, the dereference operator works on pointers, and it can be read as, “value pointed by”. Therefore, asterisk p t r, can be read as, value pointed by p t r.

## Slide 9: Pointer Arithmetic
ptr is pointer, and stored at 0x20000000
ptr = 0x20000004
What happens if:
ptr++;
Is it true? ptr = 0x20000005
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x20
0x00
0x04
0x00
Content
Address
ptr
Notes: {{Pause=2}} What will happen if we increase the pointer by 1? {{Pause=1}} Suppose the pointer p t r is stored at the memory address 20000000, in hex. The content of this pointer is 20000004, in hex. Here, we assume each word is stored in memory, in little endian format. {{Pause=1}} If we execute p t r plus plus, what is the content of p t r? Is it 20000005, in hex? {{Pause=1}} The answer is: it depends.

## Slide 10: Pointer Arithmetic
char * ptr;
char a[5];
ptr = & a[0];
ptr ++;
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x20
0x00
0x04
0x00
Content
Address
ptr
a[1]
a[0]
a[4]
a[2]
a[3]
ptr is pointer, and stored at 0x20000000
ptr = 0x20000004
What happens if:
ptr++;
Is it true? ptr = 0x20000005
Notes: {{Pause=2}} Suppose p t r points to an array of characters. {{Pause=0.5}} Each character takes one bye in memory. The pointer p t r points the beginning of the array. In other words, p t r points to, A 0. Let's see what will happen if we run p t r plus plus.

## Slide 11: Pointer Arithmetic
char * ptr;
char a[5];
ptr = & a[0];
ptr ++;
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x20
0x00
0x05
0x00
Content
Address
ptr
a[1]
a[0]
a[4]
a[2]
a[3]
ptr = ptr + sizeof(char)
ptr is pointer, and stored at 0x20000000
ptr = 0x20000004
What happens if:
ptr++;
Is it true? ptr = 0x20000005
Notes: {{Pause=2}} If we run p t r plus plus, the pointer points to the next element in this array. the content of p t r is incremented by the size of a character. Because each character takes one byte, the value of p t r is incremented by 1. Therefore, in this case, the value of p t r is 20000005, in hex.

## Slide 12: Pointer Arithmetic
int * ptr;
int a[5];
ptr = & a[0];
ptr ++;
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x20
0x00
0x04
0x00
Content
Address
ptr
a[0]
a[1]
a[2]
ptr is pointer, and stored at 0x20000000
ptr = 0x20000004
What happens if:
ptr++;
Is it true? ptr = 0x20000005
Notes: {{Pause=2}} Now, let's look at a different example. Suppose p t r points to the beginning of an integer array. If we increment the value of p t r by 1, will the value of p t r be 20000005? {{Pause=1.5}} The answer is no.

## Slide 13: Pointer Arithmetic
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x20
0x00
0x08
0x00
Content
Address
ptr
a[0]
a[1]
a[2]
ptr = ptr + sizeof(int)
int * ptr;
int a[5];
ptr = & a[0];
ptr ++;
ptr is pointer, and stored at 0x20000000
ptr = 0x20000004
What happens if:
ptr++;
Is it true? ptr = 0x20000005
Notes: {{Pause=2}} The value of p t r will be 20000008, which is the memory address of the array element, A 1. When we run p t r plus plus, the value of ptr will be incremented by 4, because each integer takes 4 bytes in memory.

## Slide 14: Pointer and Array
int *ptr; // Assume stored at 0x20000000
int a[5]; // Assume started at 0x20000004
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
ptr
a[0]
a[1]
a[2]
0x2000000F
0x2000000E
Notes: {{Pause=2}} Let's take a closer look at pointer and array. Suppose we declare a pointer p t r, {{Pause=1}} and it is stored at memory address 20000000. {{Pause=1}} We then define an integer array, A 5. {{Pause=1}} The array is stored in memory location starting at 20000004.

## Slide 15: Pointer and Array
Array name is a pointer to the first element in the array
int *ptr; // Assume stored at 0x20000000
int a[5]; // Assume started at 0x20000004
*a = 7; // array[0] = 7;
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x00
0x07
0x00
0x00
ptr
a[0]
a[1]
a[2]
0x2000000F
0x2000000E
Notes: {{Pause=2}} This C statement sets the first element to 7. This example is to show that, in C language, the array name, is a pointer, to the first element in the array.

## Slide 16: Pointer and Array
int *ptr; // Assume stored at 0x20000000
int a[5]; // Assume started at 0x20000004
*a = 7; // array[0] = 7;
ptr = a; // ptr points to array[0]
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x00
0x07
0x20
0x00
0x00
0x00
0x04
0x00
ptr
a[0]
a[1]
a[2]
0x2000000F
0x2000000E
Array name is a pointer to the first element in the array
Notes: {{Pause=2}} Here, we set p t r to the memory address of A 0. {{Pause=1}} As you can see from the memory content, the 32-bit value stored at the memory address 20000000 is {{Pause=1}} 20000004, which is the memory address of A 0.

## Slide 17: Pointer and Array
int *ptr; // Assume stored at 0x20000000
int a[5]; // Assume started at 0x20000004
*a = 7; // array[0] = 7;
ptr = a; // ptr points to array[0]
*(ptr + 2) = 15; // array[2] = 15
0x20000005
0x20000004
0x20000008
0x20000006
0x20000003
0x20000002
0x2000000D
0x2000000C
0x2000000B
0x2000000A
0x20000009
0x20000007
0x20000001
0x20000000
0x00
0x07
0x20
0x00
0x00
0x0F
0x00
0x00
0x04
0x00
ptr
a[0]
a[1]
a[2]
0x2000000F
0x2000000E
0x00
0x00
ptr + 2
ptr = ptr + 2 * sizeof (int)
Notes: {{Pause=2}} What does this statement do? {{Pause=1}} Pay attention. p t r plus 2 is not to add the value of p t r by 2. In fact, it adds p t r by 2 times, size of integer. Each integer takes four bytes, Therefore, it adds p t r by 8, pointing to the third element in this integer array.

## Slide 18: Operator Precedence
++/-- have greater precedence than *
  *ptr++
    Equivalent to *(ptr++)
    write/read the value pointed, and then increment the pointer
    x = *ptr++; is equivalent to:
      x = *ptr;
      ptr++;
  (*ptr)++
    The value pointed by ptr is incremented by 1.
    x = (*ptr)++; is equivalent to
      x = *ptr
      *ptr = * ptr + 1;
Notes: {{Pause=2}} The increment operator, plus plus, and the decrement operator, minus minus, have greater precedance than the dereference operator, asterisk. Therefore, the following two expressions are different. In the first expression, read or write the value pointed by the pointer. Then, increment the pointer, pointing to the next element in an array. For example, this C statement {{Pause=0.5}} is equivalent to the following two C statements.
{{Pause=2}} In the second expression, the value pointed by the pointer p t r is incremented by 1. The content of the pointer does not change. For example, this C statement {{Pause=0.5}} is equivalent to the following two C statements.

## Slide 19: Hard-coded Pointer: Set pin PA.5 to high
Example 1: Define an address
#define GPIOA_ODR 0x48000014
*((uint32_t *) GPIOA_ODR) |= 1<<5;
Example 2: Define a pointer
#define GPIOA_ODR ((uint32_t *) 0x48000014)
*GPIOA_ODR |= 1<<5;
Example 3: Define a de-referenced pointer
#define GPIOA_ODR (*((uint32_t *) 0x48000014))
GPIOA_ODR |= 1<<5;
Notes: {{Pause=2}} So far, we have discussed pointers that point to variables, whose memory addresses are not directly determined by software code. How to build a pointer, which points to a given specific memory address? For example, the memory address of the output data register (ODR) for G P I O Port A is determined by its designer. How to build a pointer to it so that software can easily access the value of the output data register. {{Pause=1}} Here, I give three examples, which sets G P I O pin PA 5 to high. In the first example, we define a macro, which actually is the memory address of the output data register for port A. First, we cast this constant memory address to a pointer, which can point to an unsigned 32-bit integer. Then, we use dereference operator to access the value pointed. {{Pause=1}} In the second example, we define a pointer by using this macro. This macro casts the memory address to a pointer. Therefore, in the code, we can directly use dereference operator. {{Pause=1}} In the third example, we incorporate the dereference operator into the macro. As result, software can directly use the de-referenced pointer to access the memory. The last approach has been used widely.

## Slide 20: Hard-coded Pointer: Read GPIO pins
Example 1: Define an address
#define GPIOA_IDR 0x48000010
data = *((volatile uint32_t *) GPIOA_IDR);
Example 2: Define a pointer
#define GPIOA_IDR ((volatile uint32_t *) 0x48000010)
data = * GPIOA_IDR;
Example 3: Define a de-referenced pointer
#define GPIOA_IDR (*((volatile uint32_t *) 0x48000010))
data = GPIOA_IDR;
Add volatile to force compiler to read a new value each time
Notes: {{Pause=2}} Make sure to add the keyword, volatile, if we want to force compiler to read a new value each time. The keyword, volatile, has been discussed in details in the textbook. It prevents compiler from making false optimization during the compiling process.

## Slide 21: A More Convenient Approach: Define a pointer pointing to a structure
typedef struct {
volatile uint32_t MODER; // Mode register
volatile uint32_t OTYPER; // Output type register
volatile uint32_t OSPEEDR; // Output speed register
volatile uint32_t PUPDR; // Pull-up/pull-down register
volatile uint32_t IDR; // Input data register
volatile uint32_t ODR; // Output data register
volatile uint32_t BSRR; // Bit set/reset register
volatile uint32_t LCKR; // Configuration lock register
volatile uint32_t AFR[2]; // Alternate function registers
volatile uint32_t BRR; // Bit Reset register
volatile uint32_t ASCR; // Analog switch control register
} GPIO_TypeDef;
// Casting memory address to a pointer
#define GPIOA ((GPIO_TypeDef *) 0x48000000)
GPIOA->ODR |= 1UL<<5;
IDR
ODR
BSRR
LCKR
MODER
OTYPER
OSPEEDR
PUPDR
AFR[0]
AFR[1]
BRR
ASCR
0x48000000
0x48000004
0x48000008
0x4800000C
0x48000010
0x48000014
0x48000018
0x4800001C
0x48000020
0x48000024
0x48000028
0x4800002C
Notes: {{Pause=2}} In the device header file of STM32 Cortex-M processors, the memory addresses of peripherals are cast to a struct. For example, the base memory address of G P I O port A is 48000000, in hex. {{Pause=1}} Here, we use this macro to cast this memory address to a pointer, which can points to a struct of G P I O Type. As result, we can modify the output data register (ODR) in this way. {{Pause=1}} By using a struct, software can access all registers of a peripheral more easily.