## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 5
Memory Access
Fall 2025

## Slide 2: Overview
How is data organized in memory?
  Big Endian vs Little Endian
How is data addressed?
  Register offset
    LDR r1, [r0, r3] ; offset = r3
    LDR r1, [r0, r3, LSL #2] ; offset = r3 * 4
  Immediate offset
    Pre-index: LDR r1, [r0, #4]
    Post-index: LDR r1, [r0], #4
    Pre-index with update: LDR r1, [r0, #4]!

## Slide 3: Logic View of Memory
By grouping bits, we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits

## Slide 4: Logic View of Memory
By grouping bits, we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From the software perspective, memory is an addressable array of bytes.
  The byte stored at the memory address 0x20000004 is 0b10000100
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
0b10000100
0x84
132
Binary
Hexadecimal
Decimal
Computer memory is byte-addressable!

## Slide 5: Logic View of Memory
When we refer to memory locations by address, we can only do so in units of bytes, halfwords or words
Words
  32 bits = 4 bytes = 1 word = 2 halfwords
  Memory address of a word is the lowest address of all four bytes in that word.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
The address of this word is 0x20000004
The address of this word is 0x20000000

## Slide 6: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
  Can you store a word anywhere?

## Slide 7: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a word at address 0x20000002.
  Word-address mod 4 = 0
  Can we store a word anywhere in memory?
  NO on most computers!
  A word can only be stored at an address that's divisible by 4.

## Slide 8: Logic View of Memory
Halfwords
  16 bits = 2 bytes = 1 halfword
  The right diagram has four halfwords at addresses of:
    0x20000000
    0x20000002
    0x20000004
    0x20000006
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits

## Slide 9: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a halfword at address 0x20000001.
  Can you store a halfword anywhere? NO.
  A halfword can only be stored at an address that's divisible by 2.
  Memory address of a halfword is the lowest address of its two bytes.
  Halfword-address mod 2 = 0

## Slide 10: Quiz
Memory
What are their memory address offsets?
uint32_t X[4];
1 byte
Low Address
High Address

## Slide 11: Quiz
Low Address
High Address
Memory
What are their memory address offsets?
X[3]
X[2]
X[1]
X[0]
uint32_t X[4];
1 byte
Offset = ???
Offset = ???
Offset = ???
Offset = ???

## Slide 12: Quiz
Memory
What are their memory address offsets?
X[3]
X[2]
X[1]
X[0]
uint32_t X[4];
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
0003
0002
0001
0000
1 byte
Offset of bytes
Offset = ???
Offset = ???
Offset = ???
Offset = ???

## Slide 13: Quiz
Memory
What are their memory address offsets?
X[3]
X[2]
X[1]
X[0]
uint32_t X[4];
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
0003
0002
0001
0000
1 byte
Offset = 12
Offset = 8
Offset = 4
Offset = 0
Offset of bytes
If the array starts at address pAddr,
Memory address of X[0] is pAddr
Memory address of X[1] is pAddr + 4
Memory address of X[2] is pAddr + 8
Memory address of X[3] is pAddr + 12
Sequential words are at addresses incremented by 4, not by 1!

## Slide 14
Little Endian
Which end do you break to eat a boiled egg?
Big Endian
Notes: These terms are originated from a very old story. The little endians break their boiled eggs on the smaller end. The big endians break their eggs on the larger end.

## Slide 15: Endianess
High address
Low address
Little Endian
MSB
LSB
Big Endian
LSB
MSB
LSB is at least address
MSB is at least address
byte 0
byte 1
byte 2
byte 3
Gulliver’s Travels (by Jonathan Swift, published in 1726):
Two religious sects of Lilliputians
The Little-Endians crack open their eggs from the little end
The Big-Endians break their on the big end

## Slide 16: Endianess
High address
Low address
Little Endian
MSB
LSB
Big Endian
LSB
MSB
LSB is at least address
MSB is at least address
uint32_t a = 0x87654321
0x87
0x65
0x43
0x21
byte 0
byte 1
byte 2
byte 3
byte 3 byte 2 byte 1 byte 0
Little-Endian
0x21
0x43
0x65
0x87
High address
Low address
byte 0 byte 1 byte 2 byte 3
Big-Endian
0x87
0x65
0x43
0x21
High address
Low address
Endian: byte order, not bit order!
Reading from the top
Reading from the bottom

## Slide 17: Little Endian vs Big Endian
Byte 3
Byte 2
Byte 1
Byte 0
Byte 3
Byte 2
Byte 1
Byte 0
MSB
High address
Low address
Little Endian
LSB
LSB is at least address!
Notes:   In a little-endian system, the least significant byte of a word is stored at the smallest memory address, and the most significant byte at the largest.

## Slide 18: Little Endian vs Big Endian
Byte 3
Byte 2
Byte 1
Byte 0
Byte 3
Byte 2
Byte 1
Byte 0
Byte 3
MSB
LSB
Byte 2
Byte 1
Byte 0
Little Endian
High address
Low address
Big Endian
MSB
LSB
LSB is at least address!
MSB is at least address!
High address
Low address
Notes:   In a big-endian system, the most significant byte of a word is stored at the smallest memory address, and the least significant byte at the largest.

## Slide 19: Little Endian vs Big Endian
Byte 3
Byte 2
Byte 1
Byte 0
Byte 3
MSB
LSB
Byte 2
Byte 1
Byte 0
Little Endian
Byte 3
Byte 2
Byte 1
Byte 0
High address
Low address
Big Endian
MSB
LSB
LSB is at least address!
MSB is at least address!
High address
Low address
Notes:   Again, for little endian, the Least significant byte (LSB) is stored at the lowest address. For big endian, the Most significant byte (MSB) is stored at the lowest address. The little endian stores the bytes of a word in the opposite order as the big endian.

## Slide 20: Word stored at 0x20000000?
0x04
0x03
0x02
0x01
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
Contents
Address
If Little Endian
value = 0x04030201
If Big Endian
value = 0x01020304

## Slide 21: Example
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
0xEE8C90A7
If big endianess is used
The word stored at address 0x20008000 is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 22: Example
0xA7908CEE
If little endianess is used
The word stored at address 0x20008000 is
Endian only specifies byte order, not bit order in a byte!
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 23: Endian on Modern Architecture
Intel x86 and AMD64/x86-64 use little endian.
Atmel AVR32 and OpenRISC use big endian.
Arm Cortex-M supports both Little Endian and Big Endian. However, endian maybe fixed for specific chips.
  ST’s L4 Series, TI’s Tiva C, and NXP’s K64 only supports only Little Endian.
Little Endian
MSB
LSB
Big Endian
LSB
MSB
LSB is at least address
MSB is at least address
Notes: Which endian is better? In modern computers, some computers use little endian, some use little endian, some support both. There are no significant advantages of one over the other. While Arm Cortex-M supports both, a specific Arm chip might only support only one endian. For example, ST’s L4, TI’s Tiva C, and NXP’s K64 support only Little Endian.

## Slide 24: Loading Data from Memory
ALU
Memory
ALU
Memory
Registers
Load
Notes: In modern computers, a value in the memory cannot directly be the source operands of the processor core. When we need to perform an arithmetic or logic operation on a value in the memory, the processor needs to execute the load instruction to load the data from the memory into one of the processor registers firstly.

## Slide 25: Storing Data to Memory
ALU
Memory
ALU
Memory
Registers
Store
Notes: Similarly, the result of the ALU cannot be directly saved into the memory. Instead, the result is saved into a register first, then the processor executed a store instruction to save the value to the memory. The key reasons that registers are much faster than memory. Saving values in registers temporally help improves the processor speed if those values are used repeatedly within a short timeframe.

## Slide 26: Load-Modify-Store
; Assume the memory address of x is stored in r1
LDR r0, [r1] ; load value of x from memory
ADD r0, r0, #1 ; x = x + 1
STR r0, [r1] ; store x into memory
x = x + 1;
C statement
Assume variable X resides in memory and is a 32-bit integer
Notes: Assume x is a 32-bit integer stored in the memory

## Slide 27: 3 Steps: Load, Modify, Store
ALU
Registers
Memory
Modify
Load
1
2
Store
3
x = x + 1;
Variable x resides in memory!
ALU cannot directly operate memory data!

## Slide 28: Load Instructions
LDR rt, [rs]
  Read from memory
  Mnemonic: LoaD to Register (LDR)
  rs specifies the memory address
  rt holds the 32-bit value fetched from memory
  For Example:
; Assume r0 = 0x08200004
; Load a word:
LDR r1, [r0] ; r1 = Memory.word[0x08200004]

## Slide 29: Store Instructions
STR rt, [rs]
  Write into memory
  Mnemonic: STore from Register (STR)
  rs specifies memory address
  Save the content of rt into memory
  For Example:
; Assume r0 = 0x08200004
; Store a word
STR r1, [r0] ; Memory.word[0x08200004] = r1

## Slide 30
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
0x8B
0xAD
0xF0
0x0D
0xDE
0xAD
0xBE
0xEF
Contents
Address
Memory
Processor Core
r0 | 0x20000000
r1 | 
r2 | 
r3 | 
. . . | . . .
r15 | 
ALU
Registers
32 bits
LDR r1, [r0] ; r1 = memory.word[r0]
; LDR stands for Load to Register
0xDEADBEEF
Loading Word from Memory
Notes: The ALU in the processor core cannot directly use values stored in memory as source or destination operands. When software needs to perform an arithmetic or logical operation on a value stored in the memory, software needs to load the target value from the memory to one of the core registers. Note that every processor core register has 32 bits. Here gives an example of the LDR instruction. LDR stands for load to register, and it reads a 32-bit word from the memory and saves the value into the destination register. For example, in this instruction, register r0 specifies the memory address where we will read data. Register r1 is the destination register. In this example, suppose register r0 holds this memory address, which points to this location.
This LDR instruction will load a word, i.e., 4 bytes, into the destination register r1. If we assume the system uses little-endian, then the value of register r1 will be this value: Dead beef.

## Slide 31
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
0x8B
0xAD
0xF0
0x0D
Contents
Address
Memory
Processor Core
r0 | 0x20000000
r1 | 
r2 | 
r3 | 
. . . | . . .
r15 | 
ALU
Registers
32 bits
STR r1, [r0] ; memory.word[r0] = r1
; STR stands for Store Register
0xBADDCAFE
Storing Word to Memory
Notes: When software needs to save a word into the memory, the processor core needs to run the STR instruction. STR stands for store to register. In this example, it saves the 32-bit value held in register r1 into the memory at the address specified in register r0. Assume register r0 has this value, pointing to this memory location. Suppose register r1 holds a special value, Bad Café.

## Slide 32
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
0x8B
0xAD
0xF0
0x0D
0xBA
0xDD
0xCA
0xFE
Contents
Address
Memory
Processor Core
r0 | 0x20000000
r1 | 
r2 | 
r3 | 
. . . | . . .
r15 | 
ALU
Registers
32 bits
0xBADDCAFE
STR r1, [r0] ; memory.word[r0] = r1
; STR stands for Store Register
Storing Word to Memory
Notes: Assume the system uses little endian, here are the memory values if the STR instruction completes. The least significant byte 0xFE is stored at the lowest memory address.

## Slide 33: Load/Store a Byte, Halfword, Word
LDR | Load Word | uint32_t/int32_t | unsigned or signed int
LDRB | Load Byte | uint8_t | unsigned char
LDRH | Load Halfword | uint16_t | unsigned short int
LDRSB | Load Signed Byte | int8_t | signed char
LDRSH | Load Signed Halfword | int16_t | signed short int
STR | Store Word | uint32_t/int32_t | unsigned or signed int
STRB | Store Lower Byte | uint8_t/int8_t | unsigned or signed char
STRH | Store Lower Halfword | uint16_t/int16_t | unsigned or signed short
LDRxxx R0, [R1]
; Load data from memory into a 32-bit register
STRxxx R0, [R1]
; Store data extracted from a 32-bit register into memory

## Slide 34: Load a Byte, Half-word, Word
0x87
0x02000003
0x02000002
0x02000001
0x02000000
0xE1
0xE3
0x65
LDRB r1, [r0]
Load a Byte
0x00
0x00
0x00
0xE1
0
31
LDRH r1, [r0]
Load a Halfword
0x00
0x00
0xE3
0xE1
0
31
LDR r1, [r0]
Load a Word
0x87
0x65
0xE3
0xE1
0
31
Little Endian
Assume
r0 = 0x20000000

## Slide 35: Sign Extension
0x87
0x20000003
0x20000002
0x20000001
0x20000000
0xE1
0xE3
0x65
LDRSB r1, [r0]
Load a Signed Byte
0xFF
0xFF
0xFF
0xE1
0
31
LDRSH r1, [r0]
Load a Signed Halfword
0xFF
0xFF
0xE3
0xE1
0
31
Facilitate subsequent 32-bit signed arithmetic!
Little Endian
Assume
r0 = 0x20000000

## Slide 36: Address Modes: Offset in Register
Address accessed by LDR/STR is specified by a base register plus an offset
Offset can be hold in a register
  LDR r0,[r1,r2]
  Base memory address hold in register r1
  Offset hold r2
  Target address = r1 + r2
  LDR r0,[r1,r2,LSL #2]
  Base memory address hold in register r1
  Offset = r2, LSL #2
  Target address = r1 + r2 * 4

## Slide 37: Address Modes: Immediate Offset
Address accessed by LDR/STR is specified by a base register plus an offset
Offset can be an immediate value
LDR r0,[r1,#8]
  Base memory address hold in register r1
  Offset is an immediate value
  Target address = r1 + 8
Three modes for immediate offset:
  Pre-index,
  Post-index,
  Pre-index with Update

## Slide 38: Addressing Mode: Pre-index vs Post-index
Pre-index
LDR r1, [r0, #4]
Post-index
LDR r1, [r0], #4
Pre-index with Update
LDR r1, [r0, #4]!

## Slide 39: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 40: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
0x20008000
r0

## Slide 41: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
0x20008000
r0
offset=4
r0 + offset
0x20008004

## Slide 42: Pre-index
Pre-Index: LDR r1, [r0, #4]
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
0x20008000
0x88796A5B
r1
r0
offset=4
r0 + offset
0x20008004
Assume Little Endian

## Slide 43: Accessing an Array
Pre-index
uint32_t array[10];
array[0] += 5;
array[1] += 5;
C code
LDR r1, [r0] ; Read array[0]
ADD r1, r1, #5
STR r1, [r0] ; Write to array[0]
LDR r1, [r0, #4] ; Read array[1]
ADD r1, r1, #5
STR r1, [r0, #4] ; Write to array[1]
Assume the memory address of the array starts at 0x20008000.
Assume r0 = 0x20008000.

## Slide 44: Post-index
Post-Index: LDR r1, [r0], #4
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 45: Post-index
Post-Index: LDR r1, [r0], #4
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000
0x20008000
r0

## Slide 46: Post-index
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008000
0x4C3D2E1F
r1
r0
Assume Little Endian
Post-Index: LDR r1, [r0], #4
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 47: Post-index
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008004
0x4C3D2E1F
r1
r0
Assume Little Endian
r0 = r0 + offset
Update r0 after
reading memory
Post-Index: LDR r1, [r0], #4
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 48: Pre-index with Update
Pre-Index with Update: LDR r1, [r0, #4]!
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 49: Pre-index
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008000
0x88796A5B
r1
r0
r0 + offset
0x20008004
Assume Little Endian
Pre-Index with Update: LDR r1, [r0, #4]!
Offset: range is -255 to +255
Assume: r0 = 0x20008000

## Slide 50: Pre-index
Memory Address | Memory Data
0x20008007 | 0x88
0x20008006 | 0x79
0x20008005 | 0x6A
0x20008004 | 0x5B
0x20008003 | 0x4C
0x20008002 | 0x3D
0x20008001 | 0x2E
0x20008000 | 0x1F
0x20008004
0x88796A5B
r1
r0
r0 + offset
0x20008004
Assume Little Endian
Pre-Index with Update: LDR r1, [r0, #4]!
Offset: range is -255 to +255
Assume: r0 = 0x20008000
Update r0 after
reading memory

## Slide 51: Summary of Pre-index and Post-index
Index Format | Example | Equivalent
Pre-index | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Pre-index with update | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Post-index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4
Offset range is -255 to +255
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 52: Example
LDRH r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
0x0000CDEF
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 53: Example
LDSB r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
0xFFFFFFEF
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 54: Example
STR r1, [r0], #4
; r0 = 0x20008000, r1=0x76543210
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0 before store
0x20008000
r0 after store
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 55: Example
STR r1, [r0], #4
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008004
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x76
0x20008002 | 0x54
0x20008001 | 0x32
0x20008000 | 0x10
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 56: Example
STR r1, [r0, #4]
; r0 = 0x20008000, r1=0x76543210
r0 before the store
0x20008000
r0 after the store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 57: Example
STR r1, [r0, #4]
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008000
Memory Address | Memory Data
0x20008007 | 0x76
0x20008006 | 0x54
0x20008005 | 0x32
0x20008004 | 0x10
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 58: Example
STR r1, [r0, #4]!
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 59: Example
STR r1, [r0, #4]!
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
0x20008004
Memory Address | Memory Data
0x20008007 | 0x76
0x20008006 | 0x54
0x20008005 | 0x32
0x20008004 | 0x10
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 60: Example
LDR r11, [r0]
; r0 = 0x20008000
Memory Address | Memory Data
0x20008003 | 0xEE
0x20008002 | 0x8C
0x20008001 | 0x90
0x20008000 | 0xA7
r11 before load
0x12345678
r11 after load
0xA7908CEE
If big endianess is used
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 61: Addressing Modes for Load/Store Multiple Registers
STMxx rn{!}, {register_list}
LDMxx rn{!}, {register_list}
xx = IA, IB, DA, or DB
Addressing Modes | Description | Instructions
IA | Increment After | STMIA, LDMIA
IB | Increment Before | STMIB, LDMIB
DA | Decrement After | STMDA, LDMDA
DB | Decrement Before | STMDB, LDMDB
IA: address is incremented by 4 after a word is loaded or stored.
IB: address is incremented by 4 before a word is loaded or stored.
DA: address is decremented by 4 after a word is loaded or stored.
DB: address is decremented by 4 before a word is loaded or stored.

## Slide 62: Load/Store Multiple Registers
The following are synonyms.
  STM = STMIA (Increment After) = STMEA (Empty Ascending)
  LDM = LDMIA (Increment After) = LDMFD (Full Descending)
The order in which registers are listed does not matter
  For STM/LDM, the lowest-numbered register is stored/loaded at the lowest memory address.

## Slide 63: Store Multiple Registers

## Slide 64: Load Multiple Registers

## Slide 65: Cortex-M3 & Cortex-M4 Memory Map
32-bit Memory Address
232 bytes of memory space (4 GB)
Harvard architecture: physically separated instruction memory and data memory
Code
SRAM
Peripheral
External RAM
External Device
Vendor Specific
External Peripheral Bus
Internal Peripheral Bus
0x00000000
0x20000000
0x40000000
0x60000000
0xA0000000
0xE0040000
0xE0000000
0xE0100000
0xFFFFFFFF
0.5GB
1GB
1GB
0.5GB
0.5GB
0.5GB

## Slide 66
Cortex-M3 Fixed Memory Map

## Slide 67
Cortex-M4 Fixed Memory Map

## Slide 68: Pseudo-instructions
Pseudo instruction: available to use in an assembly program, but not directly supported by hardware.
Pseudo → not real
Compilers translate it to one or multiple actual machine instructions
Pseudo instructions are provided for the convenience of programmers.

## Slide 69: LDR Pseudo-instruction
LDR Rt, =expr
LDR Rt, =label
If the value of expr can be loaded with MOV, MVN (16-bit instruction) or MOVW (32-bit instruction), the assembler uses that instruction.
If a valid MOV, MVN, MOVW instruction cannot be used, or if the label_expr syntax is used, the assembler places the constant in a literal pool and generates a PC-relative LDR instruction that reads the constant from the literal pool.
LDR r1,=0xFF0 ; loads 0xFF0 into R1
; => MOV r1,#0xFF0
LDR r2,=0xFFF ; loads 0xFFF into R2
; => MOVW r2, #0xFFF
LDR r3,=array ; loads the address of array into R3
; => LDR r3,[pc, offset_to_litpool]
; ...
; litpool DCD array
Software uses this pseudo instruction to set a register to some value without worrying about the size of the value.

## Slide 70: 12-bit Encoding of Immediate Numbers
MOV supports all 8-bit immediate numbers
Range of 8-bit immediate number: 0 – 255
Numbers out of this range but with some patterns can be encoded.

## Slide 72: ADR Pseudo-instruction
ADR: loads a program-relative or register-relative address into a register
start MOV r0,#10 ; 32-bit instruction
ADR r4,start ; 32-bit instruction
; => SUB r4,pc,#0xc

## Slide 73: Summary
Memory address is always in terms of bytes.
How is data organized in memory?
How data is addressed?
Addressing Format | Example | Equivalent
Pre-index | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Pre-index with update | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Post-Index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4