## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 12
Fixed-point and Floating-point Arithmetic
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Outline
Fixed-point Arithmetic
Floating-point Arithmetic

## Slide 3: Fixed-point Format: Q Notation
Integer Part
Fractional Part
m bits
n bits
UQm.n for unsigned fixed-point
Integer Part
Fractional Part
m bits
n bits
sign bit
Qm.n for signed fixed-point
m + n + 1 bits
Radix Point
Radix Point

## Slide 4: Converting Fixed-point UQ5.3 to Float
24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
Integer Part
Fractional Part
Radix
Point

## Slide 5: Converting Fixed-point Q4.3 to Float
-24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
Integer Part
Fractional Part
Radix
Point
Signed
Bit

## Slide 6: Convert Float to Fixed-point UQ4.12
Calculate
Round the result to the nearest,
Convert the integer to binary: 12868 = 11_0010_0100_01002
Organize into UQ4.12: 0011.0010_0100_01002
Final result in Hex: 0x3244
Error:
Example: Convert to UQ4.12
UQm.n for unsigned fixed-point

## Slide 7: Convert Float to Fixed-point Q3.12
Calculate
Round the result to an integer,
Find the 16-bit two’s complement: 1100_1101_1011_11002
Organize into Q3.12: 1100.1101_1011_11002
Final result in Hex: 0xCDBC
Error:
Example: Convert to Q3.12
Qm.n for signed fixed-point

## Slide 8: Why use fixed-point?
Floating Point
Shorter Development Time
Wide Dynamic Range
Fixed Point
Higher Performance
Lower Product Cost
More bits for precision

## Slide 9: Tradeoff between Range and Precision
Floating-Point
  Resolution: difference between two neighbor numbers
  Precision decreases as the magnitude increases
Fixed-Point
  Numbers are evenly distributed among the representable range
  Precision is fixed
A simplified 5-bit floating-point (IEEE 754 style)

## Slide 10: Tradeoff between Range and Precision
https://www.johndcook.com/blog/2018/04/15/eight-bit-floating-point/
Distribution of 8-bit IEEE-like positive representable numbers on a log scale

## Slide 11: Fixed-point Addition and Subtraction
Add/subtract two fixed-point numbers with the same format
  Simply treat them as integers, and
  Add/subtract using standard integer addition/subtraction
; r0 and r1 hold a UQ16.16
ADD r2, r0, r1 ; Simply use integer add
SUB r3, r0, r1 ; Simply use integer sub
Integer Part
Fractional Part
Integer Part
Fractional Part
Integer Part
Fractional Part
+
imaginary radix point
r0
r1
r2
+

## Slide 12: Parallel 8-bit Add and Subtract
SADD8 Rd, Rn, Rm
UADD8 Rd, Rn, Rm

## Slide 13: Parallel 8-bit Add and Subtract
SADD16 Rd,Rn,Rm
UADD16 Rd,Rn,Rm

## Slide 14: Fixed-point Multiplication in UQ16.16 or Q15.16
Integer Part
Fractional Part
Integer Part
Fractional Part
16 bits
16 bits
fA
fB
fC = fA x fB
Integer Part[15:0]
Fractional Part [31:16]
Fractional Part [31:0]
Integer Part [31:0]
32 bits
32 bits
A x B

## Slide 15: Fixed-point Multiplication in UQ16.16 or Q15.16
fC = fA x fB
Integer Part[15:0]
Fractional Part [31:16]
Fractional Part [31:0]
Integer Part [31:0]
32 bits
32 bits
A x B

## Slide 16: Fixed-point Multiplication in UQ16.16
Fractional Part [31:0]
Integer Part [31:0]
shift left 16 bits
shift right 16 bits
bitwise OR
MUL_UQ16xUQ16 PROC
UMULL r2, r3, r0, r1 ; Unsigned long multiply, 64-bit result in r3:r2
LSLS r3, r3, #16 ; Shift left the upper word r3
LSRS r2, r2, #16 ; Shift right the lower word r2
ORR r0, r2, r3 ; Pack two halfwords into a word
BX LR ; Return
ENDP
r3
0000 0000 0000 0000
Integer Part[15:0]
r3
Integer Part[15:0]
Fractional Part [31:16]
r0
r2
Fractional Part [31:16]
0000 0000 0000 0000
r2

## Slide 17: Fixed-point Multiplication in Q15.16
MUL_Q16xQ16 PROC
SMULL r2, r3, r0, r1 ; Signed long multiply, 64-bit result in r3:r2
LSLS r3, r3, #16 ; Shift left the upper word r3
LSRS r2, r2, #16 ; Shift right the lower word r2
ORR r0, r2, r3 ; Pack two halfwords into a word
BX LR
ENDP
Fractional Part [31:0]
Integer Part [31:0]
0000 0000 0000 0000
Integer Part[15:0]
shift left 16 bits
Fractional Part [31:16]
0000 0000 0000 0000
shift right 16 bits
Integer Part[15:0]
Fractional Part [31:16]
bitwise OR
r3
r3
r0
r2
r2

## Slide 18: Fixed-point Division in UQ16.16
Integer Part
Fractional Part
16 bits
16 bits
fA
fC = fA fB
Integer Part
Fractional Part
ssss ssss ssss ssss
Integer Part
Fractional Part
0000 0000 0000 0000
fA
Integer Part
Fractional Part
fB
64 bits
s = sign

## Slide 19: Fixed-point Division in UQ16.16
Integer Part
Fractional Part
16 bits
16 bits
fA
ssss ssss ssss ssss
Integer Part
Fractional Part
0000 0000 0000 0000
fA
64 bits
s = sign

## Slide 20: Fixed-point Division in UQ16.16 or Q15.16
Integer Part
Fractional Part
fA
ssss ssss ssss ssss
Integer Part
Fractional Part
0000 0000 0000 0000
fA
DIV_UQ16xUQ16 PROC
PUSH {LR}
ASRS r1, r0, #31 ; r1[31:0] = sign bits of A
LSLS r1, r1, #16 ; put sign bits in upper half word
ORR r1, r1, r0, LSR #16
LSLS r0, r0, #16 ; [r1:r0] stores sign extended A
ASRS r3, r2, #31 ; [r4:r3] stores sign extended B
BL division_64_bits ; Take four input register (r0:r1, r2:r3)
; division_64_bits places result in r0
POP {pc}
ENDP
r0

## Slide 21: Q Notation: UQm.n

## Slide 22: Signed Fixed-point Representation Qm.n
where

## Slide 23: Addition and Subtraction in UQ16.16 or Q15.16
Assume UQ16.16

## Slide 24: Addition and Subtraction in UQ16.16 or Q15.16
; r0 = fixed-point number fa ; r1 = fixed-point number fb ; r2 = fixed-point number fc add r2, r0, r1 ; fc = fa + fb sub r2, r0, r1 ; fc = fa - fb

## Slide 25: Fixed-point Division in UQ16.16 or Q15.16
ASRS r1, r0, #31 ; r1[31:0] = sign bits of A
LSLS r1, r1, #16 ; put sign bits in upper half word
ORR r1, r1, r0, LSR #16
LSLS r0, r0, #16 ; [r1:r0] stores sign extended A
ASRS r3, r2, #31 ; [r4:r3] stores sign extended B
BL division_64_bits ; Take four input register (r0:r1, r3:r4)
MOV r4, r0 ; division_64_bits places result in r0
r4 = fixed-point quotient = A ÷ B

## Slide 26: Outline
Fixed-point Arithmetic
Floating-point Arithmetic

## Slide 27: Normalization
We can convert 10.74626 to normalized format as follows:

## Slide 28: IEEE Standard 754
IEEE 754 value:
where Bias = 127 for single precision
Bias = 1023 for double precision
Not 2’s complement!

## Slide 29: Decoding 0xC1FF0000 into a floating-point number

## Slide 30: Decoding 0xC1FF0000 into a floating-point number
Sign = 1
Exponent =
Fraction =

## Slide 31: Decoding 0xC1FF0000 into a floating-point number
Fraction

## Slide 32: Decoding 0xC1FF0000 into a floating-point number
0.9921875

## Slide 33: Encoding 14.5 into IEEE Std 754 Single-Precision
  We need to solve for four 0-1 variables a, b, c, d s.t.
  , hence
14.5 = 01000001011010000000000000000000 in binary or 0x41680000 in hex
Normalization (14.5 is between 23=8 and 24=16, hence we factor out
23):

## Slide 34: Special Values
Exponents 00000000 and 111111111 are reserved.
Example of Not-A-Number (NaN)
  log(-10.0), sqrt(-1.0), 0.0/0.0, ,

## Slide 35: Subnormalized Float Number
To represent numbers between 0 and the minimum positive number that the normalized format can represent.
Normalized Format
Sub-normalized Format

## Slide 36: Overflow and Underflow
Numbers closest to zero

## Slide 37: Overflow and Underflow
Numbers farthest from zero

## Slide 38: Resolution
Consider a hypothetical five-bit floating-point system (similar to the IEEE 754 standard).
  the sign bit, an exponent (2 bits), and a fraction (2 bits)

## Slide 39: Rounding
IEEE 754 defines four different rounding rules:
  round to the nearest value,
  round toward zero (truncation),
  round toward plus infinity (rounding up), and
  round toward negative infinity (rounding down).
Rounding Rule | Data | Rounded Result
Nearest | +0.123456 | +0.12346
 | -0.123456 | -0.12346
Truncate | +0.123456 | +0.12345
 | -0.123456 | -0.12345
Rounding up | +0.123456 | +0.12346
 | -0.123456 | -0.12345
Rounding down | +0.123456 | +0.12345
 | -0.123456 | -0.12346
Assume only 5 digits are allowed after the decimal point

## Slide 40: Rounding
If bm+1 = 0, directly truncate and remove bits bm+1bm+2bm+2···bn
If bm+1 = 1 and bS = 1, round up
If bm+1 = 1 and bS = 0, round to even
  If bm = 0, directly truncate and remove bm+1bm+2bm+2···bn
  If bm = 1, round up

## Slide 41: Single-precision Rounding Example
Fraction of result has 25 bits.
Rounded to 23 bits by removing round bit and sticky bit
Example: –1.999999761581421 + (- 0.50000006)
1,01111111,11111111111111111111110
+ 1,01111101,00000000000000000000001
23-bit fraction

## Slide 42: Single-precision Rounding Example
Example: –1.999999761581421 + (- 0.50000006)
1,01111111,11111111111111111111110
+ 1,01111101,00000000000000000000001
23-bit fraction
1.11111111111111111111111×2127-127
+ 1.00000000000000000000001×2126-127
1.11111111111111111111110×20
+ 1.00000000000000000000001×2-1
1.11111111111111111111110×20
+ 0.100000000000000000000001×20
10.011111111111111111111101×20
8 bit exponent
1.00111111111111111111111101×21
Shift Right to Align
Re-normalize
25 bits

## Slide 43: Single-precision Rounding Example
Fraction of result has 25 bits.
Rounded to 23 bits by removing round bit and sticky bit
-1.00111111111111111111111 1 0
23-bit fraction
round
bit
sticky
bit
If round bit = 1 and sticky bit = 0, round to even
  If bm = 0, truncate
  If bm = 1, round up
-1.01000000000000000000000
23-bit fraction

## Slide 44: Single-precision Rounding Example
Example: –1.999999761581421 + (- 0.50000006)
1,01111111,11111111111111111111110
+ 1,01111101,00000000000000000000001
23-bit fraction
8 bit exponent
1.00111111111111111111111101×21
1.010000000000000000000000×21
1,10000000,01000000000000000000000
–1.999999761581421 + (- 0.50000006) = -2.5
If infinite precision:
Single precision:
–1.999999761581421 + (- 0.50000006) = -2.499999821581421
Rounding error: 1.784185790221216 × 10-7
Single precision representation